GYRO ERROR CORRECTION / OBJECT MOON

| UTC | 23h 59m 30s | Date | 07/10/2008 |
| --- | --- | --- | --- |
| PSN | LAT | 30° 18,4’ N |  |  |
|  | LON | 014° 19,1’ W | GB | 238° |

- Install the bearing finder on the repeater.

- Take sun bearing. We got the Gyro Bearing (GB).

- In fast, write down the UTC (h:m:s) & co-ordinates from GPS.

- From the NAUTICAL ALMANAC (“YEAR”) for the voyage date (written in the up of left and right pages (p. 10-253)) find column “MOON” on the right page in the page base.

By the argument “HOUR” & “DATE” (for example: 18h of 20/12/2007) take Greenwich Hour Angle (GHA), Declination (Dec), υ & d, which are placed in the page bottom.

For Example:	GHA  : 68° 26,3’

Dec   : 23° 46,6’ S

d       :            7,3’

- From the table “Increments and corrections” of the same manual (p. ii-xxxi -yellow pages) in the upper part, find the minutes (in our case 59m) & in the same column find seconds (in our case – 30s).

On the cross of these values in column SUN/PLANETS Take value INcr (in our case INcr = 14° 11,8’). This value always should be added to GHA:

(GHA + Incr) = GHAcor = 68° 26,3’ + 14° 11,8’ = 82° 38,1’

- Then to the GHAcor add or delete a longitude. If longitude value is “W”, then “ — ”, else if value is “E”, then “ + ”. We got the Local Hour Angle (LHA).

GHAcor + (+/- LON) = 82° 38,1’ — 14° 19,1’ = 68° 19,0’

- In the book “SIGHT REDUCTION TABLES” (for our example VOL.2 0-40°) find the latitude (e.g. LAT = 30°). Search the Z (Azimuth) on crossing of LHA & LAT on the Declination table (SAME or CONTRARY name to LAT). Correcting by interpolation the Z.

If LHA < 180° then: 360 – Zcor.

If LHA > 180° then: Z = Zcor

The difference between Z and GB (GB – Z) will be gyro error.