# VOYAGE PLAN

| Vessel : | AMBITIOUS F. | Voyage Plan Number : | 27/05 | Section | A | This Voyage Plan checked and approved, and Bridge Team briefed by the Master : |
| --- | --- | --- | --- | --- | --- | --- |
| Date : | 10.06.2005 | From : | Port Louis mooring bouys | To : | SINGAPORE berth |  |
| Plan prepared by Navigating Officer : | O. Boriskin |  |
| Charts & NP corrected to NTM | Acknowledge Familiarization with this plan : | Name : | M.A.Metwally |
| No / Date : | 19/12.05.2005 | Rank / Initials / Sign. | Chief Officer | Signature |  |
| Signature : |  | Rank / Initials / Sign. | 2 nd Officer |  |  |
| Departure Port Particulars : __Port Louis_ ; Name of the Berth : _Container Terminal _; ETD _14/05-2005 23:00 Zone time (UTC) :4E Distance to sea buoy :___1.6__________ n.m. Speed : _4 – 6 ________ knots ; ; Min. under keel clearance : ______0.66______ m ; Actual under keel clearance _____6.50_____ m: Distance: 3391 n.m. VHF channels : Pilot ___16/14/12_____ ; Port Control : ___16/12_________ ; VTS :_____________ ; GPS route No3; Other : __________; |
| TABLE OF WAY POINTS |
| No | W.P. GPS | Lat | Long E | Course | Distance to go, n.m. | Chart No | Pos. Fix. Interval | BL/D to I.N.O. | Parallel indexing Distance to I.N.O. |
| 1 |  |  | 283 | 0.6 | 713 | 5 min |  | Racon (B)-0.11 |
| 2 |  |  |  | 291 | 1.0 | 713 | 5 min | Racon (B) 192-0.11 | Racon (B)-0.11 |
| 3 | 10(PBG) | 20-07.83S | 057-27.49E | 307 | 0.9 | 713 | 5 min | Racon (B) 117-1.0 |  |
| 4 | 11 | 20-07.30S | 057-26.75E | 010 | 6.0 | 713;711 | 15 min |  |  |
| 5 | 12 | 20-01.40S | 057-27.90E | 041 | 34.4 | 711 | 15 min |  | Lt Ho – 2.4, Gunners Quoin – 2.7, Flat Isl. – 1.7 |
| 6 | 13 | 19-35.20S | 057-51.50E | 055 | 2701 | 4702;4707 | 1 hour | Flat Isl. 109-8.2 |  |
| 7 | 14 | 06-21.10N | 095-00.00E | 099 | 61.0 | 2777 | 1 hour |  |  |
| 8 | 15 | 06-12.00N | 096-00.0E | 108 | 137 | 2777 | 1 hour |  |  |
| 9 | 16 | 05-29.20N | 098-10.80E | 135 | 154 | 1353 | 1 hour |  | Racon(B)-4.0 |
| 10 | 17 | 03-41.00N | 100-00.00E | 132 | 61.6 | 3945 | 5 min | P.Jarak 018-18.5 |  |
| 11 | 18 | 03-00.00N | 100-46.10E | 131 | 18.4 | 3940 | 5 min | Racon (T) 081-5.9 | Racon (M) 1.8 |
| 12 | 19 | 02-48.00N | 101-00.00E | 118 | 29.6 | 3946 | 5 min | Racon (M) 100-3.5 | Racon (T) 1.4 |
| 13 | 20 | 02-34.25N | 101-26.10E | 129 | 43.6 | 3946 | 5 min | Racon (C) 086-2.8 |  |
| 14 | 21 | 02-07.00N | 102-00.00E | 132 | 19.4 | 3947 | 5 min | Racon (O) 268-6.8 | Racon (N) 7.2 |
| 15 | 22 | 01-54.00N | 102-14.30E | 115 | 37.6 | 3947 | 5 min | Racon (N) 272.3-11.3 | LtFl(2)10s26m -2.5 |
| 16 | 23 | 01-37.80N | 102-48.00E | 122 | 26.8 | 3947 | 5 min | LtFl(2)10s26m-217-2.5 | LtFl5s26m15M-1.5 |
| 17 | 24 | 01-23.50N | 103-10.60E | 131 | 16.6 | 3947 | 5 min | Racon (O) 344-2.5 |  |
| 18 | 25 | 01-12.60N | 103-23.00E | 122 | 19.0 | 3833 | 5 min | P Tyu Kecil 239-2.21 | Racon (D)-0.8 |
| 19 | 26 | 01-02.60N | 103-39.00E | 061 | 4.9 | 4039 | 5 min | Racon (D) 174-1.0 | Racon (TK)-0.8 |
| 20 | 27 | 01-05.00N | 103-43.20E | 044 | 4.0 | 4039 | 5 min | Racon (TK)- 184-0.9 | Racon (M)-0.7 |
| 21 | 28 | 01-07.90N | 103-46.00E | 056 | 3.7 | 4039 | 5 min | Racon (M) 132-0.7 | Racon (K)-0.35 |
| 22 | 29 | 01-10.00N | 103-49.00E | 065 | 5.6 | 4041 | 5 min | Racon (K) 197-0.6 | Racon (B)-0.75 |
| 23 | 30 | 01-12.38N | 103-54.00E | 334 | 1.25 | 4041 | 5 min | Racon (B)219-1.65 |  |
| 24 | 31(PBG) | 01-13.50N | 103-53.45E | 307 | 2.5 | 4037 | 5 min | Lt Tembakul 264-1.7 |  |
| 25 | ------- | 01-15.0N | 103-51.5E | 342 | 1 | 4037 | 5 min | Lt Buran 284-0.58 | BERTH T07 |
|  |  |  |  |  | 3391.45 |  |  |  |  |

| WP RP | REPORTING TO VTS / COAST GUARD | STATION / VHF CHANNELS | SHALLOW WATERS | DENSE / ROSS TRAFFIC AREA | CURRENTS AND TIDES | EMERGENCY ANCHORAGE |
| --- | --- | --- | --- | --- | --- | --- |
| 01 |  | Distress & Safety/ 16 |  |  |  |  |
| 02 | Reporting point | Ch 66 |  |  |  |  |
| 03 | Reporting point |  |  |  |  |  |
| 04 | Reporting point | Ch 74 |  | Port Area | NE –1knot |  |
|  |  |  |  | Port Area | NE –1knot |  |
|  |  |  |  | Port Area | NE –1knot |  |

Arrival  Port  Particulars : Singapore__; Name of the Berth : Berth T 07 ; Zone time (UTC +/-): 08E

Distance to sea buoy :___3.5 __ n.m. Speed :  6 - 4_ knots ;

Min. under keel clearance : ____0.65______ m ; Actual under keel clearance __________ m:

VHF channels :  Pilot ___20_______ ; Port Control : _____16_________ ; VTS :___74__________ ; Other : __________;

| Admiralty Nautical Publications to be used : 1. NP39 2. NP 44 3.286(4) 286(3) VOYAGE PLAN 4.ALS 79(F);77; ATT 203 | Other additional publications to be taken into consideration : 1. 2. 3. 4. |
| --- | --- |
| A/ Squat calculation for : HALF SPEED (12 knots) – 1.05 m SLOW SPEED (8.5 knots) – 0.43m DEAD SLOW SPEED (6.5 knots) – 0.28 m B/ Hull stress and stability weather recalculation for : To be re-calculated in case of ballast would be taken in WBT # |

Page 2