PASSAGE PLAN

TSCHUDI & EITZEN

# SHIP MANAGEMENT

SHIP:		    SIGLOO FINN

VOYAGE #:	           0552

DATE:		      02.02.2005

###### FROM:                        FREEPORT(BUNKERING)

###### TO:                              STENUNGSUND

The Passage Plan shall be pre-planned from BERTH TO BERTH in accordance with the STCW Code Chapter VIII Section A-VIII/2 Part 2 - VOYAGE PLANNING, «Ship Operation Manual 3.2» and the Company’s «Bridge Instruction» Placard posted on the bridge.

| (1) GENERAL INFORMATION |
| --- |
| Voyage number | 0552 |
| Port of departure | Freeport(bunkering) |
| Port of destination | Stenungsund |
| Intended speed | 13.5 knots |
| Total distance: sea | 4757,0 nm |
| Total steaming time in hours:sea | 352 h 20 m |
| ETD port of departure | 02.02.2005 20:30 |
| ETA port of destination | 17.02.2005 12:50 |
| Number of pages in this voyage plan | pgs |
| All charts and navigational publication have been corrected up to | Notice to Mariner No.: Dated: | 49/04 02.12.2004 |
| Weather stations to be used during the voyage: (Weather routeing charts reviewed and on hand.) Weather report by: weather fax, Satcom C, local VHF broadcast, Navtex (NAVAREA IV,II,I:A,B,F,D,K,T,M,P,G,O) BA 5124(02) |
| Expected weather during the voyage: |
| (2) ACKNOWLEDGEMENT |
| Prepared by: | Approved by: |
| Name | Denis Poletaev | Name | Tigran Aramyants |
| Rank | 2nd Officer | Rank | Master |
| Signature |  | Signature |  |
| Date | 02.02.2005 | Date | 02.02.2005 |
| Acknowledge and understood by: | Acknowledge and understood by: |
| Name | Stanislav Stekolnikov | Name | Alexey Krylov |
| Rank | Ch. Officer | Rank | 3rd Officer |
| Signature |  | Signature |  |
| Date | 02.02.2005 | Date | 02.02.2005 |
| (3) PORT OF DEPARTURE INFORMATION |
| Name of departure berth | Freeport Anchorage |
| VHF Channel Port Control | Freeport Harbour Control:Ch 16,14,13,12,11,10,06 |
| VHF Channel Pilot / Others | Freeport Pilots:Ch 16,14 |
| VTS / Reporting systems |  |
| Draft on departure |  |
| Forward | 6.55 m |
| Amidships | 7.05 m |
| Aft | 7.55 m |
| Vessel’s max. air draught | 30.25 m |
| Times of high and low water: (Tidal information marked on charts) |
| Standard Port |  | Date 02.02.2005 |
|  | Time | Rise |
| High water |  |  |
| Low water |  |  |
| High water |  |  |
| Low water |  |  |
| Distance Anchorage to Pilot Station | 2,4 nm |
| Estimated time to anchorage | 00 h 30 m |
| Is there a change of pilots? | No |
| If yes, where: |  |
| If yes, where: |  |
| Detailed Passage Plan Berth to Berth: (Course lines etc. shall also be marked in the charts) SEE PASSAGE PLAN – PLAN SHEET |
| (4) PORT OF ARRIVAL INFORMATION |
| Name of arrival berth | Stenungsund Berth |
| VHF Channel Port Control | Ch 16,06,11 |
| VHF Channel Pilot / Others | Marstrand Pilots:Ch 16,10,11 |
| VTS / Reporting systems | VTS Marstrand:Ch 11 |
| Draft on arrival |  |
| Forward | m |
| Amidships | m |
| Aft | m |
| Vessel’s max. air draught | m |
| Times of high and low water: (Tidal information marked on charts) |
| Standard Port |  | Date |
|  | Time | Rise |
| High water |  |  |
| Low water |  |  |
| High water |  |  |
| Low water |  |  |
| Distance Pilot to Berth | 19,5 nm |
| Estimated time to Berth | 1 h 25 m |
| Is there a change of pilots? | No |
| If yes, where: |  |
| If yes, where: |  |
| Detailed Passage Plan Berth Station to Berth: (Course lines etc. shall also be marked in the charts) SEE PASSAGE PLAN – PLAN SHEET |
| (5) PUBLICATION TO BE USED DURING THE VOYAGE: |
| West Indies Pilot Vol.I | NP 70 | 1-52,106-115 pg. |
| West Indies Pilot Vol.II | NP 71 | 1-62 pg |
| West Coasts of Spain&Portugal Pilot | NP 67 | 1-46,251-252 pg |
| Bay of Biscay Pilot | NP 22 | 1-41 pg |
| Channel Pilot | NP 27 | 1-55 pg |
| Dover Strait Pilot | NP 28 | 1-64 pg |
| North Sea(East) Pilot | NP 55 | 1-61 pg |
| Norway Pilot Vol.I | NP 56 | 1-47,213-220 pg |
| ALRS | 1(2),1(1) | . |
| ALRS | 3(2),3(1) |  |
| ALRS | 6(5),6(2),6(1) |  |
| ALL | Vol. J,D,A,B,C |  |
| ATT | Vol. 1,2 |  |
| Port Entry Guide | 1,2 |  |

| (6) NAVIGATIONAL INFORMATION – Between each WP or a group of WP’s where the conditions are a like (i. e. ocean passages) Between waypiont number.... .2.... and waypoint number... ..7..... |
| --- |
| Course |  | Distance | 3865.7 nm | Speed | 13.5 kn |
| Engine status | FAH |
| VHF Channels to be Monitored |  |
| Sailing directions | NP 69A,70,71,67,22,27,28 |
| List of lights | Vol. J,D,A |
| Other publication | ALRS 3(2),3(1),6(5),6(2),6(1); ATT Vol. 1,2; |
| (7) PARALLEL INDEXING INFORMATION |
| Target | 117°: Great Stirrup Cay: S – 13,25 |
| Minimum distance |  |
| Target | 117°: S –W Point : P – 4,25 |
| Minimum distance |  |
| Target | 071°: S – W Point : P – 5,7 |
| Minimum distance |  |
| Target | 071°: I.Flores : P – 29,8 |
| Minimum distance |  |
| Target | 072º: I.Graciosa : S – 31,8 |
| Minimum distance |  |
| Target | 032°: Racon(M) : S – 4,5 |
| Minimum distance |  |
| Target | 059º: Racon(B) : P – 6,4 |
| Minimum distance |  |
| Prevailing current |
| Direction | Currents are weak |
| Velocity |  |
| Prevailing weather/remarks: |
| Position Fixing: V isual+Radar, GPS; Radar fixes to be cross checked with GPS fixes. Good targets marked on charts. (Keep the marking as ref.) Using buoys for visual fixing must be done with great care. It must be insured that a buoy is in correct position. Position fixing intervals: harbour - not more then 5/10 min. Sea voyage – not more then 1 hour. Coastal voyage – not more then 15 min. (or according Master’s order). Vessel will be proceeding under master’s command and pilot’s advice. |
| (6) NAVIGATIONAL INFORMATION – Between each WP or a group of WP’s where the conditions are a like (i. e. ocean passages) Between waypiont number....7..... and waypoint number...14....... |
| Course |  | Distance | 357.1 nm | Speed | 13.5 kn |
| Engine status | FAH |
| VHF Channels to be Monitored |  |
| Sailing directions | NP 22,27,28 |
| List of lights | Vol. A,B |
| Other publication | ALRS 3(1),6(2),6(1); ATT Vol. 1,2; |
| (7) PARALLEL INDEXING INFORMATION |
| Target | 075°: Racon(O) : P –5,1 |
| Minimum distance |  |
| Target | 075°: Racon(T) : P – 5,1 |
| Minimum distance |  |
| Target | 075°: Greenwich Racon(M) : P – 4,8 |
| Minimum distance |  |
| Target | 022°: Cap Gris-Nez : S – 4,25 |
| Minimum distance |  |
| Target | 042°: Cap Gris-Nez : S – 4,25 |
| Minimum distance |  |
| Target | 057º: Sandettie : P – 1,4 |
| Minimum distance |  |
| Target | 040º: Noordhinder : P – 2,5 |
| Minimum distance |  |
| Prevailing current |
| Direction | Currents are various |
| Velocity |  |
| Prevailing weather/remarks: |
| Position Fixing: V isual+Radar, GPS; Radar fixes to be cross checked with GPS fixes. Good targets marked on charts. (Keep the marking as ref.) Using buoys for visual fixing must be done with great care. It must be insured that a buoy is in correct position. Position fixing intervals: harbour - not more then 5/10 min. Sea voyage – not more then 1 hour. Coastal voyage – not more then 15 min. (or according Master’s order). Vessel will be proceeding under master’s command and pilot’s advice. |
| (6) NAVIGATIONAL INFORMATION – Between each WP or a group of WP’s where the conditions are a like (i. e. ocean passages) Between waypiont number....14..... and waypoint number...21....... |
| Course |  | Distance | 534.2 nm | Speed | 13.5 kn |
| Engine status | FAH |
| VHF Channels to be Monitored |  |
| Sailing directions | NP 28,55,56 |
| List of lights | Vol. A,B,C |
| Other publication | ALRS 3(1),6(2),6(1); ATT Vol. 1,2; |
| (7) PARALLEL INDEXING INFORMATION |
| Target | 046°: Platform Horizon : P –1,8 |
| Minimum distance |  |
| Target | 026°: Platform Halfweg : S – 1,8 |
| Minimum distance |  |
| Target | 022°: Racon(C) : P – 1,9 |
| Minimum distance |  |
| Target | 022°: Platform L9-FF-1 : S – 4,2 |
| Minimum distance |  |
| Target | 360°: Platform F15-A : P – 3,7 |
| Minimum distance |  |
| Target | 034º: Norre Vorupor : S – 12,7 |
| Minimum distance |  |
| Target | 090º: Skagen W : S – 6,5 |
| Minimum distance |  |
| Prevailing current |
| Direction | Currents are various |
| Velocity |  |
| Prevailing weather/remarks: |
| Position Fixing: V isual+Radar, GPS; Radar fixes to be cross checked with GPS fixes. Good targets marked on charts. (Keep the marking as ref.) Using buoys for visual fixing must be done with great care. It must be insured that a buoy is in correct position. Position fixing intervals: harbour - not more then 5/10 min. Sea voyage – not more then 1 hour. Coastal voyage – not more then 15 min. (or according Master’s order). Vessel will be proceeding under master’s command and pilot’s advice. |
| (6) NAVIGATIONAL INFORMATION – Between each WP or a group of WP’s where the conditions are a like (i. e. ocean passages) Between waypiont number....21..... and waypoint number...28....... |
| Course |  | Distance | 12.7 nm | Speed | 13.5 kn |
| Engine status | FAH |
| VHF Channels to be Monitored |  |
| Sailing directions | NP 22,27,28 |
| List of lights | Vol. A,B |
| Other publication | ALRS 3(1),6(2),6(1); ATT Vol. 1,2; |
| (7) PARALLEL INDEXING INFORMATION |
| Target | 052°: I.Skallen : S –0,88 |
| Minimum distance |  |
| Target | 074°: I.St Dyron : P – 0,13 |
| Minimum distance |  |
| Target | 083°: I.N Meholmen : P – 0,07 |
| Minimum distance |  |
| Target | 074°: I.Stenskar : S – 0,08 |
| Minimum distance |  |
| Target | 038°: I.Katten : P – 0,23 |
| Minimum distance |  |
| Target | 029º: I.Mitholmarna : S – 0,1 |
| Minimum distance |  |
| Target | 019º: I.Son : P – 0,3 |
| Minimum distance |  |
| Prevailing current |
| Direction | Currents are weak |
| Velocity |  |
| Prevailing weather/remarks: |
| Position Fixing: V isual+Radar, GPS; Radar fixes to be cross checked with GPS fixes. Good targets marked on charts. (Keep the marking as ref.) Using buoys for visual fixing must be done with great care. It must be insured that a buoy is in correct position. Position fixing intervals: harbour - not more then 5/10 min. Sea voyage – not more then 1 hour. Coastal voyage – not more then 15 min. (or according Master’s order). Vessel will be proceeding under master’s command and pilot’s advice. |
| (6) NAVIGATIONAL INFORMATION – Between each WP or a group of WP’s where the conditions are a like (i. e. ocean passages) Between waypiont number....28..... and waypoint number...35....... |
| Course |  | Distance | 6.8 nm | Speed | 13.5 kn |
| Engine status | FAH |
| VHF Channels to be Monitored |  |
| Sailing directions | NP 22,27,28 |
| List of lights | Vol. A,B |
| Other publication | ALRS 3(1),6(2),6(1); ATT Vol. 1,2; |
| (7) PARALLEL INDEXING INFORMATION |
| Target | 026°: I.Tjorn : P –0,22 |
| Minimum distance |  |
| Target | 001°: I.Snoholmarna : S – 0,13 |
| Minimum distance |  |
| Target | 321°: I.L.Bratton : P – 0,09 |
| Minimum distance |  |
| Target | 015°: I.Kallogrundet : S – 0,08 |
| Minimum distance |  |
| Target | 059°: I.Lerskiten : S – 0,06 |
| Minimum distance |  |
| Target |  |
| Minimum distance |  |
| Target |  |
| Minimum distance |  |
| Prevailing current |
| Direction | Currents are weak |
| Velocity |  |
| Prevailing weather/remarks: |
| Position Fixing: V isual+Radar, GPS; Radar fixes to be cross checked with GPS fixes. Good targets marked on charts. (Keep the marking as ref.) Using buoys for visual fixing must be done with great care. It must be insured that a buoy is in correct position. Position fixing intervals: harbour - not more then 5/10 min. Sea voyage – not more then 1 hour. Coastal voyage – not more then 15 min. (or according Master’s order). Vessel will be proceeding under master’s command and pilot’s advice. |

*	NO-GO zones to be marked in the chart close to the track and safe margins to be

considered.

*	Emergency anchorage’s, abort lines, Pilot embark/disembark to be marked in the chart. Safe margins to be considered.

*	Highlight on the chart racon and other radar conspicuous object which will be used for position fixing. Also mark VHF reporting point during passage in the chart.

*	The SQUAT shall be considered when navigating in areas with reduced under-keel clearance.

*	Parallel index to be marked on charts.

*	”Passage Plan – Plan Sheet” is an excel sheet and is to be found in the computerised checklists as ”Passplan sheet.xls”. The passage plan – plan sheet shall at least be filled in for 3 legs during one voyage:

1) Berth (departure place) to commence sea passage.

2) Commence to end of sea passage

3) End of sea passage to berth (departure place).

# *  	Guidelines on Under Keel Clearance

Master’s shall request the local agent at least 48 hours prior to arrival for relevant under keel clearance information regarding intended terminals, anchorage and approaches.

-	Name of berth or anchorage

-	Water density

-	Water depths

-	Maximum allowable draft

-	Applicable local regulations

24 hours prior to entering port or place of destination, and prior to getting underway from such place, the Master shall:

- Calculate the deepest anticipated navigational draft, including:

- The mean draft

- Trim & List characteristics

- Intended transit speed and Squat characteristics

- Calculate the anticipated controlling depth of the passage, including considerations based on:

- Tide and Current conditions

- Sea state conditions, if applicable

- Past weather impact on water depth

- Depth at the facility, anchorage or place of destination

- Depth of the transit area found in applicable navigational aids

- Charts

- Coast Pilots

- Tide Tables

- Current Tables

- Information obtained from the local Pilot, Coast Guard or other authorities

-	Calculate the anticipated under keel clearance (anticipated controlling depth minus the deepest navigational draft)

-	Log:

- Calculated deepest navigational draft

- Anticipated controlling depth

- Calculated under keel clearance

-	On embarkation of the pilot discuss with the pilot the under keel clearance calculation, including any relevant information provided by the port agent, and potential impact on the planned transit.

-	Inform Office of the calculated anticipated under keel clearance in the event that such calculated clearance is less than one half (1/2) metre. The Master shall include all relevant information in order that Office may provide advice and assistance.

-	The Master may proceed to his destination at less than one half (1/2) metre under keel clearance only on the advice of the applicable pilot and with the concurrence of Office.

In considering the sufficiency of under keel clearance considerable weight shall be placed on the recommendations of the Pilot. In any case, the intentional grounding at an anchorage or terminal in order to facilitate cargo transfer operations is not authorized.