1. Properties of commercial gases

| Name | Molecular Mass (G/Mole) (1) | Atm. Boiling Point (°C) (1) | Critical Temp. (°C) (1) | Critical Pressure (Kpa,Abs) (1) | Liquid Relative Density 15°C/15°C (1) | Vapour Relative Density (Air=1) (1) | Flammable Range (%Vol. By Air) |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | Min (2) | Max (2) |
| Methane Ethane Propane n-Butane i-Butane Ethene Propene 1-Butene cis-2-Butene trans-2-Butene 1,3-Butadiene 1,2-Butadiene Isoprene Vinylchloride (3) Ammonia | 16.043 30.070 44.097 58.124 58.124 28.054 42.081 56.108 56.108 56.108 54.092 54.092 68.119 62.50 17.031 | - 161.52 - 88.58 - 42.07 - 0.49 - 11.81 - 103.77 - 47.72 - 6.23 3.72 0.88 - 4.41 10.85 34.07 -13.4 - 33.33 | - 82.60 32.28 96.67 152.01 134.98 9.20 91.70 146.38 162.43 155.48 152 (171) (211) 156.6 132.5 | 4604 4880 4249 3797 3648 5041 4600 4023 4220 4047 4330 (4502) (3850) 5600 11280 | (0.3) 0.3581 0.5083 0.5847 0.5637 n.p. 0.5231 0.6019 0.6277 0.6105 0.6280 0.6576 0.6866 0.90 0.6183 | 0.5539 1.0382 1.5225 2.0068 2.0068 0.9686 1.4529 1.9372 1.9372 1.9372 1.8676 1.8676 2.3519 2.152 0.5880 | 4.4 2.7 1.7 1.3 1.3 2.7 2.0 1.6 1.6 1.6 1.4 (2.0) 1.0 3.6 15 | 16.0 12.5 9.5 8.5 8.5 34.0 11.1 10 10 10 16.3 (12) 9.7 31 29 |

Note  	( )	: estimated value

n.p.	: not possible, temperature above critical temperature

(1) Ref. GPSA, SI Engineering Data Book, 1980, section 16, fig. 16-1.

(2) Ref. Chemiekaarten, Gegevens voor het veilig werken met chemicaliën, negende editie, 1993/1994.

(3) LGI, Liquid Gas Guide, 2nd edition, 1990.

Properties of commercial gases (continued)

| Name | 100% Odor Recognition (ppm) | Tlv |
| --- | --- | --- |
|  |  | (ppm) | (mg/m³) |
| Methane Ethane Propane n-Butane i-Butane Ethene Propene 1-Butene cis-2-Butene trans-2-Butene 1,3-Butadiene Vinylchloride Ammonia | n.d. 1500 11000 5000 2 800 80 0.07 0.6 0.6 (0.1 - 2) (1500 - 10000) (0.001 - 90) | - - - 800 800 - - n.d. n.d. n.d. 2 5 25 | - - - 1900 1900 - - n.d. n.d. n.d. 4.4 13 17 |

Note :  	(  )  = estimated value

n.d.  = not determined-   = non toxic

Ref.      1.	1994- 1995 Threshold Limit Values for Chemical Substances and Physical Agents and Biological Exposure Indices; American Conference of governmental industrial hygienists.

- Handbook of environmental data on organic chemicals; K. Verschueren

2. Expansion of 1 liter liquid at atm. boiling point to 15 °C and 1 bar in liter.

| Name | Volume Liter (15C And 1 Bar) |
| --- | --- |
| Methane ethane propane n-butane i-butane ethene propene 1-butene cis-2-butene trans-2-butene 1,3-butadiene VCM ammonia nitrogen | 630 432 311 239 236 482 388 261 264 258 279 365 947 691 |

Ref. Encyclopedie des Gaz, L'air Liquide, Division Scientifique,
 Elsevier Scientific Publishing Company, 1976,
 ISBN 0-444-41492-4.

3. Conversion factors

###### 3.1 Pressure conversion table

|  | Atm. | psi | mm Hg | kg/cm² | bar | Pascal | dynes/cm² | mm H2O |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Atm. | 1 | 14.696 | 760 | 1.0332 | 1.01325 | 101325 | 1013935.23 | 10332.71 |
| psi | .068046 | 1 | 51.715 | .070307 | .068948 | 6894.8 | 69013.11 | 703.087 |
| mm Hg | .0013158 | .019337 | 1 | .00135951 | .0013332 | 133.32 | 1334.15 | 13.59508 |
| kg/cm² | .9678 | 14.223 | 735.56 | 1 | .980665 | 98066.5 | 981354.27 | 10000 |
| bar | .98692 | 14.504 | 750.075 | 1.01972 | 1 | 100000 | 1001001 | 10197.162 |
| Pascal | .000009869 | .000145038 | .00750075 | .000010197 | .00001 | 1 | 10.007 | .10197162 |
| dynes/cm² | .000000986 | .00001449 | .00074954 | .000001019 | .000000999 | .09993 | 1 | .01019 |
| mm H2O | .00009678 | .0014223 | .073556 | .0001 | .0000980665 | 9.80665 | 98.1354 | 1 |

###### 3.2. Volume conversion table

|  | Cubic Inches | Cubic Feet | Cubic Yards | Cubic Centimeters | Cubic Meters |
| --- | --- | --- | --- | --- | --- |
| Cubic Inches | 1 | 0.00057870 | 0.000021433 | 16.387 | 0.000016387 |
| Cubic Feet | 1728 | 1 | 0.037037 | 28316 | 0.028316 |
| Cubic Yards | 46656 | 27 | 1 | 764550 | 0.76455 |
| Cubic Centimeters | 0.061024 | 0.000035315 | 0.0000013080 | 1 | 0.000001 |
| Cubic Meters | 61024 | 35.315 | 1.3080 | 1000000 | 1 |

Ref.	Technical Data Book - Petroleum Refining, Volume 1, fourth edition, American Petroleum Institute, 1983.

Conversion factors (continued)

###### 3.3. Liquid volume conversion table

|  | Gallons(U.S.) | Imperial Gallons | Barrels (Oil) | Cu. Inches | Milliliters | Liters |
| --- | --- | --- | --- | --- | --- | --- |
| Gallons (U.S.) | 1 | 0.83270 | 0.023809 | 231 | 3785.3 | 3.7853 |
| Imperial gallons | 1.2009 | 1 | 0.028594 | 277.42 | 4546.0 | 4.5460 |
| Barrels (Oil) | 42 | 34.973 | 1 | 9702 | 158980 | 158.98 |
| Cu. Inches | 0.0043290 | 0.0036047 | 0.00010307 | 1 | 16.387 | 0.016387 |
| Milliliters | 0.00026418 | 0.00021998 | 0.0000062900 | 0.061025 | 1 | 0.001 |
| Liters | 0.26418 | 0.21998 | 0.0062900 | 61.025 | 1000 | 1 |

###### 3.4. Flow Conversion Table

|  | Gal(U.S.)/min | Gal(U.S.)/hr | Cu ft./min | bbl(42)/hr | bbl(42)/day | Cu m/hr |
| --- | --- | --- | --- | --- | --- | --- |
| Gal(U.S.)/min | 1 | 60 | 0.13368 | 1.4286 | 34.286 | 0.22713 |
| Gal(U.S.)/hr | 0.016667 | 1 | 0.0022280 | 0.023810 | 0.57143 | 0.0037854 |
| Cu ft./min | 7.4805 | 448.83 | 1 | 10.686 | 256.47 | 1.6990 |
| bbl(42)/hr | 0.70000 | 42.000 | 0.093576 | 1 | 24.000 | 0.15898 |
| bbl(42)/day | 0.029167 | 1.7500 | 0.0038990 | 0.041667 | 1 | 0.0066245 |
| Cu m/hr | 4.4028 | 264.17 | 0.58857 | 6.2898 | 150.95 | 1 |

Ref. Technical Data Book - Petroleum Refining, Volume 1, fourth edition, American Petroleum Institute, 1983

4. Fundamental Constants

| Name | Symbol | Value | Units |
| --- | --- | --- | --- |
| Absolute temperature | T | 0 273.15 | deg K °C |
| Gas constant | R | 8.3143 0.082053 | J/(mole.K) (L.atm)/(mole.K) |
| Calorie (thermochemical) | Cal | 4.1840 | J |
| Standard millimeter of Hg pressure |  |  | 1/760 atm |
| Standard Atmosphere | Atm | 101325 14.696 | Pa psia |

Ref.	Technical Data Book - Petroleum Refining, Volume 1, fourth edition,American Petroleum Institute, 1983.

5. Typical product specifications

The herebelow given typical specifications for liquefied gases are only to be used as an example, the shown limits are only guidelines.

### 5.1. Ethylene

| Item | Unit | Limits |
| --- | --- | --- |
| Ethylene | %volume | 99.9 min |
| Ethane | ppm volume | 500 max |
| ethane +methane | ppm volume | 1000 max |
| C3 and heavier | ppm volume | 10 max |
| Acetylene | ppm volume | 5 max |
| Oxygen | ppm volume | 5 max |
| Nitrogen | ppm volume | 100max |
| Carbonmonoxide | ppm volume | 2 max |
| Carbondioxide | ppm volume | 5 max |
| methanol + ethanol + aceton | ppm volume | 10 max |
| Hydrogen | ppm volume | 10 max |
| water content | ppm weight | 10 max |
| total sulphur | ppm weight | 2 max |
| Ammonia | ppm volume | 1 max |

Note : the shown limits are the ARG spec.

### 5.2. Propylene polymer grade

| Item | Unit | Limits |
| --- | --- | --- |
| Propylene | %weight | 99.5 min |
| Propane | %weight | 0.5 max |
| methane + ethane | %weight | 0.2 max |
| ethylene + acetylene | ppm weight | 30max |
| Propadiene | ppm weight | 10 max |
| Methylacetylene | ppm weight | 5 max |
| total C4's hydrocarbons | ppm weight | 10 max |
| C5 + (green oil) | ppm weight | 10 max |
| Oxygen | ppm weight | 5 max |
| Nitrogen | ppm weight | 10 max |
| Hydrogen | ppm weight | 1 max |
| methanol | ppm volume | 5 max |
| total sulphur | ppm weight | 2 max |
| water content | ppm weight | 10 max |
| total chlorine | ppm weight | 1 max |

Note : the shown limits are the ARG spec.

#### 5.3. Propylene Chemical Grade

| Item | Unit | Limits |
| --- | --- | --- |
| Propylene | %weight | 94.0 min |
| Methane | ppm weight | 1000 max |
| Ethane | ppm weight | 500 max |
| Propane | %weight | balance |
| Ethylene | ppm weight | 50 max |
| propadiene | ppm weight | 15 max |
| Butenes | ppm weight | 200 max |
| Acetylene | ppm weight | 5 max |
| Methylacetylene | ppm weight | 25 max |
| butadiene-1,3 | ppm weight | 30 max |
| total C4's | ppm weight | 300 max |
| Oxygen | ppm weight | 8 max |
| Hydrogen | ppm weight | 10 max |
| Carbonmonoxide | ppm weight | 3 max |
| Carbondioxide | ppm weight | 10 max |
| Methanol | ppm weight | 10 max |
| water content | no free water |

#### 5.4. Propylene Refinery Grade

| Test Item | Unit | Limits |
| --- | --- | --- |
| Propylene | %weight | 70 min |
| Ethane | %weight | 1 max |
| Propane | %weight | 30 max |
| total C4's and heavier | %weight | 2 max |
| total sulphur | ppm weight | 3 max |

5.6. 1-butene

| Test Item | Unit | Limits |
| --- | --- | --- |
| butene-1 | %weight | 99.3 min |
| i-butylene | %weight | 0.2 max |
| butene-2 | %weight | 0.1 max |
| n-butane + i-butane | %weight | 0.4 max |
| butadiene-1,3 | ppm weight | 50 max |
| propadiene | ppm weight | 8 max |
| total acetylenes | ppm weight | 10 max |
| carbon dioxide | ppm weight | 2 max |
| carbon monoxide | ppm weight | 2 max |
| total carbonyls (as MEK) | ppm weight | 5 max |
| oxygen | ppm weight | 1 max |
| sulphur (as S) | ppm weight |  |
| chlorides | ppm weight |  |
| water |  |  |
| methanol | ppm weight |  |

5.7. 1,3-butadiene

| Test Item | Unit | Limits |
| --- | --- | --- |
| butadiene 1,3 | %weight | 99.6 min |
| butadiene 1,2 | ppm weight | 40 max |
| propadiene | ppm weight | 10 max |
| total acetylenes as vinylacetylene | ppm weight | 25 max |
| methylacetylene | ppm weight | 15 max |
| ethylacetylene | ppm weight | 50 max |
| vinylacetylene | ppm weight | 10 max |
| butadiene dimer | ppm weight | 50 max |
| methanol | ppm weight | 50 max |
| carbonyl content, as acetaldehyde | ppm weight | 10 max |
| total volatile sulphur | ppm weight | 2 max |
| peroxide content | ppm weight | 5 max |
| non volatile residue | ppm weight | 10 max |
| inhibitor (TBC) | ppm weight | 75-150 max |
| water | no free water |  |
| oxygen | ppm weight | 200 max |

5.8. Isobutane

| Item | Unit | Limits |
| --- | --- | --- |
| isobutane | %mol | 95 min |
| n-butane | %mol | 5 max |
| C2 and lighter | %mol | 1 max |
| propane | %mol | balance |
| total olefines | ppm weight | 100 max |
| oxygen liquid | ppm vol | 0.5 max |
| oxygen vapour | ppm vol | 0.3 max |
| total volatile sulphur | ppm weight | 2 max |
| carbonyl content as aceton | ppm weight | 2 max |

### 5.9. Crude C4 raw material spec

| Item | Unit | Limits |
| --- | --- | --- |
| butadiene 1,3 | %weight | 40 min |
| propadiene + methylacetylene | %weight | 0.4 max |
| Isobutylene | %weight | 20 min |
| butene-1 | %weight | 20 max |
| butene-2 | %weight | 10 max |
| saturated C4's | %weight | 12 max |
| butadiene 1,2 | %weight | 0.5 max |
| C3's and lighter | %weight | 0.7 max |
| C4 acetylenes | %weight | 2 max |
| C5's | %weight | 0.5 max |
| Sulphur | ppm weight | 1 max |
| carbonyls as acetaldehyde | ppm weight | 100 max |
| chloride (as Cl ) | ppm weight | 1max |
| Water | no free water |  |

5.10. Raffinate 1  (Isobutylene)

| Item | Unit | Limits |
| --- | --- | --- |
| isobutylene | %weight | 30-65 min |
| C3 and lighter | %weight | 0.5 max |
| butadiene 1,3 | %weight | 0.6 max |
| total acetylenes as vinylacetylene | ppm weight | 200 max |
| C5 diolefines | ppm weight | 20 max |
| C5 and heavier | ppm weight | 1000 max |
| sulphur content | ppm weight | 10 max |
| carbonyl content as acetaldehyde | ppm weight | 10 max |
| perioxide content as H-O-O-H |  |  |
| total chloride | ppm weight | 5 max |
| non volatile residue |  |  |
| ammonia | ppm weight | 5 max |

5.11. Raffinate 2 (n-butenes)

| Item | Unit | Limits |
| --- | --- | --- |
| total n-butenes | %weight | 66-82 min |
| n-butane | %weight | 14 min |
| iso-butene | %weight | 2 max |
| butadiene-1,3 | %weight | 0.7 max |
| C3 and lighter | %weight | 2.0 max |
| C5 and heavier | %weight | 2.0 max |
| acetylenes as vinylacetylens | ppm weight | 800 max |
| total sulphur | ppm weight | 120 max |
| total chloride | ppm weight | 15 max |
| water | no free water |  |

5.12. Vinyl chloride monomer (VCM)

| Item | Unit | Limits |
| --- | --- | --- |
| vinyl chloride monomer | %weight | 99.97 min |
| water | ppm weight | 100 max |
| iron | ppm weight | 0.5 max |
| acidity (as HCl) | ppm weight | 1 max |
| non volatiles | ppm weight | 50 max |
| acetylene | ppm weight | 2 max |
| propylene | ppm weight | 8 max |
| other hydrocarbons | ppm weight | 3 max |
| color (visual) | colorless |  |
| appearance (visual) | clear |  |

6. Dewpoint and Frostpoint

Conversion of frostpoint to dewpoint :

Metric units (°C)

| Frost Point | Dew Point | Frost Point | Dew Point | Frost Point | Dew Point | Frost Point | Dew Point |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | -12 | -13.4 | -24 | -26.6 | -36 | -39.4 |
| -1 | -1.2 | -13 | -14.5 | -25 | -27.7 | -37 | -40.5 |
| -2 | -2.3 | -14 | -15.6 | -26 | -28.8 | -38 | -41.6 |
| -3 | -3.4 | -15 | -16.7 | -27 | -29.9 | -39 | -42.6 |
| -4 | -4.5 | -16 | -17.8 | -28 | -30.9 | -40 | -43.7 |
| -5 | -5.6 | -17 | -18.9 | -29 | -32.0 | -41 | -44.7 |
| -6 | -6.8 | -18 | -20.0 | -30 | -33.0 | -42 | -45.8 |
| -7 | -7.9 | -19 | -21.1 | -31 | -34.1 | -43 | -46.8 |
| -8 | -9.0 | -20 | -22.2 | -32 | -35.2 | -44 | -47.9 |
| -9 | -10.1 | -21 | -23.3 | -33 | -36.2 | -45 | -49.0 |
| -10 | -11.2 | -22 | -24.4 | -34 | -37.3 | -46 | -50.0 |
| -11 | -12.3 | -23 | -25.5 | -35 | -38.4 |  |  |

##### Ref. EG&G Environmental Equipment, Application Data 3-050

Dewpoint is that unique temperature to which the air (or any other gas) must be cooled in order that it shall be saturated with respect to water at the existing pressure. Dewpoint temperature varies in direct proportion to the total vapour pressure.

Frost point is that unique temperature to with the air (or any other gas) must be cooled in order that is shall be saturated with respect to ice at the existing pressure. Below 0 °C dewpoint hygrometers measure the frostpoint temperature rather than the dewpoint. The table below permits conversion from dewpoint to frostpoint.

#### Relation between dewpoint and moisture content of gases

| Dewpoint (°C) | Vapour pressure (mmHg) | Relative Humidity (% H20)) | ppmv | Dewpoint (°C) | Vapour Pressure (mmHg) | Relative Humidity (% H20) | ppmv | Dewpoint (°C) | Vapour pressure (mmHg) | Relative Humidity (% H20) | ppmv |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| -150 -140 -130 -120 -118 -116 -114 -112 -110 -108 -106 -104 -102 -100 -98 -96 -94 -92 -90 -88 -86 -84 -82 -80 -78 -76 | 7*10(-15) 3*10(-10) 7*10(-8) 9*10(-8) .00000015 .00000025 .00000041 .00000066 .00000107 .00000169 .00000266 .00000413 .00000636 .00000968 .00001459 .00002178 .00003224 .00004729 .00006879 .00009924 .00014205 .0002018 .0002844 .0003981 .0005533 .0007638 | 3.9*10(-14) 1.7*10(-9) 4.0*10(-8) 5.4*10(-7) .0000009 .0000014 .0000023 .0000038 .0000061 .0000096 .000015 .000024 .000036 .000055 .000083 .00012 .00018 .00027 .00039 .00057 .00081 .00115 .00162 .00227 .00316 .00436 | 9.2*10(-12) 3.9*10(-7) 9.2*10(-6) 1.2*10(-4) .00020 .00033 .00054 .00087 .00141 .00222 .00350 .00543 .00837 .0127 .0192 .0287 .0424 .0622 .0905 .1305 .1869 .2655 .3742 .5238 .7280 1.005 | -74 -72 -70 -68 -66 -64 -62 -60 -58 -56 -54 -52 -50 -48 -46 -44 -42 -40 -38 -36 -34 -32 -30 -28 -26 -24 | .0010476 .0014275 .001933 .002603 .003483 .004635 .006135 .008076 .010576 .013780 .01787 .02305 .02961 .03786 .04819 .06108 .07709 .09691 .12133 .15133 .1880 .2328 .2871 .3529 .4323 .5277 | .00597 .00814 .0110 .0148 .0199 .0264 .0350 .0461 .0603 .0786 .1019 .131 .169 .216 .275 .348 .440 .553 .692 .863 1.07 1.33 1.64 2.01 2.47 3.01 | 1.378 1.878 2.543 3.425 4.583 6.099 8.072 10.626 13.916 18.132 23.513 30.329 38.961 49.816 63.408 80.368 101.43 127.51 159.64 199.12 247.37 306.32 377.76 464.34 568.82 694.34 | -22 -20 -18 -16 -14 -12 -10 -8 -6 -4 -2 0 2 4 6 8 10 12 14 16 18 20 | .6422 .7790 .9421 1.136 1.365 1.636 1.956 2.331 2.771 3.285 3.884 4.581 5.292 6.099 7.012 8.045 9.209 10.518 11.988 13.635 15.478 17.535 | 3.66 4.44 5.37 6.48 7.78 9.33 11.15 13.29 15.80 18.73 22.15 26.12 30.18 34.78 39.99 45.88 52.52 59.98 68.37 77.76 88.27 100.00 | 845.00 1025.00 1239.61 1494.74 1796.05 2152.63 2573.68 3067.11 3646.05 4322.37 5110.53 6027.63 6963.16 8025.00 9226.32 10585.53 12447.10 13839.47 15773.68 17940.79 20365.79 23072.37 |

Ref. Shaw moisture meters, Westgate, Bradford, 1988 ; 1994 Annual Book of ASTM standards, volume 10.03, ASTM 2029.

7.  Water solubility in liquefied gases and boil-off vapours

Solubility of water in liquefied gases and in equilibrium boil-off vapour at temperatures from –45 °C to +45 °c

##### Ref. Hydrates in LPG cargoes, A technical review, SIGTTO '84

8. Solubility of water in liquid Butadiene 1-3

9. Butadiene 
Dimer 
Formation 
versus 
temperature

10. Interconversion of analysis to gas-volume, liquid volume or weight basis

###### Table 1

| Original Basis | Desired Basis | Operation | Factor Column In Table 2 |
| --- | --- | --- | --- |
| Gas volume Gas volume Weight Weight Liquid volume Liquid volume | Weight Liquid volume Gas volume Liquid volume Gas volume Weight | multiply by multiply by divide by divide by divide by multiply by | 1 2 1 3 2 3 |

###### Table 2

| Compound | Column 1 | Column 2 | Column 3 |
| --- | --- | --- | --- |
|  | Molecular mass | Liquid volume in ml of ideal gas at 60 °F and 760 mmHg | Specific gravity 60/60F (vac.) |
| Methane Ethane Ethylene Propane Propylene Propadiene methylacetylene n-Butane i-Butane 1-Butene trans-2-Butene cis-2-Butene 1,2-Butadiene 1,3-Butadiene Ethylacetylene n-Pentane i-Pentane neo-Pentane 1-Pentene trans-2-Pentene cis-2-Pentene 2-methyl-1-Butene 3-methyl-1-Butene 2-methyl-2-Butene Cyclopentane Isoprene | 16.04 30.07 28.05 44.10 42.08 40.06 40.06 58.12 58.12 56.11 56.11 56.11 54.09 54.09 54.09 72.15 72.15 72.15 70.13 70.13 70.13 70.13 70.13 70.13 70.13 68.12 | 0.00226 0.003566 0.0032 0.003675 0.003413 0.00282 0.00273 0.004205 0.004362 0.003944 0.003887 0.003780 0.00347 0.003643 0.00328 0.004830 0.004879 0.005108 0.004589 0.004537 0.004482 0.004519 0.004684 0.00447 0.003948 0.004195 | 0.30 0.3562 0.37 0.5070 0.5210 0.600 0.621 0.5840 0.5629 0.6011 0.6100 0.6272 0.658 0.6272 0.696 0.6311 0.6247 0.5967 0.6457 0.6530 0.6611 0.6557 0.6325 0.663 0.7505 0.6861 |

Example :

- Original basis : gas volume or mole %

- Desired basis : Weight %

Compound	Original basis	Operation	Factor Column 1	Product

Mole%		(Table 1)	(Table 2)

Methane	33.3			     		16.04			 534.1

Ethane		33.3			     		30.07			1001.3

Propane	33.4			     		44.09			1472.6

-------

Total	100.0							Total	3008.0

Compound	Product					Weight %

Methane	534.1		0.03324	=	17.8

Ethane		1001.3		0.03324	=	33.3

Propane	1472.6		0.03324	=	48.9

_____

Total 100.0

Ref. 	Interconcersion of analysis of C5 and lighter hydrocarbons to gas-volume, liquid-volume, or weight basis; 1995 Annual Book of ASTM Standards, , Petroleum Products and Lubricants (II); ASTM D 2421.

9. Guidelines for cargo tank conditioning prior loading liquefied gases

The change over from one product to a complete different one should be undertaken with great care and expertise. Moreover if the quality of the next cargo is explicitly higher than the quality of the previous cargo or in case purity demands are high and impurity requirements minimal, the change over will be an extensive and specialized operation. When changing grades are preformed one should first investigate the safety compatibility of the consecutive cargoes. In the table herebelow, guidelines for changing cargoes are given.

Explanation of symbols:

O2 content	:	The permissible oxygen (O2) content in vapour phase in volume 			percent.

Dew point	:	The dew point in degrees Celsius.

W		:	Waterwash.

N2		: 	Nitrogen purge only.

N2/I		:	Nitrogen or inert gas purge.

L.F.		:	Cargo tanks, lines, cooling equipment, etc. must be liquid free.

V		:	Visual inspection (Be aware of the TLV values of the product).

Rest. Vap.	:	Amount of previous cargo permitted in the vapour phase at tank 			bottom level in volume percent.

This table must be regarded as a minimum guideline only. The final cargo tank conditions prior to loading will be given by the characters. Notwithstanding anything else contained herein, owners remain fully responsible for maintaining the condition of the cargo as it is received on board the vessel.

###### Changing grades guidelines

| next cargo | ammonia | butane | butadiene | raff-1 (butene) | c4-raff | ethylene | propane | propylenepolym.grd | propylenechem.grd | propylen refin.grd | p.o. | v.c.m. | c4-crude |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| O2 content dewpoint | <8% | <0.5% | <0.2% | <0.3% | <0.3% | <0.3% <-50C | <0.5% | <0.3% <-25C | <0.3% | <0.3% | <500 ppm | <0.1% | <0.2% |
| Previous cargo |  |  |  |  |  |  |  |  |  |  |  |  |  |
| ammonia rest vap. |  | V,N2/I | W,V,N2/I | W,V,N2/I | W,V,N2/I | W,V,N2 | V,N2/I | W,V,N2 | W,V,N2 | W,V,N2 | NOT Permitted | W,V,N2 | W,V,N2/I |
| butane rest vap. | N2 <5% |  | N2/I <2% | N2/I <5% | L.F. | V,N2 | N2/I <5% | V,N2 | V,N2 | L.F. | V,N2 | V,N2 | L.F. |
| butadiene rest vap. | V, N2 | L.F. |  | N2/I <5% | N2/I <25% | V,N2 | N2/I <5% | V,N2 | V,N2 | V,N2 | V,N2 | V,N2 | L.F. |
| raff-1 rest vap. | V, N2 | L.F. | N2/I <5% |  | L.F. | V,N2 | N2/I <5% | V,N2 | V,N2 | V,N2 | V,N2 | V,N2 | L.F. |
| C4-raff rest vap. | V, N2 | L.F. | N2/I <2% | N2/I <25% |  | V,N2 | N2/I <5% | V,N2 | V,N2 | V,N2 | V,N2 | V,N2 | L.F. |
| ethylene rest vap. | N2 <5% | L.F. | N2/I <5% | N2/I <5% | N2/I <5% |  | N2/I <5% | N2 <3000 ppm | N2 <3000 ppm | N2 <5% | V,N2 | N2 <1000ppm | N2/I <5% |
| propane rest vap. | N2 <5% | L.F. | N2/I <5% | N2/I <5% | N2/I <5% | N2 <1000ppm |  | N2 <5% | N <5% | L.F. | V,N2 | N2 <1000ppm | N2/I <5% |
| propylene polymer grd rest vap. | N2 <5% | L.F. | N2/I <5% | N2/I <5% | N2/I <5% | N2 <1000ppm | N2/I <5% |  | L.F. | L.F. | V,N2 | N2 <1000ppm | N2/I <5% |
| propylene chemical grd rest vap. | N2 <5% | L.F. | N2/I <5% | N2/I <5% | N2/I <5% | N2 <1000ppm | N2/I <5% | N2 <5% |  | L.F. | V,N2 | N2 <1000ppm | N2/I <5% |
| propylene refinery grd rest vap. | N2 <5% | L.F. | N2/I <5% | N2/I <5% | N2/I <5% | V,N2 | N2/I <5% | N2 <5% | N2 <5% |  | V,N2 | N2 <1000ppm | N2/I <5% |
| P.O. | W,V,N2 | W,V,N2/I | W,V,N2/I | W,V,N2/I | W,V,N2/I | W,V,N2 | W,V,N2/I | W,V,N2 | W,V,N2 | W,V,N2 |  | W,V,N2 | W,V,N2/I |
| V.C.M. | V, N2 | V,N2/I | V,N2/I | V,N2/I | V,N2/I | V,N2 | V,N2/I | V,N2 | V,N2 | V,N2 | V,N2 |  | V,N2/I |
| Crude C4 rest vap. | V, N2 | L.F. | N2/I <5% | N2/I <5% | N2/I <5% | V,N2 | N2/I <5% | V,N2 | V,N2 | V,N2 | VN2 | ,N2 |  |

10. Purging operations of gas carriers

10.1. Nitrogen consumption for dilution method :

10.2. Conversion of nitrogen quantities :

- 1 liter liquid nitrogen ( -196 °C) = 0.8086 kg = 691 liter vapours (at 15 °C and 1 bar)

- 1 kg of nitrogen = 855 liter vapours (at 15 °C and 1 bar)

Ref. 	Encyclopedie des Gaz, L'air Liquide, Division Scientifique, Elsevier Scientific Publishing Company, 1976, ISBN 0-444-41492-4.

# Text boxes

5 ºC

10 ºC

15 ºC

25 ºC

# Butadiene Dimer (Vulyl Cyclyhexene) Content, ppm by weight

0 		5 		10 		15		20		25 		30 		                                                                       Теmperature, degrees Centigrade

1000

900

800

700

600

500

400

300

200

100

0

1500

1400

1300

1100

1000

900

800

700

600

500

400

300

200

100

0

Water solubility, ppm by weight

-20 	–10 	0 	10 	20 	30 	40 	50 	60

# Temperature, Degrees Centigrade