M/V  “  FOREST   GUN  “

MONROVIA

Port  of  discharging :                                                                   Date  :

DISCHARGING      SEQUENCE.

1-St     RUN    -      Commencenced   Discharging  :    Holds  No.  1 , 3 , and   5

To  continue  until  Cargoes  need  trimming  then  to  shift  to  next  Holds.

2-Nd    RUN   -       Commenced  Discharging  :          Holds  No.   2, 4 , and  6

To  continue  until  Cargoes  need  trimming  then  to  shift  to  next  Holds.

3-Rd     RUN   -   Until   Completion

1.  To  dischrge  Cargo  Holds  alternately  avoid  TWO  CRANES  per  Hopper

to  avoid  overload.

2.  Make  sure  CARGO  HOLD  No.  4   is  completed  first  -  for  this  is  the

BALLAST   HOLD.

3.  To  discharge  only  at  the  center  of  the  hold  to  avoid  accidental

|  | grabbing of the WEB FRAMES, thus damaging the buckets. |
| --- | --- |
| 4. | To avoid giving too much slack on the wires to avoid damage. |
| 5. | When using “ INTERLOCK SWITCH - EMERGENCY STOP BUTTON, |
|  | make sure that the CRANES will also Stop. Thus, preventing overloading when re-starting the conveyors. |

For  Discharging   Terminal

Prepared   by                                                                                    Noted    by

Chief  Officer   V.Pupkin                                                                  Capt. Yuriy  Senko

Master

# Text boxes

COMPANY LO HERE