# Text boxes

## FREQUENCIES  FOR  DISTRESS  AND  SAFETY  COMMUNICATION

Mayday

Pan Pan

Securite

1

| R/Telephone |
| --- |
|  | ch. 16 |  |
|  | 2182.0 |  |
|  | 4125.0 |  |
|  | 6215.0 |  |
|  | 8291.0 |  |
|  | 12290.0 |  |
|  | 16420.0 |  |

| D S C |
| --- |
|  | ch. 70 |  |
|  | 2187.5 |  |
|  | 4207.5 |  |
|  | 6312.0 |  |
|  | 8414.5 |  |
|  | 12577.0 |  |
|  | 16804.5 |  |

| R/Telex |
| --- |
|  | --- |  |
|  | 2174.5 |  |
|  | 4177.5 |  |
|  | 6268.0 |  |
|  | 8376.5 |  |
|  | 12520.0 |  |
|  | 16695.0 |  |

### ON  SCENE  OF  S.A.R.  COMMUNICATION :

### VHF  -  ch. 16

### MF    -  2182 kHz

| Communication |
| --- |
| with aircraft |
| ch. 6 |  |
| 3023.0 | kHz |
| 4125.0 | kHz |
| 5680.0 | kHz |
| 121.5 | MHz |
| 123.1 | MHz |

#### NAVIGATION  AND  SAFETY  INFORMATION  ( MSI )

| MSI HF NBDP |
| --- |
|  | 4210.0 | kHz |
|  | 6314.0 | kHz |
|  | 8416.5 | kHz |
|  | 12579.0 | kHz |
|  | 16806.5 | kHz |
|  | 19680.5 | kHz |
|  | 22376.0 | kHz |
|  | 26100.5 | kHz |

| NAVTEX |
| --- |
| 518 kHz | - International |
| 490 kHz | - National |
| 4209.5 kHz | - Additional |

SAFETY NET

1530 - 1545 MHz

1626.5 - 1646.5 MHz

Inmarsat System

INMARSAT

|  |  | D S C |
| --- | --- | --- |

DISTRESS  ALERT  ACKNOWLEDGEMENT

VHF / MF  BAND

- ASSISTANCE  REQUESTED  AND  USUALLY

AVAILABLE,  BECAUSE  DISTANCE  IS  SHORT.

STEP  1

- TO  INFORM  CAPTAIN.

- DISTRESS  INFO  MUST  BE  ENTERED  IN  THE  RADIO  LOG.

- TO  CALL  DEDICATED  GMDSS  OFFICER,  IF  NECESSARY.

STEP  2

- RADIO  WATCH  TO  BE  OPENED  ON  CH. 16 / 2182  kHz

WITH  RECORD  IN  RADIO  LOG.

STEP  3

- MAKE  A  PAUSE  3–5  MINUTES  AND  LISTEN.

- IF  DISTRESS  ALERT  NOT  ACKNOWLEDGED

BY  COAST  STATION,  ON  CAPTAIN’S  ORDER

ACKNOWLEDGE  THE  ALERT  TO  THE  SHIP

IN  DISTRESS  BY  RADIOTELEPHONY  ONLY.

HF  BAND

- DISTANCE  USUALLY  IS  RATHER  LONG.

- ASSISTANCE  REQUESTED  FROM  RCC.

STEP  1

- TO  INFORM  CAPTAIN.

- DISTRESS  INFO  MUST  BE  ENTERED  IN  THE  RADIO  LOG.

- TO  CALL  DEDICATED  GMDSS  OFFICER,  IF  NECESSARY.

STEP  2

- RADIO  WATCH  TO  BE  OPENED  ON  ASSOCIATED

CHANNELS  WITH  RECORD  IN  RADIO  LOG.

STEP  3

- MAKE  A  PAUSE  3 – 5  MINUTES.

- IF  DISTRESS  ALERT  NOT  ACKNOWLEDGED

BY  COAST  STATION,  ON  CAPTAIN’S  ORDER

TRANSMIT  DISTRESS  RELAY  ON  HF  TO  RCC.

- CONTACT  RCC  VIA  MOST  EFFICIENT  WAY,

IF  OWN  VESSEL  IS  ABLE  TO  ASSIST.

- ENTER  DETAILS  IN  RADIO  LOG.

= NEVER  SEND  DSC  ACKNOWLEDGEMENT  TO  DISTRESS  ALERT  YOURSELF =

2

1

|  |  | D S C |
| --- | --- | --- |

DISTRESS  CALL

RECEIVED  ON

CH. 70 / 2187.5 kHz

VHF

MAYDAY

<VSL  IN  DISTR>	X 3

THIS  IS

<VSL  IDNT>		X 3

RECEIVED  MAYDAY

( RRR  MAYDAY )

| NAVTEX |  |  |
| --- | --- | --- |

| NAVTEX |  |  |
| --- | --- | --- |

INMARSAT

|  |  | D S C |
| --- | --- | --- |

DISTRESS  CALL

RECEIVED  ON

DSC  HF

| 4207.5 | 6312.0 |
| --- | --- |
| 8414.5 | 12577.0 |
| 16804.5 kHz |

TELEX

TELEX

HF

4125.0

6215.0

8291.0

12290.0

16420.0

4177.5

6268.0

8376.5

12520.0

16695.0

4177.5

6268.0

8376.5

12520.0

16695.0

TELEX

4125.0

6215.0

8291.0

12290.0

16420.0

HF

DISTRESS  CALL

RECEIVED  ON

DSC  HF

| 4207.5 | 6312.0 |
| --- | --- |
| 8414.5 | 12577.0 |
| 16804.5 kHz |

|  |  | D S C |
| --- | --- | --- |

MAYDAY  RELAY		X 3

THIS  IS

<VSL  NAME, CALL  SIGN>	X 3

MAYDAY

<VSL NAME IN DISTRESS>

MESSAGE BEGINS

< M E S S A G E T E X T >

MESSAGE ENDS

THIS  IS  <VSL  NAME>

RECEIVED  MAYDAY

( RRR  MAYDAY )

|  |  | D S C |
| --- | --- | --- |

DISTRESS  CALL

RECEIVED  ON

CH. 70 / 2187.5 kHz

VHF

3

DISTRESS   RELAY   PROCEDURE

SHIP  STATION  SHALL  SEND  A  DISTRESS  RELAY  IN  ANY  OF  THE  FOLLOWING  CASES :

- WHEN  THE  MOBILE  UNIT  IN  DISTRESS  IS  NOT

ITSELF  IN  POSITION  TO  TRANSMIT  THE  ALERT

(EX.,  AIRCRAFT  HAS  CRASHED   IN  THE  VICINITY

WITHOUT  ANY  DISTRESS  ALERT  TRANSMITTED);

- WHEN  MASTER  CONSIDERS  THAT  THE  FURTHER

HELP  IS  NECESSARY  (EX.,  VHF  DISTRESS  ALERT

RECEIVED  IN  THE  SEA  AREA  A2 / A3,  I.E.  VERY

FAR  FROM  THE  COAST  LINE);

A  STATION  IN  THE  MOBILE  OR  MOBILE-SATELLITE

SERVICE  TRANSMITTING  A  DISTRESS  ALERT  SHALL

INDICATE   THAT   IT   IS   NOT   ITSELF   IN   DISTRESS:

GENERAL  AND  SEARCH & RESCUE

COORDINATING  COMMUNICATIONS:

- RCC,  CRS  OR  OSC  MAY  IMPOSE  SILENCE

ON  STATIONS  WHICH  INTERFERE  WITH

DISTRESS  TRAFFIC  –  SEELONCE  MAYDAY.

THIS  INSTRUCTION  SHALL  BE  ADDRESSED

TO  ALL  STATIONS  OR  TO  ONE  STATION

ONLY,  ACCORDING  TO  CIRCUMSTANCES.

- WHEN  DISTRESS  TRAFFIC  HAS  CEASED  ON

FREQUENCIES  WHICH  HAVE  BEEN  USED

FOR  DISTRESS  TRAFFIC,  RCC ‘LL  INITIATE

A  MESSAGE  FOR  TRANSMISSION  ON  THESE

FREQUENCIES  -  SEELONCE  FEENEE ,  THAT

DISTRESS  TRAFFIC  HAS  FINISHED.

- STATIONS  ARE  FORBIDDEN  TO  USE  DISTRESS

FREQUENCIES  UNTIL  THEY  RECEIVE  MESSAGE

INDICATING  THAT  NORMAL  WORKING  MAY

BE  RESUMED  -  PRUDONCE.

TELEX

|  |  | D S C |
| --- | --- | --- |

MAYDAY

<ALL  SHIPS> 				X 3

THIS  IS

<CRS>  /  <OSC>			X 3

TIME  ...  UTC

<VSL  IN  DISTRESS>

SEELONCE  FEENEE

MAYDAY

<ALL  SHIPS>  /  <VSL  NAME>		X 3

THIS  IS

<CRS>  /  <OSC>			X 3

SEELONCE  MAYDAY

MAYDAY

<ALL  SHIPS> 				X 3

THIS  IS

<CRS>  /  <OSC>			X 3

TIME  ...  UTC

<VSL  IN  DISTRESS>

PRUDONCE

MAYDAY

<ALL  SHIPS> 				X 3

THIS  IS

<CRC>  /  <OSC>			X 3

TIME  ...  UTC

<VSL  IN  DISTRESS>

PRUDONCE

DISTRESS   CANCEL   PROCEDURE

STEP 1.

STOP   TRANSMISSION

( IF  AVAILABLE )

REFER  TO  MANUAL  INSTRUCTIONS  TO  PROCEED  CORRECT  WAY.

IT  IS  RECOMMENDED  NOT  TO  DISABLE  EQUIPMENT  BY  MEANS  OF  “POWER – OFF”.

STEP 2.

TRANSMIT  ANNOUNCEMENT

( DISTRESS  CANCEL  MESSAGE )

TO  INFORM  ALL  STATIONS  WHICH  COULD   RECEIVE  FAULT  ALERT.

NAME,  CALL  SIGN,  ID,  POSITION,

PLEASE  CANCEL  MY  < Inm-C / DSC / EPIRB >

DISTRESS  ALERT  OF  DATE,  TIME  UTC

Inmarsat-C  alert

To:  RCC

USE  THE  SAME  CES,  PRIORITY  -  DISTRESS.

EPIRB  alert

To:  RCC

USE  ANY  EQUIPMENT  -

TO  ANY  RCC  IN  AREA.

(ENTER  EPIRB  TYPE / ID)

DSC  alert

To:  All  stations

USE  ASSOCIATED

WORKING  CHANNELS.

4

STEP 3.

ENTER  DETAILS  IN  RADIO  LOG

FOLLOWING  EVENTS  TO  BE  ENTERED :  DISTRESS  ALERT  TRANSMISSION,  DISTRESS  CANCEL  MESSAGE  TRANSMISSION,  ITS  ACKNOWLEDGEMENT

BY  OTHER  STATIONS  -  KEEP  ALL  PRINT-OUTS.

To:  RCC

From:  MMSI, Name, call sign, Inm-C Nr, pstn

Cancel my Inm-C distress

Alert of Date, Time (utc)

MASTER

To:  RCC

From:  MMSI, Name, call sign, position

Cancel my EPIRB Alert of Date, Time (utc). EPIRB Type, Reg. Nr.

MASTER

Mayday

All  stations		x 3

This is

MMSI, Name, call sign,

position

Cancel my DSC alert of Date, Time (utc), Freq.

MASTER