GLOSSARY

TERMS USED ON ADMIRALTY CHARTS AND IN ASSOCIATED PUBLICATIONS

| Scope |
| --- |
| Definitions given are those in Departmental use and | aeronautical radiobeacon. A radiobeacon primarily |
| have no significance in International Law. Only terms | for the use of aircraft. Usually abbreviated to “aero |
| which are not already defined in English Dictionaries, | radiobeacon” |
| or which may be used with a significantly different |  |
| connotation are included in the glossary. | affluent. A tributary river or brook. |
| Exceptions to the definitions of certain terms in this |  |
| glossary, due to local custom and long usage, may | afloat. Floating, as opposed to being aground. |
| occasionally be met. |  |
| Foreign and local terms will be found in the | age of the Moon. The interval in days and decimals |
| glossaries of the appropriate volumes of Admiralty | of a day since the last New Moon. |
| Sailing Directions. |  |
| Lights, and terms used in association with lights, | age of the tide. Old term for the lag between the |
| Light-structures and fog signals, are described with | time of new or full Moon and the time of maximum |
| equivalent terms in 13 languages in Admiralty List of | spring tidal range. |
| Lights. |  |
| Weather reporting terms, with their equivalents in | agger. See double tide. |
| French, Spanish and Russian, are given in Admiralty, |  |
| List of Radio Signals Vol. 3. | agonic Iine. A line joining points on the Earth's |
|  | surface where there is no magnetic variation. |
| Terms |  |
|  | aground. Resting on the bottom. |
| abeam. See beam. |  |
|  | ALC. Articulated Loading Column. See 3.1 1 0. |
| abnormal magnetic variation. Designation applied |  |
| to any anomalous value of the magnetic variation | alongside. A ship is alongside when side by side with |
| of which the cause is unknown. cf local | a wharf, wall, jetty, or another ship. |
| magnetic anomaly. |  |
|  | ALP. Articulated Loading Platform. See 3.1 1 0. |
| aboard. In the sense used in pilotage and ship |  |
| handling means 'near'. eg 'To keep the E shore | amphidrome. A point in the sea where the tide has |
| aboard'. 'Close aboard' means 'Very near'. cf | no amplitude. Co-tidal lines radiate from an |
| borrow. | amphidromic point and co-range lines encircle it. |
| above. Uptide or upstream of a position. | anchorage. Water area which is suitable and of depth neither too deep nor too shallow, nor in a situation |
| above-water. A shoal, rock or other feature is termed above-water if it is visible at any state of the tide | too exposed , for vessels to ride in safety. An area set apart for vessels to anchor, such as: |
| cf awash, dries, below-water. | examination anchorage. One used by ships while awaiting examination. |
| abrupt. Steep; precipitous. cf bold. | quarantine anchorage. A special anchorage set aside in many ports, for ships in quarantine. |
| abyssal or abysmal. Relating to the greatest depths of the ocean (literally, without bottom). | safety fairway anchorage. An anchorage adjacent to a shipping safety fairway(qv). |
| abyssal gap. A narrow break in a ridge or rise, or | anchor buoy. Small buoy occasionally used to mark |
| separating two abyssal plains. | the position of the anchor when on the bottom; |
|  | usually painted green (starboard) or red (port), |
| abyssal hills. A tract of small elevations on the sea | and secured to the crown of the anchor by a buoy |
| floor. | rope. |
| abyssal plain. A flat, gently sloping or nearly level | angle of cut. The lesser angle between two, position |
| region at abyssal depths. | lines. |
| accretion or deposition. The depositing of material | aphelion. The point in the orbit of a planet which is |
| on the bottom or the coast by water movement; | farthest from the Sun. cf perihelion. |
| the opposite to erosion (qv). |  |
|  | apogee. The point in the orbit of the Moon which is |
| advance. When altering course, the distance that the | farthest from the Earth. cf perigee. |
| compass platform of a ship has advanced in the |  |
| direction of the original course on completion of a | approaches. The waterways that give access or |
| turn (the steadying point). It is measured from | passage to harbours, channels, etc. |
| the point where the wheel was put over. |  |

- 1 -

| GLOSSARY |
| --- |
| apron. The portion of a wharf or quay lying between | back. The wind is said to back when it changes |
| the waterside edge and the sheds, railway, lines or road. | direction anticlockwise |
| arch. Geologically, a covered passage cut through a | backshore. That part of the shore whose seaward |
| small headland by wave action. | limit is the waterline of MHWS and whose landward |
|  | limit is the extreme limit of wave action(such as occurs |
| archipelagic apron. A gentle slope with a generally | in onshore gales at equinoctial spring tides (qv)). |
| smooth surface on the sea floor, particularly found |  |
| around groups of islands or seamounts. | backwash. Waves reflected from obstructions such as |
|  | cliffs, seawalls, breakwaters, etc, running seaward |
| arc of visibility. The sector, or sectors, in which a | and combining with the incoming waves to cause |
| light is visible from seaward. | a steep and confused sea. |
| area to be avoided. A routeing measure comprising | backwash marks. Small scale oblique reticulate |
| an area within defined limits in which either navigation | pattern sometimes produced by the return swash |
| is particularly hazardous or it is exceptionally | of the waves on a sandy beach. cf ripple marks, beach cusps. |
| important to avoid casualties and which should |  |
| be avoided by all ships, or certain classes of ship. | backwater. An arm of the sea, usually lying parallel |
|  | with the coastal behind a narrow strip of land, or |
| arm (of a jetty, etc). A narrow portion projecting | an arm of a river out of the main channel, and out |
| from the main body. | of the main tidal stream or current. |
| arm of the sea. A comparatively narrow branch or | bank. Oceanographically, an area of positive relief |
| offshoot from a body of the sea. | over which the depth of water is relatively shallow, but |
|  | normally sufficient for safe surface navigation. The term |
| arming the lead. Placing tallow in the recess in the bottom | should not be used for features rising from the deep ocean. |
| of the sounding lead to ascertain the nature of the bottom. | Also, the margin of a watercourse, river, lake, canal, etc. |
|  | The right bank of a river is the one on the right |
| articulated loading platform or column (ALP) or | hand when facing downstream |
| (ALC). See 3.1 1 0.. |  |
|  | bar. A bank of sand, mud, gravel or shingle, etc near |
| artificial harbour. A harbour where the desired | the mouth of a river or at the approach to a |
| protection from wind and sea is obtained from | harbour, causing an obstruction to entry. |
| moles, jetties, breakwaters, etc. (The breakwater |  |
| may have been constructed by sinking concrete | bar buoy. A buoy indicating the position of a bar. |
| barges, vessels, etc, to form a temporary shelter.) |  |
|  | barrier. An obstruction, usually artificial in a river. |
| artificial horizon. A horizon produced by bubble, | eg Thames Barrier. |
| gyro or mercury trough to allow measurement of |  |
| altitude of celestial bodies. | barrier reef A coral reef, lying roughly parallel with |
|  | the shore, but separated from it by a channel or |
| astronomical arguments. See Admiralty Tide Tables. | lagoon. The distance offshore may vary from a |
|  | few metres to several miles. |
| astronomical twilight. The period between the end of |  |
| nautical twilight (qv) and the time when the Sun's | basalt. Dark green or brown igneous rock, often in |
| centre is 18( below the horizon in the evening, and | columnar strata. |
| the period between the time when the Sun's centre |  |
| is 18( below the horizon in the morning and the | basin. An almost land-locked area leading off an inlet, firth |
| beginning of nautical twilight in the morning. | or sound. Also, an area of water limited in extent and |
|  | nearly enclosed by structures alongside which vessels can lie. |
| atoll. A ring-shaped coral reef which has islands or | Oceanographically, a depression more or less |
| islets on it, the shallow rim enclosing a deeper natural | equidimensional in form, and of variable extent. |
| area or lagoon; often springing from oceanic depths. | tidal basin. A basin without caisson or gates |
|  | in which the level of water rises and falls |
| atollon. A small atoll on the margin of a larger one. | with the tide. Sometimes called an open basin. |
|  | non-tidal basin. A basin closed by a caisson or |
| awash. A shoal, rock or other feature is termed awash when | gates to shut it off from open water, so that a |
| its highest part is within 0.1 m of the level of the water. | constant level of water can be maintained in |
| In Admiralty Sailing Directions and on charts | it. Also called a wet dock. |
| such a feature is termed awash when its highest | impounding basin. A basin in which water |
| part is within 0.1 m, or with fathoms charts | can be held at a certain level, either to keep |
| within 1 foot, of chart datum (qv). | craft afloat or to provide water for sluicing. |
| awash at high water. May be just visible at MHWS or MHHW. | turning basin. An area of water or |
| cf dries, above-water. | enlargement of a channel in a port, where |
| - 2 - |

GLOSSARY

| vessels are enabled to turn, and which is kept | below-water. A shoal, rock or other feature is termed |
| --- | --- |
| clear of buoys, etc for that purpose. | below-water or underwater if it is not visible at any |
|  | state of the tide. ef above-water. |
| bathymetry. The science of the measurement of |  |
| marine depths. Submarine relief. | bench. See terrace. |
| bay. A comparatively gradual indentation in the | benchmark. A mark, which may. consist of an arrow cut in |
| coastline, the seaward opening of which is usually | masonry, a bolthead or a rivet fixed in concrete, etc, whose |
| wider than the penetration into the land. cf bight, gulf. | height, relative to some particular datum is exactly |
|  | known. (See Admiralty Tidal Handbook No. 2.) |
| bayou. Term used in Florida for a small bay, and in |  |
| Mississippi and Louisiana for a waterway through | berm. An horizontal ledge on the side of an embankment |
| lowlands or stamps, connecting other bodies of | or cutting to intercept falling earth or to add strength. |
| water, and usually tidal or with imperceptible current. | Also, a narrow, nearly horizontal shelf or ledge above |
|  | the foreshore built of material thrown up by storm |
| beach. Any part of the shore where mud, sand, shingle, | waves. The seaward margin is the crest of the berm |
| pebbles, etc, accumulate in a more or less. continuous sheet. |  |
| The term is not used to describe areas of jagged reef, rocks or coral. | berth. The space assigned to or taken up by a vessel |
| to beach. To run a vessel or boat ashore. To, | when anchored or when lying alongside a wharf jetty, etc. |
| haul a boat up on a beach. | to give a wide berth. To keep well away from |
|  | another ship or any feature. |
| beach cusps. Triangular ridges, or accumulations, of |  |
| sand or other detritus regularly spaced along the | bight. A crescent-shaped indentation in the coastline, |
| shore, the apex of the triangle pointing towards | of large extent and not more than a 90( |
| the water, giving a serrated form to the water edge. | sector of a circle. cf bay, gulf. |
| beach ridges. The seaward boundaries of successive | bilge (or keel) blocks. A row of wooden blocks on |
| positions of beaches on seaward-advancing shores. | which the bilges (or keel) of a ship rest when she |
| The intervening depressions may be extensive and | is in dock or on a slipway. |
| contain a lagoon, marsh, mangrove swamp, etc, or |  |
| be narrow and consist of sand. cf storm beach. | bill. A narrow promontory. |
| beacon. A fixed artificial navigational mark, | blather. Very wet mud, a feature of estuaries and rivers; of a |
| sometimes called a daybeacon in the USA and | dangerous nature such that a weight will at once sink into it. |
| Canada. It can be recognised by means of its |  |
| shape, colour, pattern or topmark. It may carry a | blind rollers. When a swell wave encounters shoal |
| light, radar reflector or other navigational aid. | water it is slowed and becomes steeper. If the |
|  | depth or extent of the shoal or rock is sufficient |
| beacon tower. A major masonry beacon the structure | to cause the wave to steepen markedly but not to |
| of which is as distinctive as the topmark. | break, the resulting wave is termed a blind roller. |
| beam: on the. An object is said to be on the beam, or abeam, | bluff. A headland or short stretch of cliff with a broad |
| if its bearing is approximately 90( from the ship’s head. | perpendicular face. |
|  | As adjective: Having broad perpendicular or |
| beam sea. The condition where the sea and swell approach | nearly perpendicular face. |
| the ship at approximately 90( from the ship's head. |  |
|  | boat camber. See camber. |
| bearing: |  |
| anchor bearing. The bearing of a shore | boat harbour. An area of sheltered water in a harbour set |
| object from the position of the anchor. | aside for the use of boats, usually with moorings, buoys, etc. |
| check bearing. The bearing of an extra |  |
| object taken to check the accuracy of a fix. | boat house. A shed at the water’s edge or above a |
| clearing bearing. The bearing of an object, | slipway for housing a boat or boats. |
| usually taken from a chart, to indicate |  |
| whether a ship is clear of danger. | boat pound. See pound. |
| line of bearing. A ship runs on a line of bearing if she makes |  |
| good a ground track on a constant bearing of an object. | boat slip. A slipway designed specifically for boats. |
| bed. The bottom of the ocean, sea, lake or river | boat yard. A boat-building establishment. |
| Usually qualified, eg seabed, river bed. |  |
|  | bog. Wet spongy ground consisting of decaying vegetation, |
| bell-buoy. A buoy fitted with a bell which may be | which retains stagnant water, too soft to bear the weight |
| actuated automatically or by wave motion. | of any heavy body. An extreme case of swamp or morass. |

- 3 -

GLOSSARY

| bold. Rising steeply from deep water. Well marked. | bridge-islet. An island which it connected to the |
| --- | --- |
| Clear cut. cf abrupt. | mainland, or to a larger island, at low water, or at |
|  | certain states of the tide, by a narrow ridge of |
| bold-to. Synonymous with steep-to. | rock, sand, shingle, etc. |
| bollard. A post usually steel or reinforced concrete) firmly | broach to. To slew around inadvertently broadside |
| embeded in or secured on a wharf, jetty, etc, for mooring | on to the sea, when running before it. |
| vessels by means of wires -or ropes extending from the |  |
| vessel and secured to the post. A very small bollard for | broadside on. Beam on (eg to wind or sea). |
| the use of barges and harbour craft may he called a 'dollie'. |  |
|  | broken water. A general term for a turbulent and |
| boom. A floating barrier of timber used to protect a | breaking sea in contrast to comparatively smooth |
| river or harbour mouth or to enclose a boat | and unbroken water in the vicinity. |
| harbour or timber pound. |  |
| Also, a barrier of hawsers and nets supported | brook . small stream. |
| by buoys used in the defence of a port or anchorage. |  |
|  | brow. An arrangement of wooden planking to give |
| booming ground. A term used mainly in Canadian waters and | passage between ship and shore when the ship is |
| similar to timber pound (qv) where logs are temporarily held | alongside. Also called a 'gangway'. |
| and stored for making up into rafts. The area is usually |  |
| enclosed by a boom to retain the logs. | building slip. A space in a shipbuilding yard where |
|  | foundations for launching ways and keel blocks |
| bore. A tidal wave which propagetes as a solitary wave | exist and which is occupied by a ship when being built. |
| with a steep leading edge up certain rivers. |  |
| Formation is most apparent in wedge-shaped | buoy. A 'floating, and. moored, artificial navigation |
| shoaling estuaries at times of spring tides. See | mark. It can he recognised by means of its shape, |
| Admiralty Manual of Tides. | colour, pattern, topmark or light character, or a |
|  | combination of these. It may carry various |
| borrow. In the sense used in pilotage means 'keep | additional aids to navigation. cf lanby, light- buoy. |
| towards, but not too near', eg ''To borrow on the |  |
| E side of the channel'. cf aboard. | buoyant beacon. A floating mark coupled to a sinker |
|  | either directly or by a cable that is held in tension |
| bottom, nature of the. The material of which the | by the buoyancy of the mark. Its appearance |
| seabed is formed, eg mud, stones. | above the water generally resembles a beacon |
|  | rather than a buoy; it does not rise and fall with |
| boulders. Water-rounded stones more than 256 mm | the tide; and it normally remains in a vertical or |
| in size, ie larger than a man's head, cf cobbles. | near-vertical position. Formerly known as, a Pivoted Beacon. |
| brackish. Water in which salinity values range from |  |
| approximately 0.50 to 17.00. |  |
|  | cable. A nautical unit of measurement. being one |
| breakers. Waves or swell which have become so steep, | tenth of a sea mile. See mile. |
| either on reaching shoal water or on encountering | Also, a term often used to refer to the chain cable by, |
| a contrary current or by the action of wind, that | which a vessel is secured to her anchor. Also used to |
| the crest falls over and breaks into foam. | refer to submarine, or overhead, power or telephone cables. |
| breaking sea. The partial collapse of the crests of | cable buoy. A buoy marking the end of a submarine |
| waves, less complete than in the case of breakers, | cable on which a cable ship is working. Also used |
| but from the same cause; also know as White Horses. | in the sense of a telegraph buoy (qv). |
| breakwater. A solid structure, such as a wall or mole, | cairn. A mound of rough stones or concrete of |
| to break the force of the waves, sometimes detached | pyramidal or beehive shape used as a landmark. |
| from the shore, protecting a harbour or anchorage. | caisson. A structure used to close the entrance to dry |
| Vessels usually cannot lie alongside a breakwater. | docks, locks and non-tidal basins. They are of two |
|  | kinds; floating caissons which are detachable from |
| bridge. A narrow ridge of rock, sand or shingle, across | the entrance they close, and sliding caisson which |
| the bottom of a channel so as to constitute a shoal | slide into a recess at the side of the dock. cf |
| or shallow.. | cofferdam. |
| Structure carrying road, etc, across waterway, road, ravine, | There are also dry docks which are closed by |
| etc. Movable bridges are usually swing bridges or lifting | raising a flap-type door, hinged at the outer side |
| or bascule bridges. Swing bridges may pivot about a point, | of the dock sill. |
| either in mid- channel or on the bank. Bascule bridges may be |  |
| single or double, depending on whether they lift | calcareous. Formed of, or containing, carbonate of |
| from one or both banks. | lime or limestone. |

- 4 -

GLOSSARY

| calling-in point. See reporting point. | the best and safest passage for vessels or boats. |
| --- | --- |
|  | The name given to certain wide straits or |
| CALM. Catenary Anchor Leg Mooring. See 3.106. | arms of the sea, eg English Channel, Bristol Channel. |
|  | Oceanographically, a river valley-like elongated |
| calving. The breaking away of rock, stones, earth, etc | depression in ocean basins, commonly found in fans (qv). |
| from the face of a cliff. For Ice term, see Ice Glossary. |  |
|  | character or characteristic of a light. The |
| camber. A small basin usually with a narrow | distinctive rhythm and colour, or colours, of a |
| entrance, generally situated inside a harbour. eg | light signal that provide the identification or |
| Boat camber: a small basin for the exclusive use of boats. | message, See Admiralty List of Lights. |
| camel. A tank filled with water and placed against | chart datum. A level so low that the tide will not |
| the hull of 2t stranded or sunken vessel. It is well | frequently fall below it. In the United Kingdom, |
| secured to the vessel and then pumped out, the | this level is normally approximately the level of |
| buoyancy thus added helping to lift the vessel. | Lowest Astronomical Tide. It is the level below |
|  | which soundings are given on Admiralty charts, |
| can buoy. A nearly cylindrical buoy moored so that a | and above which are given the drying heights of |
| flat end is uppermost. | features which are periodically covered and |
|  | uncovered by the tide. Chart datum is also the |
| canal. A channel dredged or cut through dry land or | level to which tidal levels and predictions are |
| through drying shoals or banks and used as a. | referred in Admiralty Tide Tables. See 4. 1 |
| waterway. cf ship canal. |  |
|  | cill See dock sill. |
| canal port. A port so situated that the waterway is |  |
| entirely artificial. | cinders. Fragments formed when magma is blow |
|  | into the air; larger in size than volcanic ash. |
| canyon. A deep gorge or ravine with steep sides, at |  |
| the bottom of which a river flows. | circular radiobeacon. A radiobeacon which |
| Oceanographically, a relatively narrow, deep | transmits the same signal in all directions. |
| depression with steep sides, the bottom of which |  |
| slopes continuously, downwards. | civil twilight. The periods of the day between the |
|  | time when the Sun's centre is 6( below the horizon |
| cape. a piece of land, or point, facing the open sea | and Sunrise (morning twilight), or between sunset |
| and projecting into it beyond the adjacent coast. | and the time when the Sun's centre is 6( below. |
|  | the horizon (evening twilight). |
| cargo transfer area. See transhipment area. |  |
| cast. To turn a ship to a desired direction without | claw off. To beat or reach to windward away from a lee shore. |
| gaining headway or sternway. |  |
|  | clay. A stiff tenacious sediment having a |
| catamaran. A floating stage or raft used in shipyards, | preponderance of grains with diameters of less |
| for working from, and sometimes used as a fender | than 0.004 mm. It is impossible to differentiate |
| between ship and wharf, etc. | between clay and silt by eye, but a sample of |
| Also, a type of twin-hulled yacht. | wet clay, when dried in the palm of the hand, |
| (The name is taken from various native-built craft common | will not rub off when the hands are rubbed together. |
| in the East Indies and some other parts of the world.) |  |
|  | clean. Applied to the bottom of the sea, harbour or |
| catenary anchor leg mooring (CALM). See 3.106. | river, means free from rocks or obstructions. cf foul. |
| catwalk. A narrow footway forming a bridge, eg | clearing bearing. See bearing. |
| connecting a mooring dolphin to a pierhead. Also |  |
| known as a walkway. | clearing marks. Selected marks, natural or |
|  | otherwise, which in transit clear a danger or which |
| causeway. A raised roadway of solid structure built | mark the boundary between safe and dangerous |
| across low or wet ground or across a stretch of water. | areas for navigation. |
| cay. A small insular feature usually with scant | cliff. Land projecting nearly vertically from the water |
| vegetation; usually of sand or coral. Often applied | or from surrounding land, and varying from an inconspicuous |
| to smaller coral shoals. cf islet. | slope at the margin of a low coastal plain to a high vertical |
|  | feature at the seaward edge of high ground. Can |
| centreline controlling depth. See controlling depths. | be formed by a fault in geological strata (inland). |
| channel. A comparatively deep waterway, natural. | close (verb). To approach near |
| dredged, through a river, harbour, strait, etc, or |  |
| a navigable route through shoal, which affords | close aboard. Very near. |

- 5 -

GLOSSARY

| coast. The meeting of the land and sea considered as | conspicuous object. A natural or artificial mark |
| --- | --- |
| the boundary of the land. cf shore. | which is outstanding, easily identifiable, and |
| Also, the narrow strip immediately landward of | clearly visible to the Mariner over a large area of |
| the waterline of MHWS, or sometimes a much | sea in varying conditions of light. If the scale is |
| broader zone extending some distance inland. | large enough they will normally be shown on |
|  | charts in bold capitals, or on older charts by the |
| coastal plain. A strip of flat consolidated land varying | note 'conspic'. cf prominent. |
| in width which may occur immediately landward |  |
| of the coastline. | constants (harmonic). The phase-lag (g) and the |
|  | amplitude (H) of a constituent of the tide. |
| coastal waters. The sea in the vicinity of the coast |  |
| (within which the coasting trade is carried out). | constants (non-harmonic). The average time and |
|  | height difference of high and low water, referred |
| coasting. Navigating from headland to headland in | to the times and heights at a standard port; the |
| sight of land, or sufficiently often in sight of land | time can also be referred to the time of Moon's transit. |
| to fix the position of the ship by land features. |  |
|  | constituent (of the tide). The tidal curve can be |
| coastland. The strip of land with a somewhat | considered as being composed of a number of |
| indeterminate inner limit, immediately landward | cosine curves, having different speeds, phase-lags |
| of she coastline. It may include such features as | and amplitudes, the speed being determined from |
| sand dunes, saltings, etc, which are associated | astronomical theory and the phase-lags and |
| proximity to the sea, and merges into the | amplitudes being determined from observation |
| innerland where the features cease. | and analysis. These cosine curves are known as |
|  | constituents of the tide. See Admiralty Tidal |
| coastline. The landward limit of the beach. The | Handbooks No 1. |
| extreme limit of direct wave action (such as occurs |  |
| in on shore gales during Equinoctial Spring Tides. | container. A rigid, non-disposable, cargo-carrying |
| cf backshore. It may be some distance above the | unit, with or without wheels. Standard lengths |
| waterline of Mean High Water Springs, but for | are 6.1 m (Twenty-foot Equivalent Unit (teu)) |
| practical hydrographic purposes the two are | and 12.2m (Forty-foot Equivalent Unit (teu)): |
| usually regarded as coincident. | both width and height are standardised at 2.44 m. |
| Also, a general term used in describing the | The main types of container are: |
| shore or coast as viewed from seaward, eg a low coastline. | collapsible: Can be stowed when not in use; |
|  | dry bulk: For cargoes such as dry chemicals or grain; |
| coast radio station. See radio stations. | dry cargo: For general cargo; |
|  | flat rack: For timber, large items or machinery; |
| coastwise (adjective and adverb). Near to the coast, | refrigerated: Insulated and usually fitted with |
| eg Coastwise traffic is that which sails round the | its own refrigeration systems. |
| coast and to sail coastwise means, coasting as |  |
| opposed to keeping out to sea. | container terminal. A specially equipped berth with |
|  | storage area, where standard cargo containers are |
| cobbles. Water-rounded stones of from 64 mm to | loaded or unloaded. |
| 256 mm in size, ie from the diameter of a man's |  |
| clenched fist when viewed sideways to slightly | continental borderland. A province adjacent to a |
| larger than the size of a man's head. cf pebbles, boulders. | continent, normally occupied by or bordering a |
|  | continental shelf, that is highly irregular, with depths |
| cocked hat. The triangle sometimes formed by the | well in excess of those typical of a continental shelf. |
| intersection of three lines of bearing on the chart. cf cut. |  |
|  | continental margin. The zone, generally consisting |
| cofferdam. Watertight screen or enclosure used in | of the shelf, slope and rise, separating the |
| laying foundations underwater; sometimes called a caisson. | continent from the deep sea bottom. |
| combers. Steep, long swell waves with high breaking crests. | continental rise. A gentle slope rising from the |
|  | oceanic depths towards the foot of the continental slope. |
| cone. See fan. |  |
|  | continental shelf. A zone adjacent to a continent (or |
| confused sea. The disorderly sea in a race; also when | around an island) and extending from the low |
| from different directions meet, due normally | water line to a depth at which there is usually a |
| to a sudden shift in the direction of the wind. | marked increase of slope towards oceanic depths. |
|  | Conventionally, its edge is taken as 200 m, but it |
| conformal projection. Another name for | may be between about 100 m and 350 m. |
| orthomorphic projection (qv). |  |
|  | continental slope. The slope seaward from the shelf |
| conical buoy. A cone-shaped buoy moored to float | edge to the beginning of a continental rise or the |
| point up. cf can buoy, nun buoy. | point where there is a general reduction in slope. |

- 6 -

GLOSSARY

| contour. A line joining points of the same height | at a standard port or as intervals after the time-of |
| --- | --- |
| above or depths below, the datum. cf fathom line. | Moon's transit. |
| controlling depth. Depths in a channel are | course. The intended direction of the ship's head. |
| designated as follows: |  |
| controlling depth. The least depth within the | course made good. The resultant horizontal |
| limits of a channel: it restricts the safe use of | direction of actual travel. The direction of a point |
| the channel to draughts of less than that depth. | of arrival from a point of departure. |
| centreline controlling depth. A depth which |  |
| applies only to the channel centreline: lesser | cove. A small indentation in a coast (usually a cliffy |
| depths may exist in the remainder of the channel. | one), frequently, with a restricted entrance and |
| mid-channel controlling depth. A depth | often circular or semi-circular in shape. |
| which applies only to the middle half of the channel. |  |
|  | cradle. A carriage of wood or metal in which a vessel |
| convergence. The boundary or region where two | sits on a slipway. |
| converging currents meet, with the result that the |  |
| water of the current of higher density sinks below | craft. A term applied to small vessels and boats. |
| the surface and spreads out at a depth which | harbour craft. Boats, barges, lighters,. etc, used |
| depends on its density. | on harbour work. |
|  | a handy craft. An easily manoeuvred boat. |
| conveyor. Belt of buckets or similar contrivance for |  |
| transporting cargo, especially ores or coal, from | crane. A mechanical contrivance for lifting weights. |
| ship to shore or vice versa. | The main types are: |
|  | cargo crane. For transferring cargo between |
| coping. The top course of masonry in a wall: the | a ship's hold and the shore or lighter; |
| waterside top edge of a wall. | container crane. Specifically intended for |
|  | handling containers; |
| coral. Hard calcareous substance secreted by many | fixed crane. Built on the shore for use in |
| species of marine polyps for support, habitation, | one place only; |
| .etc. It may be found either dead or alive. See 4.52. | floating crane. Mounted on a lighter or |
|  | pontoon. cf crane lighter; |
| coral island. An island principally or entirely | gantry crane. Mounted on a frame or |
| formed of coral. It may be one of three kinds: | structure spanning an intervening space. cf |
| an elevated coral reef forming an island; a reef | transporter; |
| island formed by the accumulation of coral | luffing crane. Can move a load nearer or farther from |
| debris on a submerged fringing or barrier reef; | the base of the crane by raising or lowering the jib; |
| or an atoll. | mobile or crawler crane. Self-propelled on |
|  | wheels or caterpillar tracks; |
| coral reef. Reefs, often of large extent, composed | portal crane. A type of gantry crane with vertical legs |
| chiefly of coral and its derivatives. See atoll, | giving sufficient height and width for vehicles |
| barrier reef, fringing reef. | or railway trucks to pass between them; |
|  | wharf crane. Located on a wharf or pier |
| co-range lines. Lines on a tidal chart joining points | specifically for serving vessels alongside it. |
| which have the same tidal range or amplitude; also | crane lighter. A lighter especially fitted with a crane. |
| called co-amplitude lines. Usually. drawn for a | May be self-propelled or towed. |
| particular tidal constitutent or tidal condition (eg |  |
| mean spring tides). | crater. A bowl-shaped cavity. in particular, at the |
|  | summit or on the side of a volcano. |
| cordillera. An entire mountain province, including all |  |
| the subordinate ranges and groups and the interior | creek. A comparatively narrow inlet, of fresh or salt |
| plateaux and basins. | water, which is tidal throughout its course. |
| coriolis force. An apparent force acting on a body in | crest. Of a hill, the head, summit or top: of a mountain |
| motion, due to the rotation of the Earth, causing | range, the line joining the highest points. Similarly, |
| deflection (eg of winds and currents), to the right | of an elevation of the seabed, or of a swell or wave. |
| in the N hemisphere and to the left in the S |  |
| hemisphere. | cross-sea. A wave formation imposed across the |
|  | prevailing waves. cf confused sea. |
| co-tidal chart. A chart combining co-range lines with |  |
| co-tidal lines; co-tidal charts may refer to the tide | cross-swell. Similar to cross-sea but the waves are |
| as a whole or to one or more tidal constituents. | longer swell waves. |
| co-tidal lines. Lines joining points at which high | culvert. A tunnelled drain or means of conveying water beneath |
| water (or low water) occurs simultaneously. The | a canal, railway embankment or road (sometimes the |
| times may be expressed as differences from times | size of a small bridge, ie up to about 3 m across). |

- 7 -

GLOSSARY

| Also, a channel for electric cables. | which has been accurately surveyed for clearance |
| --- | --- |
|  | of sea bottom and submerged obstacles as |
| current. The non-tidal horizontal movement of the | indicated on the chart. cf recommended track.. |
| sea which may be in the upper, lower or in all |  |
| layers. In some areas this movement may be | defile. A narrow mountain pass or gorge. |
| nearly constant in rate and direction while in |  |
| others it may vary seasonally or fluctuate with | degaussing range. An area about 2 cables in extent |
| changes in meteorological conditions. The term is | set aside for measuring ships' magnetic fields. |
| often used improperly to denote tidal streams. See 4.17. | Sensing instruments are installed on the seabed |
|  | in the range with cables leading to a control |
| cut. The intersection on the chart of two or more | position ashore. The range is usually marked by buoys. |
| position lines. |  |
| An opening in an elevation or channel. Similar | degenerate amphidrome. A terrestial point on a |
| to a canal but shorter. May constitute a | tidal chart from which co-tidal lines appear to radiate. |
| straightening of a bend in a winding channel. |  |
|  | delta. A tract of alluvial land, generally triangular, |
| cut tide. A tide which fails to reach its predicted | enclosed and traversed by the diverging mouths |
| height at high water. | of a river. |
|  | departure; point of. The last position fixed relative |
|  | to the land at the beginning of an ocean voyage or passage. |
| dam. A bank of earth or masonry, etc, built to |  |
| obstruct the flow of water, or to contain it. | deposition. See accretion. |
| dan buoy. An anchored float, ballasted to float | depth. The vertical distance from the sea surface to |
| upright carrying a stave through its centre with a | the seabed, at any state of the tide. |
| flag, a light or other distinguishing mark. | Hydrographically, the depth of water below chart |
|  | datum. cf sounding. |
| danger. The term is used to imply a danger to surface |  |
| navigation. | derrick. A contrivance for hoisting heavy weights. |
|  | Usually consisting of a wooden or metal spar with |
| danger angle: horizontal or vertical. The angle | one end raised by a topping lift from a post or |
| subtended at the observer's eye, by the horizontal | mast and the other end pivoted near the base. |
| distance between two objects or by the height or | diatom. Microscopic phytoplankton, especially |
| elevation of an object, which indicates the limit of | common in the polar seas; develops delicate cases |
| safe approach to an off-lying danger. | of silica. |
| danger line. A dotted line on the chart enclosing, or | diatom ooze. A siliceous deep-sea ooze formed of the |
| bordering, an obstruction, wreck, or other danger. | shells of diatorns. |
| Date Line. The International Date Line, accepted by | diffuser. An arrangement of multiple outlets for |
| international usage, is a modification of the 180( | distributing liquid at the seaward end of a pipeline |
| meridian to include islands of any group, etc on | or outfall. |
| the same side of the line. Its position is shown on |  |
| Chart 5006 - The World -Time Zone Chart and | dike. See dyke. |
| described in Admiralty List of Radio Signals Vol 5. |  |
| cf time zones. | directional radiobeacon. A radiobeacon which |
| When the Date Line is crossed on an E course | transmits two signals in such a way that they are |
| the date is put back one day, on a W course the | of equal strength on only one bearing. |
| date is advanced one day. |  |
|  | discoloured water. See 4.45. |
| datum. See horizontal datum, vertical datum. |  |
|  | diurnal inequality. The inequality, either in the |
| daybeacon. A term used in the USA and Canada for | heights of successive high waters or in the |
| a beacon: in the USA it is restricted to unlighted beacons. | intervals between successive high or low waters. |
| daymark. Large unlit beacon. Term also used to | diurnal stream. A tidal stream which reverses its |
| denote an unlit topmark or other distinguishing | direction once during the day. |
| mark or shape incorporated into a beacon, light- |  |
| buoy or buoy. | diurnal tide. A tide which has only one high water |
|  | and one low water each day; that part of a tide |
| deep. A relatively small area of greater depth than its | which has one complete oscillation in a day. |
| surroundings, primarily used for the deeper parts |  |
| of the great ocean trenches. cf hole. | dock. An area of water artificially enclosed in which |
|  | the depth of water can be regulated. Also used |
| deep-water route. A route within defined limits | loosely to mean a tidal basin (qv). |

- 8 -

GLOSSARY

| to dock. To be admitted to a dock. | height above chart datum, which is indicated on |
| --- | --- |
| to dock a ship. To receive a ship into dock, or dry dock. | charts by a bar under the figure, or the legend |
| docks. The area comprising the basins, quays, | 'Dries' which may be abbreviated to 'Dr'. cf awash. |
| wharves, etc, and offices of a port; the dock area. |  |
|  | drift. The distance covered by a vessel in a given time |
| dock sill. The horizontal masonry or timber work at | due solely to the movement of current or tidal stream, or both. |
| the bottom of the entrance to a dock or lock | Also a detached and floating mass of soil and |
| against which the caisson or gates close. The | growth torn front the shore or river bank by |
| depth of water controlling the use of the dock is | floods, often mistaken for an islet. (Common in the |
| measured at the sill. | East Indies.) |
|  | (verb) To move by action of the wind and |
| dockyard. That part of a port which contains the | current without control. |
| facilities for building or repairing ships. |  |
|  | drift angle. The angle between the ground track and |
| dollie. See bollard. | water track. |
| dolphin. A built-up post, usually of wood, erected on | drift current. A horizontal movement in the upper |
| shore or in the water. | layers of the sea, caused by wind. See 4.23. |
| berthing dolphins. Dolphins against which a |  |
| ship may lie. Also known as breasting dolphins. | drilling rig. A movable floating platform used to |
| mooring dolphins. Dolphins which support bollards for | examine a possible oil or gasfield. See 3.97. |
| a ship’s mooring lines. The ship does not come into |  |
| contact with them as they are set clear of the berth. | drillship. A ship specially designed for offshore |
| deviation dolphin. Dolphin which a ship may | drilling of the seabed. See 3.97. |
| swing around for compass adjustment. |  |
|  | dry dock. An excavation in the ground, faced with |
| double tide. A tide which, due to a combination of | masonry or concrete, into which a ship is admitted |
| shallow water effects, contains either two high | for underwater cleaning and repairs. The entrance |
| waters or two low waters in each tidal cycle. | can be closed by a caisson or gate. The water is pumped |
| At Hook of Holland, this phenomenon occurs | out after a vessel has entered, leaving her dry, resting |
| with the low waters and is known as the Agger. | on blocks and generally also supported by shores. |
|  | Sometimes called a 'graving dock'. cf floating dock. |
| downstream. In particular, the direction in which the |  |
| stream is flowing; in general, in rivers and river | dry harbour. A small harbour which dries out, or |
| ports, whether tidal or not, the direction to seaward. | nearly so, at LW. Vessels using it must be |
|  | prepared to take the ground on the falling tide. |
| drag. A ship is said to drag (her anchor) if the anchor |  |
| will not hold her in position. | drying heights. Heights above chart datum of |
| Also commonly used by seamen to describe the | features which are periodically, covered and |
| retardation of a ship caused by shallow water. | exposed by the rise and fall of the tide. cf awash. |
| drag sweep. To tow a wire or bar set horizontally | dumb lighter. A lighter incapable of self-propulsion. |
| beneath the surface of the water to determine the |  |
| least depth over an obstruction or to ascertain that | dumping ground. An area similar to a spoil ground. |
| a required minimum depth exists in a channel. |  |
| Used as a noun, to denote the apparatus for this. | dune. A ridge or hill of dry wind-blown sand which |
|  | may, or may not, be in a state of migration. |
| dredge. To deepen or attempt to deepen by, removing, | Vegetation (frequently planted on purpose) often |
| material from the bottom. | stabilises previously migrating dunes. Coastal dunes |
| Also an apparatus for bringing up bottom | may occur in the vicinity of sandy shores, but cannot |
| samples, gathering deep water organisms, etc. | survive wave action consequently they are features |
| dredged area. Area where the depths have been | of the coastland rather than of the foreshore. |
| increased by, the removal of material from the bottom. |  |
| dredger or dredge. A special vessel fitted with | duration (of rise or fall of the tide). The time interval |
| machinery for dredging, employed in deepening, | between successive high and low waters. |
| channels, harbours, etc, and removing |  |
| obstructions to navigation such as shoals and | dyke or dike. A causeway or loose rubble embankment |
| banks. The various types include: Bucket | built in shallow water in a similar way to a training |
| dredgers, Grab dredgers and Suction dredgers. | wall, but not necessarily for the same purpose. |
|  | Sometimes built across shallow banks at the side of an |
| dredging anchor. A vessel is said to be dredging | estuary to stabilise the sandbanks by protection against |
| anchor when moving, under control, with her | wave action, and to prevent silting in the channel |
| anchor moving along the seabed. | In the Netherlands: an embankment to prevent |
|  | flooding and encroachment by the sea. |
| dries. A feature which is covered and uncovered by | In Orkney and Shetland Islands: a wall. |
| the tide is said to dry. The drying height is the | Also used to mean an artificial ditsh. |

- 9 -

GLOSSARY

| ebb channel. See flood channel. | when a ship is floating at her designed draught marks. |
| --- | --- |
| ebb tide. A loose term applied both to the failing tide | Exposed Location Single Buoy Mooring (ELSBM). See 3.107. |
| and to the outgoing tidal stream. |  |
|  | eyot. A small island in a river. |
| eddy. A circular motion in water; a horizontal |  |
| movement in a different direction from that of the |  |
| general direction of the tidal stream in the vicinity, |  |
| caused by obstructions such as islands, rocks, etc, or by | fairway. The main navigable channel, often buoyed, |
| the frictional effects of beaches, banks, breakwaters, etc. | in a river, or running through or into a harbour. |
| elbow. A change of direction in the contour of a | falling tide. The period between high water and the |
| submerged bank or shoal; a sharp change in the | succeeding low water. |
| direction of a channel, breakwater, pier, etc. |  |
|  | fan. A relatively smooth feature normally sloping away |
| elevation. That which rises above its surroundings, | from the lower termination of a canyon or canyon |
| such as a hill, etc. | system. Also termed a Cone. |
| On a chart, the elevation of a feature is its height |  |
| above the level of MHWS or MHHW. cf heights. | fastener. See snag. |
| ELSBM. Exposed Location Single Buoy Mooring. See3.107. | fathom. A unit of measurement used for soundings. |
|  | Equal to 6 feet or 1.8288 m. |
| embankment. A sloping structure of stone, rubble or earth, |  |
| raising the height of a river bank, or used as the | fathom lines. Submarine contour lines drawn on |
| foundation for, or strengthening of, a causeway or dyke. | charts, indicating equal depths in fathoms. |
| embayed. To be in such a position, or under such | ferry. A boat, pontoon, or any craft, used to convey |
| adverse conditions, in a bay that extrication is | passengers or vehicles to and fro across a harbour, |
| difficult if not impossible. | river, etc. See also train ferry. |
|  | To ferry. To convey in a boat, to and fro over |
| entrance lock. A lock situated between the tideway | a river, across a harbour, etc. |
| and an enclosed basin. Since their levels vary the |  |
| lock has two sets of gates by means of which | fetch. The area of the sea surface over which seas are |
| vessels can pass either way at all states of the tide. | generated by a wind having a constant direction and speed. |
| Sometimes known as a Tidal lock. | Also, the length of the generating area, |
|  | measured in the direction of the wind, in which |
| equilibrium tide. The hypothetical tide which would | the seas are generated. |
| be produced by the lunar and solar tidal forces in |  |
| the absence of ocean constraints and dynamics. | fish aggregating device. A general term used to |
|  | designate fish havens, marine farms (qv), etc. |
| equinoctial spring tide. A spring tide (greater than |  |
| average) occurring near the equinox (in March | fish farm. See marine farm. |
| and September). |  |
|  | fish haven. An area where concrete blocks, hulks, |
| equinox. Either of the two points at which the Sun | disused car bodies, etc, are dumped to provide |
| crosses the equator: or the dates on which these | suitable conditions for fish to breed in. Devices |
| occurrences take place. | may also be moored in rnid-water or on the |
|  | surface to serve the same purpose. |
| erosion. The wearing away of the coast (or banks of a | In Japanese waters, the term 'floating fish |
| river) by water action; the opposite of accretion. | haven' may be used instead of marine farm |
|  | (qv). |
| escarpment. An elongated and comparatively steep | Draught permitting, vessels may navigate over |
| slope separating flat or gently sloping areas. | seabed fish havens, but they are hazards to |
|  | anchoring or seabed operations. |
| established direction of traffic flow. See traffic flow. |  |
|  | fish pound. A barrier across the mouth of a creek |
| estuary. An arm of the sea at the mouth of a tidal | placed to retain fish in a creek. |
| river, usually encumbered with shoals, where the |  |
| tidal effect is influenced by the river current. | fish stakes. A row of stakes set out from the shore, |
|  | frequently to a considerable distance; often |
| estuary port. A port built at the tidal mouth or | terminating in a partly decked enclosure from |
| estuary of a river. | which a net can be lowered. |
| even keel. The state of a ship when her draught | fish trap. An enclosure of stakes set in a stream or |
| forward and aft are the same. Loosely applied | shallow water as a trap for fish. |

- 10 -

GLOSSARY

| fish weir. An enclosure of stakes set in a stream or on | foraminifera. Single-celled animals consisting of a |
| --- | --- |
| the shoreline as a trap for fish. | mass of jelly-like flesh with no definite organs or |
|  | parts of the body; covered with a casing of carbonate |
| fishing ground. Area wherein craft congregate to fish; | of lime common in the surface waters of the sea. |
| most particularly those areas occupied periodically |  |
| by the large fishing fleets. | forced tide. A tide which exceeds its predicted height |
|  | at high water. |
| fishing harbour or port. One especially equipped for |  |
| the convenience of the fishing industry, the | foreland. A promontory or headland. |
| handling of fish and the maintenance of its vessels. |  |
|  | foreshore. A part of the shore lying between high and |
| fitting-out basin. A basin in a shipyard sited and | low water lines of Mean Spring tides. |
| equipped, to accommodate ships to complete the |  |
| installation of machinery, etc, after launching. | form lines. Lines drawn on a chart to indicate the |
|  | slope and general shape of the hill. features; |
| fix. The position of the ship determined by observations. | generalised contour lines which do not represent |
|  | any specific or standardised heights. ef hachure. |
| flat. An extensive area, level or nearly so, consisting |  |
| usually of mud, but sometimes of sand or rock, | foul area, foul bottom or foul patch. An area where |
| which is covered at high water and is attached to | the seabed is strewn with wreckage or other obstructions, |
| the shore. Sometimes called Tidal flats. cf ledge. | no longer dangerous to surface navigation, |
|  | but making it unsuitable for anchoring. |
| floating beacon. A moored or anchored floating mark | foul ground. An area where the holding |
| ballasted to float upright, usually displaying a flag | qualities for an anchor are poor, or where danger |
| on a tall pole, and sometimes carrying a light or | of striking or fouling the ground or other |
| radar reflector; used particularly in hydrographic | obstructions exist. |
| surveying. |  |
|  | foul bottom. The bottom of a ship when encrusted |
| floating bridge. A power-worked pontoon used as a | with marine growth. |
| ferry which propels itself across a harbour, river, |  |
| canal, etc, by means of guide chains. | fracture zone. An extensive linear zone of irregular |
|  | topography of the. sea floor, characterised by |
| floating crane. See crane. | steep-sided or asymmetrical ridges, troughs or |
|  | escarpments. |
| floating dock. A watertight structure capable of being |  |
| submerged sufficiently, by admission of water | free port. A port where certain import and export |
| into the pontoon tanks, to admit a vessel. The | duties are waived (unless the goods pass into the |
| tanks are then pumped out, the dock and vessel | country), to facilitate re-shiprnent to other |
| rising until the latter is clear of the water, thus | countries. cf transit port. |
| serving the same purpose as a dry dock. |  |
|  | freshet. An abnormal amount of fresh water running |
| flood channel. A channel in tidal waters through | into a river, estuary or the sea, caused by heavy |
| which the flood (incoming) tidal stream flows | or prolonged rain or melted snow. |
| more strongly, or for a longer duration of time, |  |
| than the ebb. It is characterised by a sill or bar | fringing reef. A reef, generally coral, closely attached to the |
| of sand or others consolidated matter at the inner | shore with no lagoon or passage between it and the land. |
| end, ie the least depth in the channel occurs |  |
| close to the inner end. Ebb channels occur in | full and change. See high water full and change. |
| close association with, and _usually alongside, |  |
| flood channels: they have a sill at their outer end. | furrow. Oceanographically, a fissure which |
|  | penetrates roughly perpendicularly to the run of |
| flood-mark. A mark, consisting usually of a | the contours, into the continental or island shelf |
| horizontal line and a date, sometimes found on | or slope. cf canyon. |
| riverside buildings, dock walls, etc, to mark the |  |
| highest level reached by flood waters at the date |  |
| indicated. |  |
|  | gangway. Similar to a brow (qv) when it is |
| flood tide. A loose term applied both to the rising | sometimes called a gangplank. |
| tide and to the incoming tidal stream. cf ebb tide. | Also, the actual opening in the ship's side by |
|  | which a ship is entered or left. |
| flow. The combination of tidal stream and current; | Also, a passage-way in a ship. |
| the whole water movement. |  |
| Also a loose term for flood (eg ebb and flow). | gap. Oceanographically, a break in a ridge or rise. |
| following sea. One running in the same direction as | gar. A swashway, gut or natural channel through |
| the ship is steering. | shoals. |
| - 11 - |

GLOSSARY

| geodesic. The shortest distance between two points on the | ground track. See track. |
| --- | --- |
| spheroid. It is equivalent to a great circle on the sphere. |  |
|  | groyne. A low wall-like structure, generally of wood |
| geodetic datum. See horizontal datum. | or stone, usually extending at right angles from |
|  | the shore, to prevent erosion. Frequently erected |
| geographical mile. See mile. | in estuaries and rivers to direct the flow of the |
|  | water and prevent silting or encourage accretion. |
| geoid. An imaginary surface which is everywhere |  |
| perpendicular to the plumb line, and which on | gulf. A portion of the sea partly enclosed by land; |
| average coincides with Mean Sea Level in the | usually of larger extent and greater relative |
| open ocean. Its shape approximates to that of a | penetration than a bay. |
| spheroid, but it is irregular due to the uneven |  |
| distribution of the Earth's mass. | gut. A natural narrow inlet of deep water in a bank or |
|  | shoal, sometimes forming a channel through it. It |
| gird. To gird a ship is to prevent her from swinging | may also refer to the main part of a channel. |
| to wind and tide. Of a tug, to be towed broadside |  |
| on through the water by her tow-rope. | guyot. See tablemount. |
| globigerina ooze. Ooze which has the limy skeletons |  |
| of foraminifera as its principal constituent, the |  |
| dominant element being the calcareous tests of the | hachures. Shading lines sometimes used on charts |
| globigerina (a spherical shelled organism). | and maps to indicate the general slope and shape |
|  | of hill forms. cf form lines. |
| godown. A term used in Eastern ports for a |  |
| warehouse or store. | half tide. The height of the tide halfway between high |
|  | water and low water. cf. mean tide level. |
| gong-buoy. A buoy fitted with a gong which may be |  |
| actuated automatically or by wave motion. | half-tide basin. A basin the gates of which are open for |
|  | entry and departure some hours before and after high water. |
| gradient currents. Currents caused by pressure |  |
| gradients in the water. See 4.27. | half-tide rock. Formerly used to describe rocks which |
|  | are awash at about mean tide level. |
| gravel. Coarse sand and small water-worn or rounded |  |
| stones; varying in size from about the diameter of the top | harbour. A stretch of water where vessels can anchor, |
| of a man's thumb to the size of a pinhead. cf sand, pebbles. | or secure to buoys or alongside wharves, etc, and |
|  | obtain protection from sea and swell. The protection |
| graving dock. Another name for a dry dock. To grave | may be afforded by natural features or by artificial |
| is an old term meaning to bum off the accretions | works. cf artificial harbour, island harbour. |
| on a ship's bottom before tarring, etc. |  |
|  | Harbour Board. See Port Authority. |
| grid. A systematic rectangular network of lines |  |
| superimposed on a chart or map and lettered and | harbour reach. See reach. |
| numbered in such a way that the position of any feature |  |
| can be defined with any required degree of precision. | hard. A strip of gravel, stone or concrete, built on a |
|  | beach across the foreshore to facilitate landing or |
| grid reference. The position of a feature given in | the hauling up of boats. |
| grid letters and numbers. |  |
|  | harmonic analysis. An analysis of tidal observations, |
| gridiron. A flat framework, usually baulks of timber | carried out to determine the harmonic constituents |
| placed parallel with each other, erected on the | of the tide, as a basis for tidal predictions. |
| foreshore below the high water line, and in such |  |
| a position that a vessel can be moved over it at high | harmonic constants. See constants (harmonic). |
| water and left dry and resting on it at low water. |  |
|  | harmonic constituent. See constituent (of the tide). |
| ground. A portion of the Earth's crust which may be |  |
| submerged or above water, eg spoil ground. | harmonic prediction. Prediction of the tide by |
| middle ground, swampy ground, landing ground. | combining harmonic constituents. |
| to ground. To run ashore or touch bottom. |  |
|  | haven. A harbour or place of refuge for vessels from |
| ground speed. The speed of a vessel over the ground. | the violence of wind and sea. In the strict sense it |
|  | should be accessible at all states of the tide and |
| ground swell. A long ocean swell; also this swell as it | conditions of weather. |
| reaches depths of less than half its length and |  |
| becomes shorter and steeper; ie influenced by the ground. | head. A comparatively high promontory with a steep |

- 12 -

GLOSSARY

| face. An unnamed head is usually described as a headland. | Highest Astronomical Tide (HAT). The highest |
| --- | --- |
| Also, the inner part of a bay, creek, etc, eg the | tidal level which can be predicted to occur under |
| head of the bay. | average meteorological conditions and under any |
| Also, the seaward end of a jetty, pier, etc. | combination of astronomical conditions. |
| head sea. A sea coming from the direction in which a | holding ground. The sea bottom of an anchorage is |
| ship is heading; the opposite to a following sea. | described as good or bad holding ground |
|  | according to its capacity for gripping the anchor |
| heading. Synonymous with ship's head. | and chain cable. In general, clay, mud and sand |
|  | are good; shingle, shell and rock are bad. |
| headland. See head. |  |
|  | hole. A small area of considerably greater depths than |
| headway. Motion in a forward direction. | those in the vicinity of less area than a deep. |
| Also, an obsolescent term synonymous with |  |
| vertical clearance (qv). | hollow sea. A very deep and steep sea. |
| heavy sea. A rough, high sea. | hopper. A barge used in harbours, etc, for conveying |
|  | sullage or spoil to a spoil ground (where it is |
| height. The vertical distance between the top of an | discharged through the bottom of the barge). |
| object and its base. |  |
| On Admiralty charts, the term 'height' (except | horizontal datum. A reference for specifying |
| in the case of drying heights) is used in the sense | positions on the Earth's surface. Each datum is |
| of elevation (qv) and unless otherwise stated, is | associated with a particular reference spheroid. |
| expressed, in metres or feet as appropriate, above | Positions referred to different datum’s can differ |
| the level of MHWS, MHHW, or, in places where | by several hundred metres. |
| there is no tide, above the level of the sea. cf |  |
| elevation, High Water Datum. | hydrography. The science and art of measuring the |
| Also, the height of a vessel is the height of the | oceans, seas, rivers and other waters, with their |
| highest point of a vessel's structure (eg radar | marginal land areas, inclusive of all fundamental |
| aerial, funnel, cranes, masthead) above her waterline. | elements which have to he known for the safe |
|  | navigation of such areas, and the publication of such |
| height of the tide. The vertical distance at any instant | information in a form suitable for the use of navigators. |
| between sea level and chart datum. |  |
| heights. A comparatively level plateau at the summit |  |
| of a precipitous mountain. | impounding basin. A basin in which water can be |
|  | held by means of a sluice, weir or gate. Used for |
| high focal plane buoy. A light-buoy on which the | keeping craft afloat when the tide drops below a |
| signal light is fitted particularly high above the | certain level, or to provide water for sluicing a |
| waterline. Used as fairway or landfall buoys. cf lanby. | channel which is very shallow and tends to collect silt. |
| High Water (HW). The highest level reached by the | index chart. An outline chart on which the limits and |
| tide in one complete cycle. | numbers of navigational charts, volumes of |
|  | Sailing Directions, etc, are shown. |
| higher high water. The higher of two successive |  |
| high waters where diurnal inequality is present. | Indian Spring Low Water. A level, originally |
|  | devised by Sir George Darwin for use in Indian |
| high water datum or datum for heights. The high | waters, determined from harmonic constants and |
| water plane to which elevations of land features | used as chart datum in some parts of the world. |
| are referred. On Admiralty charts this datum is |  |
| normally the level of MHWS when the tide is | inland waterways. The navigable systems of waters |
| predominantly semi-diurnal, or MHHW when | comprising canals. rivers, lakes, etc, within the land territory. |
| the tide is predominantly diurnal. |  |
|  | inlet. A small indentation in the coastline usually |
| high water full and change. The average interval at | tapering towards its head. cf creek. |
| any place between Moon's transit and the next |  |
| following high water on days of full or new Moon. | inner harbour. A harbour within a harbour, provided |
| Obsolete. | with quays, etc, at which vessels can berth. |
| high water stand. A prolonged period of negligible | inshore. Close to the shore. Used sometimes to indicate |
| vertical movement near high water, this being a | shoreward of a position in contrast to seaward of it. |
| regular feature of the tides in certain localities |  |
| while in other places stands are caused by | inshore traffic zone. A routeing measure comprising |
| meteorological conditions. | a designated area between the landward boundary |
|  | of a Traffic Separation Scheme and the adjacent |
| high water springs. See Mean High Water Springs. | coast, to be used in accordance with the provisions |

- 13 -

GLOSSARY

| of the International Regulations for Preventing | levelling system giving the plane to which |
| --- | --- |
| Collisions at Sea (1972). | elevations of features shown on maps are referred. |
|  | The most usual plane for land survey datums is |
| ironbound coast. A rock-bound coast without | an approximation to MSL. |
| anchorage or harbour. |  |
|  | landfall. The first sight or radar, indication of land at |
| island harbour. A harbour formed, or mainly | the end of a passage. |
| protected, by islands. |  |
|  | landfall buoy. A buoy with a tall superstructure, mark- |
| island shelf. The zone around an island and | ing the seaward end of the approach to a harbour |
| extending from the low water line to a depth at | or estuary. It may be situated out of sight of land. |
| which there is usually a marked increase in slope |  |
| towards oceanic depths. | landing. A place where boats may ground in safety; a |
|  | contraction of ‘landing place used by boats’. May |
| island slope (shoulder or talus). The declivity from | by artificial, consisting of a platform or steps, or |
| the outer edge of the island shelf into deeper water. | the equivalent in natural rock. |
| island terminal or structure. Deep-water structure | landing stage. A platform or pontoon connected with |
| not connected to the shore by a causeway or jetty. | the shore, for landing or embarking passengers or goods. |
| Submarine pipelines or overhead cableways are | Ships can berth alongside the larger landing stages. |
| used to transport cargoes between the island and |  |
| the shore. | landlocked. Sheltered by land from all or very nearly |
|  | all directions. |
| isobathic. Of equal depth. |  |
|  | landmark. A prominent artificial or natural feature |
| isogonic. Of equal magnetic variation (declination). | on land such as a tower or church, used as an aid |
|  | to navigation. |
|  | landslip. Sliding down of a mass of land on a cliff, |
| jetty. A structure generally of wood, masonry, | mountain or cutting. |
| concrete or iron, which projects usually at right- |  |
| angles from the coast or some other structure. | lanes; shipping. Much frequented shipping tracks |
| Vessels normally lie alongside parallel with the | crossing an ocean or sea. |
| main axis of the structure. |  |
| Also, term used in the USA and Canada for a | LASH (Light Aboard SHip). A cargo-carrying |
| training wall (qv). | system using specially built ships and lighters. |
|  | Cargoes are loaded into LASH lighters which are |
|  | towed to a LASH ship where the loaded lighters |
|  | are embarked. At their destination the LASH |
| key. See cay. | lighters are disembarked and towed away to their |
|  | unloading berths. Special berths or anchorage’s are |
| knot. The nautical unit of speed. ie 1 nautical mile (of | sometimes designated for LASH ships. |
| 1852 m) per hour. |  |
|  | launching. The sliding of a newly-built ship by the |
|  | action of its own weight into the water down a specially |
|  | prepared slipway--stern first or beam on(side launch). |
| lagoon. An enclosed area of salt or brackish water | launching cradle. The frame in which a ship |
| separated from the open sea by more or less, but | is supporting for launching. |
| not completely, effective obstacles, such as low |  |
| sandbanks. | lava. An igneous rock. It is formed by the cooling of |
| The name is most commonly used for the area of | magma (ie matter flowing from a volcano or |
| water enclosed by a barrier reef or atoll. | fissure in the ground) on the Earth's surface. |
| lanby (Large Automatic Navigational BuoY). A | layering. A method of emphasising on a chart |
| very large light-buoy, used as in alternative to a | differences of height or depth by the use of |
| light-vessel, to mark offshore positions important | varying tint. |
| to the Mariner. Lanbys vary in size up to a |  |
| displacement of 140 tonnes and a diameter or | lead (Pronounced 'leed'). The weight used in sounding |
| height of 12m. Radiobeacon, racons, or radar | with a leadline. |
| reflectors may be fitted to them. Full details of | (Pronounced ‘leed’). A narrow channel; especially |
| lanbys are given in Admiralty List of Lights. | thought drift ice, or in rock or coral- studded waters. |
| land levelling system. A network of benchmarks, | leading lights. Lights at different elevations so situated |
| etc, connected by levelling to a common datum. | as to define a leading line when brought into transit. |
| land survey datum. The point of origin of a land | leading line. A suitable line for a vessel to follow |

- 14 -

GLOSSARY

| through a given area of water as defined by | linkspan. A pontoon carrying a ramp placed between |
| --- | --- |
| leading marks located on a farther part of the line. | a ro-ro vessel and a wharf to enable vehicles to |
|  | embark or disembark from the wharf. |
| leading mark. One of a set of two or more navigation |  |
| marks that define a leading line. | liquid natural gas (LNG). Gas, predominantly |
|  | rnethane, from oilfield sources. Held in liquid |
| ledge. A flat-topped ridge or narrow flat of rocks, | state at atmospheric pressure at a temperature of |
| extending from an island or coast. cf shelf. | about - 162( C for transport and storage. |
| lee shore. The shore towards which the wind is blowing. | liquid petroleum gas (LPG). Light hydrocarbon |
|  | material, gaseous at normal temperatures and |
| lee side. The side of the ship or object which is away | pressures. By-product of petroleum refining and |
| from the wind and therefore sheltered. | oil production. Held at liquid state under pressure |
|  | for transport and storage. Liquid petroleum gases |
| lee tide. A tidal stream running in the same direction | include propane and butane. |
| as the wind is blowing. |  |
|  | local knowledge. The use of a pilot, local seafarer |
| levee. Large river embankment built to prevent flooding. | competent to act as a pilot, or past experience. |
| A naturally raised river bank built up by flood deposit. |  |
| Oceanographically, an embankment bordering a | local magnetic anomaly. A magnetic anomaly |
| canyon; valley or channel. | (qv) covering a small area. See 4.59. |
| light-beacon. A beacon from which a light is exhibited. | lock. An enclosure at the entrance to a tidal basin, or |
| cf buoyant beacon. | canal, with caissons or gates at each end by means |
|  | of which ships are passed from one water level to |
| light-buoy. A buoy carrying a structure from which | another without materially altering the higher level. |
| is exhibited a light, which may have any of the | to lock a vessel. To pass a vessel through a lock. |
| characteristics of a light exhibited from a |  |
| lighthouse other than sectors. cf lanby, light- float. | loom. The vague appearance of land, vessels, etc, when |
|  | first sighted in darkness, or through fog, smoke or haze. |
| light-float. An unmanned fully-automated vessel, comparable | Also, the diffused glow of a light seen when the light |
| in size to a light-vessel, or a boat- shaped unmanned float | itself is below the horizon or obscured by an obstacle. |
| carrying a light and sometimes sounding a fog |  |
| signal. The former is a major navigational light; the | Low Water (LW). The lowest level reached by the tide |
| latter may sometimes be used instead of a light-buoy | in one complete cycle. |
| where there are strong tidal streams or currents. |  |
|  | low water neaps. See Mean Low Water Neaps. |
| lightening area. See transhipment area. |  |
|  | lower low water. The lower of two successive LWs |
| lighter. A general name for a broad flat-bottomed | where diurnal inequality is present. |
| craft used for transporting cargo and other goods |  |
| between vessels and the shore. Lighters may be | Lowest Astronomical Tide (LAT). The lowest tidal |
| self-propelled but are usually towed. There are also | level which can be, predicted to occur under |
| lighters rigged for special purposes, cf. dumb | average meteorological conditions and under any |
| lighter, mooring lighter, crane lighter. | combination of astronomical conditions. See 4.1. |
| lighthouse. A distinctive structure from which a light | loxodrome. See rhumb line. |
| or lights are exhibited as an aid to navigation. |  |
|  | lunitidal interval. The time interval between the |
| lighthouse buoy. A name formerly used for a lanby. | transit of the Moon and the next following high |
|  | or low water; hence high water lunitidal interval, |
| lights. A comprehensive term including all | low water lunitidal interval, mean high water |
| illuminated aids to navigation, other than those | interval and mean low water interval. |
| exhibited from floating structures. |  |
| lights in line. Two or more lights so situated that |  |
| when in transit they define the limit of an area, | madrepore. A common form of coral; |
| the alignment of a cable, or an alignment for use | probably the most wide-spread of reef-building corals. |
| of anchoring, etc. Unlike leading lights they do |  |
| not mark a direction to be followed. | magnetic anomaly. An effect, permanently |
|  | superimposed on the Earth's normal magnetic |
| light-vessel (sometimes known as light-ship). A | field and characterised by abnormal values of the |
| manned vessel, secured in a designated locality | elements of compass variation, dip, and |
| carrying a light of high luminous intensity and | geomagnetic force. See abnormal magnetic |
| usually sounding a fog signal to assist navigation. | variation, and 4.59. |

- 15 -

GLOSSARY

| magnetic variation. the angle which the magnetic | fortnight) when the range of the tide is least. |
| --- | --- |
| meridian makes with the true meridian. Called | Mean Low Water Neaps (MLWN). The height |
| 'magnetic declination' by physicists. | of mean low water neaps is the average height |
|  | obtained from two successive low waters during |
| main ship channel. The channel having the greatest | the same periods. |
| depth and easiest for navigation. |  |
|  | Mean Higher High Water (MHHW). The height of |
| mainland. A term applied to a major portion of land | the mean of the higher of the two daily high |
| in relation to off-lying islands. | waters over a long period of time. When only one |
|  | high water occurs on a day this is taken as the |
| make the land. Make a landfall (qv). To sight and | higher high water. |
| approach the land after being out of sight of land at sea. | Used where the tide is predominantly diurnal. |
| makes. Run in a certain direction, eg 'the stream is | Mean Higher Low Water (MHLW). The height of |
| making to the N means the stream is running northward. | the mean of the higher of the two daily low waters |
|  | over a long period of time. |
| manganese. A black mineral used in glass-making, |  |
| etc, found as a bottom sediment. | Mean Lower High Water (MLHW). The height of |
|  | the mean of the lower of the two daily high waters |
| mangrove swamp. A flat low-lying area of mud and | over a long period of time. |
| silt, lying between the high and low water lines of spring |  |
| tide covered by the stilt-like roots of the mangrove | Mean Lower Low Water (MLLW). The height of |
| and associated vegetation. A feature of tropical waters. | the mean of the lower of the two daily low waters |
|  | over a long period of time. When only one low water |
| marina. An area provided with berthing and shore | occurs on a day this is taken as the lower low water. |
| facilities for yachts. |  |
|  | Mean Sea Level (MSL). The average level of the sea |
| marine farm. A structure, on the surface or | surface over a long period, preferably 18.6 years, |
| submerged, in which fish are reared. They may | or the average level which would exist in the |
| obstruct navigation and are sometimes marked by | absence of tides. |
| buoys (special) which may be lighted. They are |  |
| not necessarily confined to inshore locations and | Mean Tide Level. The mean of the heights of |
| may be moved. See also fish haven, fish | MHWS, MHWN, MLWS and MLWN. |
| aggregating device. |  |
|  | measured distance. The shortest distance between |
| marine railway. A term sometimes applied to a patent | two or more sets of parallel transits set up on |
| slip, more particularly in Canada and the USA. | shore to determine the speed of a vessel. The |
|  | length and direction of the distance are charted. |
| mark. A fixed feature on land or rnoored at sea, which can |  |
| be identified on the chart and used to fix a ship's position. | median valley. The axial depression of the mid- |
|  | oceanic ridge system. Also called a Rift or Rift Valley. |
| marl. A crumbling earthy deposit, particularly one of |  |
| clay mixed with sand, decomposed shells, etc. A | mid-channel controlling depth. See controlling depth. |
| layer of marl is sometimes quite compact. |  |
|  | mile. |
| Mean High Water (MHW). The average of all high | The International nautical mile is 1852 m. |
| water heights as defined above, for a year. cf High | The unit used by the United Kingdom until |
| Water. Hence Mean Low Water. | 1970 was the British Standard nautical mile of |
|  | 6080 ft or 1853.18 m. |
| Mean High Water Springs (MHWS). The height of | The sea mile is the length of 1 minute of arc, 6080 ft or 1853.18 m. |
| mean high water springs is the average, | measured along the meridian, in the latitude of |
| throughout a year when the average maximum | the position; its length varies both with the |
| declination of the Moon is 23.5(, of the heights of | latitude and with the dimensions of the spheroid in use. |
| two successive high waters during those periods | The statute mile is the unit of distance of 1760 |
| of 24 hours (approximately once a fortnight) when | yards or 5280 ft (1609.3 m). |
| the range of the tide is greatest. | The geographical mile is the length of 1 minute |
| Mean Low Water Springs (MLWS). The height of mean | of arc, measured along the equator; its value is |
| low water springs is the average height obtained by | determined by the dimensions of the spheroid in use. |
| two successive low waters during the same periods. |  |
|  | moat. An annular depression that may not be |
| Mean High Water Neaps (MHWN). The height of | continuous, located at the base of many |
| mean high water neaps is the average, throughout | seamounts, islands and other isolated elevations. |
| a year when the average declination of the Moon |  |
| is 23.5(, of the heights of two successive high waters | mole. A breakwater alongside the sheltered side of |
| during those periods (approximately once a | which vessels can lie. |

- 16 -

GLOSSARY

| Also, a concrete or stone structure, within an | neap tide. A tide of relatively small range occurring |
| --- | --- |
| artificial harbour, at right-angles to the coast or | near the time of the Moon's first and last quarters. |
| the structure from which it extends, alongside |  |
| which vessels can lie. | neck (of land). A narrow isthmus or promontory. |
| monobuoy. Term formerly used for a Single Point | no bottom sounding. A depth obtained at which the |
| Mooring (qv). | lead or sounder has not reached the bottom. |
| moor. To secure a vessel, craft, or boat, or other | nodal point. The point of minimum tidal range in an |
| floating object by ropes, chains, etc, to the shore | amphidromic system. An amphidromic point. |
| or to anchors. |  |
| Also, to ride with both anchors down laid at | noise range. An area set aside for measuring the |
| some distance apart, and the ship lying midway | underwater noise generated by a ship. Acoustic |
| between them. | sensing instruments are installed on the seabed |
|  | with cables leading to a control position ashore. |
| mooring buoy. A buoy of special construction which | The area is often marked by buoys. |
| carries the ring of the moorings to which a vessel |  |
| secures. | nun buoy. A buoy in the shape of two cones, base to |
|  | base, and moored from one point so that the other is |
| mooring lighter. A lighter especially fitted for | more or less upright. Used in the USA for a buoy |
| handling, laying and weighing moorings. | with a conical or truncated conical-shaped top. |
| mooring tower. A metal tower standing on the |  |
| seabed to which ships can moor. See 3.112. |  |
|  | observation spot. A position at which precise |
| moorings. Gear usually consisting of anchors or | astronomical observations for latitude and |
| clumps, cables, and a buoy to which a ship can | longitude have been obtained. |
| secure. |  |
| The moorings. A place in which a vessel may be | obstruction. A danger to navigation, the exact nature of |
| secured. | which is not specified or has not been determined. |
| Morse code light. A light in which flashes of | ocean. The great body of water surrounding the land |
| different duration are grouped in such a manner | masses of the globe, or more specifically one of |
| as to reproduce a Morse code character. | the main areas into which the body of water has |
|  | been divided by geographers. Any of the major |
| mud. A sediment having predominance of grains with | expanses of salt water on the surface of the globe. |
| diameters less than 0.06 mm. |  |
| The term is a general term referring to mixtures | ocean swell. A swell encountered in the open ocean |
| of sediments in water and applies to both clays and silts. | in great depths. |
| The geological name is ‘lutite’. |  |
|  | oceanography. The study of the oceans especially of |
|  | the physical features of the sea water and seabed |
|  | and of marine flora and fauna. |
| narrows. A contracted part of a channel or river. |  |
|  | offing. The part of the sea distant but visible from |
| natural scale. The ratio between a measurement on | the shore or from an anchorage. |
| a chart or map and the actual distance on the |  |
| surface of the Earth which that measurement | offshore. To seaward of, but not close to, the shore, |
| represents. It is expressed as a ratio with a | as in ‘offshore fishing’. |
| numerator of one, eg 1/25 000 or 1:25 000. | Also, from the shore, as in ‘offshore wind ‘. |
|  | Oceanographically, the region extending |
| nautical mile. See mile.. | seaward from the low water line of Mean Spring |
|  | tides to the continental or island slope |
| nautical twilight. The period between the end of |  |
| civil twilight (qv) and the time when the Sun's | offshore installation. Any structure such as a drilling rig, |
| centre is 12( below the horizon in the evening, | production platform, wellhead. SPM, etc, set up offshore. |
| and the period between the time when the Sun's |  |
| centre is 12( below the horizon and the beginning | ogival buoy. A buoy with an arch-shaped vertical |
| of civil twilight in the morning. cf astronomical twilight. | cross-section above the waterline. |
| navigable. Affording passage for ships or boats. | ooze. Very soft mud, slime; especially on the bed of a |
| Also, capable of being navigated. | river or estuary. |
|  | Oceanographically, fine-grained soft deposits of |
| navigation. The art of determining a ship's position | the deep-sea. formed from the shells and skeletons |
| and of taking her in safety from one place to another. | of planktonic animals and plants. See diatom, |
|  | globigerina ooze, pteropod ooze, radiolarian ooze. |

- 17 -

GLOSSARY

| open. Two marks are said to be open when they are | parallel of latitude. Small circle on the Earth's |
| --- | --- |
| exactly in transit. | surface parallel with the equator. |
| to open. To being into view, eg 'to open the land |  |
| eastward of a cape'. | pass. A comparatively narrow channel often with high |
|  | ground or cliff on either side, and leading to a |
| open basin. See basin. | harbour or river. |
|  | Also, a passage through or over a mountain range. |
| open coast. An unsheltered, harbourless coast open |  |
| to the weather. | passage. A navigable channel, especially one through |
|  | reefs or islands. |
| open harbour. Unsheltered harbour, exposed to the sea. | Also, a sea journey between defined points; one |
|  | or more passages may constitute a voyage. |
| open roadstead. An anchorage unprotected from the weather. |  |
|  | patch. A portion of water or land which has distinctive |
| open water. Waters where in all circumstances a ship | characteristics, eg drying patch (of land, ground, sand, etc), shoal |
| has complete freedom of manoeuvre. cf restricted waters. | patch (of water), and discoloured patch (of water, rock, etc). |
|  | In British hydrographic usage 'patch' may be |
| opening. A general term to indicate a gap or passage. | used as an alternative to 'shoal', both being |
| eg an opening in a reef. | limited to a detached area which constitutes a danger. |
| Ordnance Datum. The datum, or series of daturns, | patent slip. A cradle supported on carriages running |
| established on the mainland and adjacent islands | on rails on the shore from about the level of High |
| of the British Isles as the point of origin for the | Water Springs to the level of Low Water Springs. |
| land levelling system. | The cradle can be run into the water to receive a |
| Ordnance Datum (Newlyn). This point of origin | small or medium-sized vessel and then hauled up |
| corresponds to the average value of MSL at | until the vessel is clear of the water for bottom |
| Newlyn during the years 1915 to 1921. | cleaning and repair. |
| Ordnance Datum (Liverpool). The point of origin |  |
| of an early land levelling system, now obsolete. | pay off. A ship is said to pay off when her head falls |
|  | away from the wind. |
| Ordnance Survey. The Government survey of Great Britain; |  |
| the responsible authority for Ordnance Survey maps. | pebbles. Water-rounded material of from 4 to 64 mm |
|  | in size, ie from the diameter of the top of a man’s |
| origin, point of. A fixed point in a co-ordinate system | thumb to the diameter of his clenched fist when |
| or grid to which all measurements are referred. | viewed sideways. |
| orthodrome. A great circle track. | pens. A series of parallel jetties for berthing small craft. |
| orthomorphic or conformal projection. Charts and | perch. A small beacon, often an untrimmed sapling, |
| maps on this type of projection have the property | used to mark channels through mud flats or |
| that small areas on the Earth's surface retain their | sandbanks; may or may not carry a topmark; often |
| shape on the chart or map, the meridians and | of an impermanent nature. |
| parallels being at right-angles to one another and |  |
| the scale at any one point being the same in all | perigee. The point in the orbit of the Moon which is |
| directions. Mercator's and stereographic | nearest to the Earth. When the Moon is in perigee |
| projections are examples used in hydrography. | the tidal range is increased. cf apogee. |
| outer harbour. A sheltered area, even in bad weather, | perigee tide. A spring tide, greater than average, |
| outside the harbour proper, the inner harbour and the docks. | occurring when the Moon is in perigee. |
| outfall. A narrow outlet of a river into the sea or a | perihelion. The point in the orbit of a planet which |
| lake, as opposed to the opening out at a mouth. | is nearest to the Sun. cf aphelion. |
| Also, the mouth of a sewer or other pipe |  |
| discharging into the sea. | phase (of the Moon). The appearance at a given time |
|  | of the illuminated surface of the Moon. |
| outfall buoy. Buoy marking the position where a |  |
| sewer or other pipe discharges into the sea. | phosphorescence. The name formerly applied to |
|  | bioluminescence. See 4.46. |
| overfalls. Also known as tide-rips. Turbulence |  |
| associated with the flow of strong tidal streams | phytoplankton. The microscopic floating plant life of |
| over abrupt changes in depth, or with the meeting | the oceans; the basic food source for most marine life. |
| of tidal streams flowing from different directions. |  |
|  | pier. A structure, usually of wood, masonry, concrete |
| overtide. Harmonic constituents of short period, | or iron, extending approximately at right-angles |
| associated with shallow water effect. | from the coast into the sea. The head, alongside |

- 18 -

GLOSSARY

| which vessels can lie with their fore-and-aft line | plankton. Collective name for the microscopic |
| --- | --- |
| at right-angles to the main structure, is frequently | floating and drifting plant and animal life found |
| wider than the body of the pier. | throughout the world's oceans. A distinction can |
| Some piers, however, were built solely as promenades. | be made between neretic(coastal) and oceanic |
| Also used for the structure joining a wharf to | (deep-water) plankton. See phytoplankton, zooplankton. |
| the land. |  |
| piers. Supports for the spans of a bridge. | plateau. Extensive elevated region with level (or |
|  | nearly level) surface. cf tableland. |
| pierhead. The seaward end of a pier, frequently set | Oceanographically, a flat or nearly flat area of |
| at right-angles to the pier in the form of a T or L | considerable extent which is relatively shallow, |
|  | dropping off abruptly on one or more sides. |
| pile. A heavy baulk of timber or a column of |  |
| reinforced concrete, steel or other material, driven | point. A sharp and usually comparatively low piece of |
| vertically into the bed of the sea or of a river. It | land jutting out from the coast or forming a |
| may be used to mark a channel or to serve as part | turning-point in the coastline. |
| support for construction .York such as a pier, |  |
| wharf or jetty. | point of origin. See origin; point of. |
| pile beacon. A beacon formed of one or more piles. | polyzoa. Minute creatures of the sea, which always |
|  | live in colonies, some of which are small and |
| pile fender. A pile driven loosely into the seabed in | branching and others large and with strong lime |
| front of a wharf, etc, to absorb the shock of a | skeletons which give them the appearance of corals. |
| vessel going alongside. |  |
|  | pontoon. A broad, flat-bottomed floating structure |
| pile lighthouse. A lighthouse erected on a pile foundation. | (often of heavy timber baulks) rectangular in |
|  | shape, used for many purposes in a port, as a ferry |
| pile moorings. Permanent moorings to which a vessel | landing place, a pierhead, or alongside a vessel to |
| is secured fore and aft between piles. | assist in loading or discharging. |
| pillar buoy. A buoy of which the part of the body above | port. A commercial harbour or the commercial part |
| the waterline is a pillar, or of which the greater | of a harbour in which are situated the quays, wharves, |
| part of the superstructure is a pillar or a lattice tower. | facilities for working cargo, warehouses, docks, |
|  | repair shops, etc. The word also embraces, |
| pilot. Person qualified to take charge of ships | geographically, the city or borough which |
| entering, leaving, and moving within certain | serves shipping interests. See also ports named |
| navigable waters. | after location, eg canal port, seaport, river port, etc. |
| The term Admiralty Pilot is commonly used to |  |
| designate a volume of Sailing Directions | Port Authority. Persons or corporation, owners of, or |
| published by the Hydrographic Department. | entrusted with or invested with the power of managing |
|  | a port. May be called a Harbour Board, Port Trust, |
| pilotage. The conducting of a vessel ,within restricted waters. | Port Commission, Harbour Commission, Marine Department, etc. |
| Also, the fee for the services of a pilot. |  |
|  | port radio station. See radio station. |
| pilotage waters. Those areas covered by a regular |  |
| pilotage service. | position line. A line on a chart, representing a line |
|  | on the Earth's surface, on which a ship's position |
| pinnacle (rock). A rock, which may or may not be | can be said to lie, such as might be obtained from |
| dangerous to navigation, rising sheer from the | a single bearing, the observations of one heavenly |
| bottom of the sea, and of which no warning is | body, or an arc of a range circle. |
| given by sounding. |  |
| Oceanographically, any high pillar of rock or | pound (or pond). Small body of still water in the form |
| coral, shaped like a tower or spire, standing alone | of a camber or small basin in a dockyard, used for |
| or cresting a summit. | the storage of boats or other gear afloat. eg boat |
|  | pound, timber pound. |
| pitch. Angular motion of a ship in the fore-and-aft |  |
| plane. cf roll, scend. | pratique. Licence to hold intercourse with the shore |
|  | granted to a vessel after quarantine or on showing |
| pitching. The facing of the sloping sides of a | a clean bill of health. |
| breakwater, which may be paved, or consist of |  |
| stones, tetrapods or rubble. | precautionary area. A routeing measure comprising |
|  | an area within defined limits where ships must |
| pivoted beacon or tower. See buoyant beacon. | navigate with particular caution and within which |
|  | the direction of traffic flow may be recommended. |
| plain. Oceanographically, a flat gently sloping or |  |
| nearly level region of the sea floor. | production platform. A permanently-manned |

- 19 -

GLOSSARY

| offshore structure sited on an oil or gasfield. See3-102. | distinguishable and outstanding on a radar screen |
| --- | --- |
|  | on most bearings from seaward. |
| project depth. The design dredging depth of a channel. |  |
|  | radar assistance. The communicating to a vessel of navigational |
| projection. A geometrical representation on a plane | information determined by a shore radar, when requested. |
| of a part of the Earth's surface. |  |
|  | radio. Wireless Telegraphy (WT) and Telephony |
| prominent object. An object which is easily | (RT). The internationally agreed prefix to all |
| identifiable, but does not justify being classified | appliance operated by wireless or radio. |
| as conspicuous. |  |
|  | radio bearing. The bearing of a radio transmission. |
| province. Oceanographically, a region identifiable by |  |
| a group of similar physiographic features whose | radio calling-in point. See reporting point. |
| characteristics are markedly in contrast with |  |
| surrounding areas. | radio fog signal. Special transmissions provided by a |
|  | radiobeacon as an aid to navigation during periods |
| pteropod ooze. Limy deposits, formed from the dead | of fog and low visibility. |
| bodies of small swimming snails or sea butterflies, |  |
| commonest near the equator. Found in shallower | radio lighthouse. See rotating pattern radiobeacon. |
| water than globigerina ooze, and especially near |  |
| coral islands and on submerged elevations far from | radio station. |
| land. | coast radio stations are normally open for'public |
|  | correspondence' through which ships can pass |
| pumice. A light, porous or cellular type of lava, | messages for onward transmission. These stations |
| occasionally to be found floating on the sea | are usually connected to the national telephone |
| surface. | system. See Admiralty List of Radio Signals Vol 1. |
|  | port radio stations normally operate in the |
|  | VHF band through which messages can be |
|  | passed to Port Authorities. These messages |
| quadrature. A term applied principally to the Sun | are restricted to the movement, berthing and |
| and Moon when their longitudes differ by 90( (ie | safety of ships, and in emergency to the safety |
| halfway between full and new Moon). | of persons. Port radio stations may be associated |
|  | with radar surveillance and traffic control centres |
| quarantine. Isolation imposed on an infected vessel. | in large ports. See Admiralty List of Radio Signals Vol 6. |
| All vessels are considered to be in quarantine until |  |
| granted pratique (qv). | radiobeacon. A radio transmitting station on shore |
|  | or at an offshore mark, not necessarily manned, |
| quarantine anchorage. See anchorage. | or light-buoy, of whose transmissions a ship may |
|  | take bearings. See aero, circular, rotating |
| quartz. Crystalline silica. Usually colourless and | pattern and directional radiobeacons. |
| transparent, but varies considerably in opaqueness |  |
| and colour, the most common solid mineral. | radiolaria. Forms of foraminifera having skeletons of silica. |
| quay. A solid structure usually of stone, masonry or | radiolarian ooze. A siliceous deep-sea ooze formed |
| concrete (as distinguished from a pile structure) | of the skeletons of radiolaria. |
| alongside which vessels may lie to work cargoes. It |  |
| usually runs along or nearly along the line of the | radome. A dome, usually of glass reinforced plastic, |
| shore of the inner part of a port system. | housing radar aerial. On shore installations these |
|  | domes are often conspicuous or prominent. Term |
| quayage. Comprehensive term embracing all the | is also used for domes or pods housing similar |
| structures in a port alongside which vessels can lie. | equipment in ships and on aircraft. |
| Also, the charge made for berthing on a quay. |  |
| cf wharfage. | raise the land. To sight the land by approaching to |
|  | the point where it appears above the horizon, |
| quoin. A wedge; sometimes used to describe the shape | Similarly, to raise a light or another ship.. |
| of an island or hill. |  |
|  | raised beach. An old beach, raised appreciably |
|  | beyond the inshore limit of wave action, by earth |
|  | movements which have caused the sea to recede. |
| race. Fast-running water, frequently tidal, caused by |  |
| passage through a constricted channel, over | ramp. A sloping road or pathway from the sea or river |
| shallows, or in the vicinity of headlands, etc. | bed to above high water, in place of steps, eg the |
| Eddies are often associated with races. | roadway from a beach to the top of a seawall. |
|  | Also, an inclined platform between the shore |
| radar conspicuous object. Any object that is readily | and a vessel, with one end adjustable for height, |

- 20 -

GLOSSARY

| to enable vehicles to drive on and off the vessel. | refuge harbour. An artificial harbour built on an |
| --- | --- |
|  | exposed coast for vessels forced to take shelter |
| range. Term used in the USA and Canada for transit (qv). | from the weather. |
| range of the tide. The differences in level between | refuge hut. A hut containing emergency rations and |
| successive high and low waters or vice versa. | clothing, maintained on some barren and isolated |
|  | coasts for the use of shipwrecked persons. |
| rate (of tidal streams and currents). The velocity, |  |
| usually expressed in knots. | reporting point. A position in the approaches to |
|  | certain ports where traffic is controlled by a vessel |
| ratio of ranges. A factor, found on or deduced from | traffic service at which ships entering or leaving |
| a co-tidal chart, whereby the range of the tide | report their progress as directed in Admiralty List |
| offshore can be calculated. | of Radio Signals Vol 6. Also known by certain |
|  | authorities as a Calling-in Point or Way Point. |
| reach. A comparatively straight part of a river or |  |
| channel, between two bends. | restricted waters. Areas which, for navigational |
| harbour reach. Reach of a winding river or of | reasons such as the presence of sandbanks or other |
| an estuary which leads directly to the harbour. | dangers, confine the movements of shipping to |
|  | narrow limits, cf open waters. |
| recommended direction of traffic flow. A traffic |  |
| flow pattern indicating a recommended | retroreflector. A surface or device from which most |
| directional movement of traffic where it is | of the reflection of light can occur as retroreflection. |
| impracticable or unnecessary to adopt an |  |
| established direction of traffic flow. | rhumb line or loxodrome. Any line on the Earth's |
|  | surface which cuts all meridians at the same angle, |
| recommended route. A route of undefined width, | ie a line of constant bearing. |
| for the convenience of ships in transit, which is |  |
| often marked by centreline buoys. | ride to the anchor. To lie at anchor with freedom to |
|  | yaw and swing. |
| recommended track. A track shown on a chart, |  |
| which all or certain vessels are recommended to follow. | ridge. Oceanographically, it has the three following means: |
| The best known track through an imperfectly | A long narrow elevation with steep sides; |
| charted area or through an intricate channel, or | A long narrow elevation often separating ocean |
| the best track for deep-draught vessels in shallow | basins. cf rise. |
| waters, or the route authorised for vessels of a | The major oceanic mountain system of global extent. |
| certain draught, are among the recommended |  |
| tracks shown on charts. | rift valley. See median valley. |
| They are shown on charts by pecked lines, with |  |
| arrows where necessary to show the direction to | ripple marks. Small ridges caused by wave action on |
| be followed, but where the tracks are defined by | sandy or silty shores, and on the seabed. cf |
| leading marks, whether charted or not, they are | backwash marks, beach cusps. |
| shown in firm lines. |  |
| In a routeing system, it means a route which | rips: tide. See overfalls. |
| has been specially examined to ensure so far as |  |
| possible that it is free of dangers and along which | rise. Oceanographically, a broad elevation that rises |
| ships are advised to navigate. | gently and generally smoothly from the sea floor. |
|  | A synonym for the last-listed definition of ridge. |
| rectilinear stream. A tidal stream which runs |  |
| alternatively in approximately opposite directions, | rising tide. The period between low water and high water. |
| with a period of slack water in between. cf rotary streams. |  |
|  | river basin. A region which contributes to the supply |
| reduction of soundings. The adjustment of | of water to a river or rivers. The catchment area of a river. |
| soundings to the selected chart datum by correction |  |
| for the height of the tide, which gives charted depths. | river port. A port that lies on the banks of a river. cf |
|  | canal port, seaport, estuary port. |
| reef. An area of rocks or coral, detached or not, the |  |
| depth over which constitutes a danger to surface | roads. An open anchorage which may, or may not, be |
| navigation. Also, sometimes used for a low rocky | protected by shoals, reefs, etc. Affording less |
| or coral area, some of which is above water. | protection than a harbour. Sometimes found |
| Oceanographically, rocks lying at or near the sea surface. | outside harbours. |
| reef island. See coral island. | roadstead. Alternative name for roads. |
| reflector. A device fitted to buoys and beacons to | rock. An extensive geological term, but limited in |
| reflect rays of light. | hydrography to hard, solid masses of the Earth’s |

- 21 -

GLOSSARY

| surface rising from the bottom of the sea, either | saddle. A low part, resembling in shape a saddle, in a |
| --- | --- |
| completely submerged or projecting permanently, | ridge or between contiguous seamounts. |
| or at times, above water. |  |
|  | saddlehill. A hill with two summits separated by a |
| roll. The angular motion of a ship in the athwartship | depression, appearing from some directions like a saddle. |
| plane. cf pitch. |  |
|  | safe overhead clearance. The height above the datum |
| roll-on, roll-off (Ro-Ro). Term applied to ships, | of heights at which the highest point of a ship can pass |
| wharves, berths and terminals, where vehicles can | under an overhead power cable without risk of |
| embark or disembark by driving on or off a vessel. | electrical discharge from the cable to the ship. See 3.126. |
| root. The landward end of the structure of a jetty, pier, etc. | SALS. Single Anchor Leg Storage system. See 3.1 1 1. |
| rotary streams. Tidal streams, the direction of which | saltings. Lands in proximity to salt water, which are |
| gradually turn either clockwise or anti-clockwise | covered at times by the tide. |
| through 360( in one tidal cycle. |  |
|  | sand. A sediment consisting of an accumulation of |
| rotating pattern radiobeacon or radio lighthouse. | particles which range in size from a pin's head to |
| A radiobeacon which enables a ship to determine | a fine grain. The most common sediment on the |
| her true bearing in relation to it, without the use | continental shelves are of two principal types: |
| of direction-finding equipment, See Admiralty | Terrigenous sand which is made up from the |
| List of Radio Signals Vol 2. | breaking up of rocks on land by weathering, |
|  | the small fragments being carried out to sea |
| roundabout. A routeing measure comprising a | by streams. (The most common constituent |
| separation point or circular separation zone and a | of terrigenous sand is quartz, but many other |
| circular traffic lane within defined limits. Traffic | minerals are also included.) |
| within the roundabout is separated by moving in | Calcarenite sand made up from shells or shell |
| a counterclockwise direction around the | fragments, foraminifera, coral debris and |
| separation point or zone. | other organisms that contain calcium carbonate. |
|  | Also, a shoal area of sand, sometimes connected |
| routeing system. Any system of one or more routes | with the shore or detached. Some sands partly dry |
| or routeing measures aimed at reducing the risk of | and some are always submerged. cf. shifting sand. |
| casualties; it includes traffic separation schemes, |  |
| two-way routes, recommended tracks, areas to be | SBM. Single Point Buoy Mooring. See 3.104. |
| avoided, inshore traffic zones, roundabouts, |  |
| precautionary areas and deep-water routes. | scale (on a chart or map). A graduated line used to |
|  | measure or plot distances. On large scale |
| rubble. Waste fragments of stone, brick, concrete, etc, | Admiralty charts the following scales are usually |
| or pieces of undressed stone, used as a foundation | provided: Latitude and Distance, Feet, and |
| or for protecting the sides of breakwaters and | Metres; and on ungraduated plans, Longitude. cf |
| seawalls. See pitching. | natural scale. |
| run. The distance a ship has travelled through the water. | scend or send. |
| the run of the coast. The trend of the coast. | of a ship. A ship is said to scend heavily when |
| to run down a coast. To sail parallel with it. | her bow or stern pitches with great force into the |
| to run before the wind. To steer a course downwind. | trough of the sea. |
|  | of waves. The vertical movement of waves or |
| runnel. A depression in a beach usually roughly | swell alongside a wharf, jetty, cliff, rocks, etc. |
| parallel with the waterline for much of its course; |  |
| frequently associated with rills debouching over | scoriae. Cellular lava or clinker-like fragments of it. |
| the beach, but also occurring when there is a |  |
| sudden change in the gradient, eg as caused by | scour. The clearing of a channel by the action of water. |
| breakers during the stand of the tide near high or | Also the local deepening close to an islet, rock |
| low water. | or obstruction due to the clearing action of the |
|  | tidal streams or currents. |
| running survey. A survey in which the greater part |  |
| of the work is done from the ship sounding and | scouring basin. A backwater or basin by the side of a |
| moving along the coast, fixed by dead reckoning, | channel or small harbour from which water can |
| astronomical observations, or other means, and | be released quickly near low water for the purpose |
| observing angles, bearings and distances to plot | of scouring the channel or harbour. |
| the general configuration of the land and offshore |  |
| details. | sea. The expanse of salt water which covers most of |
| Similarly, a running survey of a river by boats. | the Earth's surface. |
|  | Also, a sub-division of the above, next in size |
|  | to an ocean, partly and sometimes wholly enclosed |

- 22 -

GLOSSARY

| by land, but usually with access to open water. | separation zone or separation line. A zone or line |
| --- | --- |
| Also, the waves raised by the wind blowing in | separating the traffic lands in which ships are |
| the immediate neighbourhood of the place of | proceeding in opposite or nearly opposite directions; |
| observation at the time of observation. See 4.30. | or separating a traffic lane from the adjacent sea area; |
|  | or separating traffic lanes designated for particular |
| sea mile. See mile. | classes of ships proceeding in the same direction. |
| sea reach. The most seaward reach of a river or estuary. | set (of the stream). The direction in which a tidal |
|  | stream or current is flowing. |
| sea room. Space clear of the shore which offers no |  |
| danger to navigation and affords freedom of manoeuvre. | shackle of cable. The length of a continuous portion |
|  | of chain cable between two joining shackles. In |
| sea-way. The open water outside the confines of a harbour. | British ship the standard length of a shackle of |
| Also, a rough sea caused by wind, tide or both. | cable is 15 fathoms (27,432 m). |
| seaboard. Alternative name for coastal region. | shallow. A shoal area in a river, or extending across a |
|  | river, where the depths are less than those |
| seachannel. A long narrow U- or V-shaped shallow depression of | upstream or downstream of it. |
| the sea floor, usually occurring on a gently sloping fan or plain. | to shoal. To become more shallow. |
| seaknoll. An isolated submarine hill or elevation less | shallow water effect (tidal). A general term descriptive of the |
| prominent than a searnount. | distortion of the tidal curve from that of a pure cosine curve, most |
|  | marked in areas where there is a large amount of shallow water. |
| seamark. A daymark erected with the express |  |
| purpose of being visible from a distance to seaward. | sheer. A ship is said to take a sheer if, usually due to |
|  | some external influence, her bows unexpectedly |
| seamount. A large isolated underwater elevation | deviate from her course. |
| characteristically of conical form. |  |
|  | shelf. See ledge, continental shelf, island shelf. |
| seamount chain. Several seamounts in a line. |  |
|  | shelf edge or shelf break. A narrow zone at the outer margin |
| seamount group. Three or more seamounts not in a | of a shelf along which there is a marked increase of slope. |
| line and with bases separated by a relatively flat sea floor. |  |
|  | shell. A hard outer case, conch, crust, or skeleton, of |
| seamount range. Three or more seamounts having | many sea animals. |
| connected bases and aligned along a ridge or rise. |  |
|  | shifting sand. Sand of such fine particles and other conditions |
| seapeak. A conical seamount. | that it drifts with the action of the water or wind. |
| seaport. A port situated on the coast with unimpeded | shingle. A descriptive term for gravel (qv). |
| connection with the sea. cf canal port, estuary |  |
| port, river port. | ship canal. A canal large enough to permit the |
|  | passage of ocean-going vessels. |
| seashore. See shore. |  |
|  | shiplift. An installation for dry docking vessels |
| seasonal changes (in sea level). Variations in the sea | whereby they are raised clear of the water on a |
| level associated with seasonal changes in wind | grid and cradle. Ship and cradle can then be |
| direction, barometric pressure,rainfall,etc.Sec.4.6. | transferred ashore on rails to a refitting area |
|  | leaving the shiplift free to lift or refloat other vessels. |
| seawall. A solid structure, usually, of masonry and |  |
| earth, or tetrapods built along the coast to prevent | shipping safety fairway. Area designated as a |
| erosion or encroachment by the sea. Ships cannot | fairway by USA within which no artificial island |
| usually lie alongside a seawall. | or fixed structure, whether temporary or |
|  | permanent is permitted. |
| sector of a light. The portion of a circle defined by |  |
| bearings from seaward within which a light shows | ship's head or heading. The direction in which |
| a specified character or colour, or is obscured. | ship is pointing at any moment. |
| seiche. See 4.1 1. | shipyard. A yard or place containing facilities in the |
|  | way of slips and workshops, etc, for the |
| semi-diurnal (stream or tide). Undergoing a | construction, launching, fitting-out, maintenance |
| complete cycle in half a day. | and repair of ships and vessels. |
| send. See scend. | shoal. A detached area of any material the depth over |

- 23 -

GLOSSARY

| which constitutes a danger to surface navigation. | its greatest declination N or S, or the dates on |
| --- | --- |
| The term shoal is not generally used for dangers | which this occurs. |
| which are composed entirely of rock or coral. cf |  |
| bank, shallow. | solstitial spring tide. The spring tide (greater than |
| Oceanographically, an offshore hazard to surface | average) occurring near the solstices. |
| navigation composed of unconsolidated material. |  |
|  | sound. A passage between two sea areas. A passage |
| shore. The meeting of sea and land considered as a | having an outlet at either end. |
| boundary of the sea. cf coast. Interchangeable | Also, an arm of the sea or large inlet. |
| with coast when used in a wide sense to denote |  |
| land bordering the sea as seen from a vessel. cf foreshore. | sounding. Measured or charted depth of water or the |
| Also, a prop fixed under the ship's bottom or at | measurement of such a depth. cf reduction of soundings. |
| her side, to support her in dry dock. | to sound. To determine the depth of water. |
| to shore up. To support my means of shores |  |
| round a vessel. | SPAR. See 3.108. |
| shoreline. Another name for coastline (qv), in a | spar buoy. A buoy in the form of a pole which is |
| more general sense. | moored to float nearly vertical. |
| sill. Oceanographically, the saddle of any submarine | speed. The speed of a vessel refers to her speed through |
| morphological feature which separates basins | the water unless otherwise specified. cf ground speed. |
| from one another. |  |
| See also dock sill. | spending beach. The beach in a wave basin (qv) on |
|  | which the waves entering the harbour entrance |
| sill depth. The greatest depth over a sill. | expend themselves, only a small residue |
|  | penetrating the inner harbour. |
| silt. Sediment deposited by water in a channel or |  |
| harbour or on the shore, in still areas, or where | spherical buoy. A buoy, the visible portion of which |
| an obstruction is met. A finer sediment than sand. cf clay. | shows an approximately spherical shape. |
| to silt. To choke or be choked by silt. |  |
|  | spheroid. A mathematically regular surface |
| Single Anchor Leg Storage (SALS). See 3.11 1. | resembling a slightly flattened sphere, defined by, |
|  | the length of its axes and used to approximate the |
| Single Point Buoy Mooring (SPBM or SBM). See 3.104. | geoid in geodetic computations. eg Airy (used in- |
|  | Great Britain, International, etc). |
| skerry. A rocky islet. |  |
|  | spindle buoy. A buoy, similar in height to a spar |
| slack water. That period of negligible horizontal water | buoy, but conical instead of cylindrical. |
| movement when a rectilinear tidal stream is changing direction. |  |
|  | spit. A long narrow shoal (if submerged) or a tongue |
| slake. An accumulation of mud or ooze on the bed of | of land (if above water), extending from the shore |
| a river, channel or harbour. Also, such an | and formed of any, material. |
| accumulation left exposed by the tide. |  |
|  | spoil. Mud, sand, silt or other deposit obtained from |
| slick. A local calm streak on the water caused by oil. | the bottom of a channel or harbour, by dredging. |
| Also, the calm patch left by the quarter of a |  |
| ship when turning sharply. | spoil ground. An area set aside, clear of the channel |
|  | and in deep water when possible, for dumping |
| slime. Fine oozy mud or other substance of similar | spoil obtained by dredging, sullage, etc. |
| consistency. | A spoil ground buoy marks the limit of a spoil ground. |
| slip dock. A combination of patent slip and dock | SPM. Single Point Mooring. See 3.104. |
| (the water is excluded by gates and side walls) |  |
| used where there is considerable range of the tide. | spring tide. A tide of relatively large range occurring |
|  | near the times of new and full Moon. |
| slipway or slips. Applied loosely to a building slip. |  |
| A craft or small vessel under repair may be | spur. A projection from a range of mountains or hills or a cliff. |
| hauled on the slips to be clear of the water. | Also, a small projection from a jetty or wharf, |
|  | at an angle to its main axis. |
| snag. A small feature on the seabed capable of | Oceanographically, a subordinate ridge or rise |
| damaging nets and other fishing gear. Also called | projecting outward from a large feature of elevation. |
| a fastener. |  |
|  | stack. A precipitous detached rock of considerable height. |
| solstices. The two points at which the Sun reaches | Also, a pillar left when the roof of an arch |

- 24 -

GLOSSARY

| collapses through continued weathering or wave action. | sullage. Refuse, silt or other bottom deposit for |
| --- | --- |
|  | disposal on a spoil ground, open sea, or some |
| staith or staithe. A berth for ships alongside where | place clear of the channel. |
| the walls or rails project over the ship, enabling | sullage barge. The lighter or barge used for the |
| cargo (in most cases coal) to be tipped direct from | conveyance of sullage. |
| the railway trucks into the vessel’s holds. |  |
|  | surf. The broken water between the outermost line of |
| stand of the tide. A prolonged period during which | breakers and the shore. Also used when referring |
| the tide does not rise or fall noticeably. In some | to breakers on a detached reef. |
| cases this is a normal feature of the tidal |  |
| conditions; in others it is caused by certain unusual | surface current. A current of variable extent in the |
| meteorological conditions. cf high water stand. | upper few metres of the water column. See 4. 1 8. |
| stand on. To continue on the same course. | surge. The difference in height between predicted and |
|  | observed tides due to abnormal weather |
| Standard Time. The legal time common to a country | conditions. See 4.5 and Admiralty Tide Tables. cf |
| or area, normally related to that of the Time Zone | positive surge, negative surge, storm surge. |
| in ,which it wholly or partly 1ies. See Admiralty | to surge. A rope or wire is surged round the |
| List of Radio Signals Vol 5. | revolving drum of a winch when it is desired to |
|  | maintain or ease the strain without heaving in at |
| statute mile. See mile. | the speed of the winch. |
| steep-to. Any part of the shore or the sides of a bank | surging. The horizontal movement of a ship alongside |
| or shoal descends steeply to greater depths is described | due to waves or swell. |
| as steep-to. Boat landings are described as steep-to |  |
| when the gradient is steeper than about 1 in 6. | suspended well. An oil or gas well, not in use, but |
|  | whose wellhead has been capped at the seabed for |
| steerage way. The minimum speed required to keep | possible subsequent use. See 3.101. |
| the vessel under control by means of the rudder. |  |
|  | swamped mooring. A non-operational mooring |
| stern the tide. To proceed against the tidal stream at such a | when the mooring buoy has been temporarily seabed. |
| speed that the vessel remains stationary, over the ground. |  |
| Also, to turn the bows into the tidal stream. | swash. The thin sheet of water sliding up the |
|  | foreshore after a wave breaks. |
| stippling. The graduations of shade or colour | Also, a shoal in a tideway or estuary close |
| produced on a chart by means of dots. | enough to the surface to cause overfalls. |
| stones. A descriptive term for any loose piece of | swashway or swatchway. A chamber across a bank. |
| broken rock lying on the sea floor, ranging in size | or through shoals. cf gut. |
| from that of pebbles to boulders. |  |
| Used in place-names to indicate large detached | sweep. Commonly used contraction of drag sweep(qv). |
| rocks or islets, eg Seven Stones, Mewstone. |  |
|  | swell. See 4.32. |
| storm beach. A beach covered with coarse sand, |  |
| pebbles, shingle or stones, as a result of storm | syzygy. An astronomical term denoting that two |
| waves above the foreshore, and usually | celestial bodies have the same celestial hour angle, |
| characterised by berms or beach ridges. | or celestial hour angles differing by 180(. When |
|  | the sun and Moon are in syzygy spring tides occur. |
| strait. A comparatively narrow passage connecting |  |
| two seas or two large bodies of water. |  |
| strath. Oceanographically, a broad elongated | tableknoll. A knoll having a comparatively smooth, |
| depression with relatively steep walls located on a | flat top with minor irregularities. |
| continental shelf. The longitudinal profile of the |  |
| floor is gently undulating with the greatest depths | tableland. An extensive elevated region with a flat- |
| often found in the inshore portion. | topped level surface. |
| strip light. A light whose source has a linear form, | tablemount. A seamount having a comparatively |
| generally horizontal, which can reach a length of | smooth, flat top. Also called a guyot. |
| several metres. Used on heads of piers, along |  |
| quay walls, at the corners of quays and on dolphins. | tank farm. A barge group of oil storage tanks, usually, |
| It may have a rhythmic character and be coloured. | near an oil terminal or refinery. |
| submerged. A feature is said to be submerged if it | telegraph buoy. A buoy marking the position of a |
| has sunk under water, or has been covered over with water. | submarine telegraph cable. cf cable buoy. |

- 25 -

GLOSSARY

| terminal. A number of berths grouped together and | - Time Zones- The World and described in |
| --- | --- |
| provided with facilities for handling a particular | Admiralty List of Radio Signals Vol 5. cf |
| form of cargo, eg oil terminal, container terminal, etc. | Standard Time, Date Line. |
| terrace or bench. A relatively flat horizontal or | tongue. A long, narrow and usually low, salient point |
| gently inclined surface, sometimes long and | of land. cf spit. |
| narrow, which is bounded by a steeper ascending |  |
| slope on one side and by a steeper descending | topmark. An identification shape, fitted on the tops of |
| slope on the opposite side. | beacons and buoys. cf daymark. |
| tetrapods. Concrete masses the size of boulders, cast | topography. Detailed description or representation on |
| with four stump-legs so that the masses interlock. | a chart or map, of the natural and artificial |
| Used for the pitching of breakwaters and seawalls. | features of a district. |
|  | Also the features themselves. |
| tidal angles and factors. Astronomical data, |  |
| combining the effects of several tidal constituents, | toroidal buoy. A buoy shaped like a ring in the |
| used for the prediction of tides by the Admiralty | vertical plane, usually with a central support with |
| Method. See Admiralty Tide Tables. | a shape, mainly used for oceanographical purposes. |
| tidal basin. See basin. | track. The path followed, or to be followed, between |
|  | one position and another. This path may be the |
| tidal harbour. A harbour in which the water lavel | ground track, over the ground, or the water track, |
| rises and falls with the tide as distinct from a | through the water. Used in the sense of ground |
| harbour in which the water is enclosed at a high | track in the term recommended track (qv). |
| level by locks and gates. | Also used in ships' roureing to mean the |
|  | recommended route to be followed when |
| tide gauge. An instrument which registers the height | proceeding between predetermined positions. |
| of the tide against a scale. | tractive forces. See tide-raising forces. |
| automatic tide gauge. An instrument which |  |
| measures and records the tidal data. | traffic flow: |
| pressure tide gauge. An instrument which | established direction of traffic flow. A traffic flow |
| measures the pressure below the sea surface; this | pattern indicating the directional movement of traffic |
| pressure may be converted to water depth if the | as established within a Traffic Separation Scheme. |
| air pressure, the gravitational acceleration and the | recommended direction of traffic flow. A |
| water density are known. | traffic flow pattern indicating a recommended |
|  | directional movement of traffic where it is |
| tidepole. A graduated vertical staff used for | impracticable or unnecessary to adopt an |
| measuring the height of the tide. | established direction of traffic flow. |
| tide-pools. Pools worn in seashore rocks, left full of | traffic lane. An area within defined limits in which |
| water when the tide level has fallen below them. | one-way traffic is established. Natural obstacles, |
|  | including those forming separation zones, may |
| tide race. See race. | constitute a boundary. |
| tide-raising forces. The forces exerted by the Sun | Traffic Separation Scheme. A routeing measure aimed at |
| and Moon which cause the tides. | the separation of opposing streams of' traffic by appropriate |
|  | means and by the establishment of traffic lane. |
| tide-rip. See overfalls. |  |
|  | train ferry. A ferry, fitted with railway lines to transport |
| tide-rode. An anchored or moored ship is tide-rode | railway, carriages and wagons across the water. |
| when heading into the tidal stream. cf wind-rode. |  |
|  | training wall. A mound often of' rubble, frequently |
| tideway. Where the full strength of the tidal stream | submerged, built alongside the channel of an |
| is experienced, as opposed to inshore where only | estuary or river to direct the tidal stream or |
| weak tidal streams may be experienced. | current, or both, through the channel so that they |
| Also, the channel in which the tidal stream sets. | may assist in keeping it clear of silt. |
|  | Termed 'jetty' in the USA and Canada. |
| timber pound. See pound. |  |
|  | transfer of datum. The method of determining a new |
| time signal. A special signal, usually, by radio for the | chart datum by reference to an established datum |
| purpose of checking the errors of chronometers. | whereby the tide will fall to the datum at the new |
| See Admiralty List of Radio Signals Vol 5. | position when it fails to datum at the old one. |
| Time Zones. Longitudinal zones of the Earth's | transhipment area or lightening area. Area designated for |
| surface each 15( in extent, for which a Zone Time | transfer of cargo from one vessel to another to reduce the |
| is designated. The zones are shown on Chart 5006 | draught of the larger vessel. Also known as cargo transfer area. |

- 26 -

GLOSSARY

| transit. Two objects in line are said to be 'in transit'. cf range. | twilight. See astronomical, nautical and civil |
| --- | --- |
|  | twilight. |
| transit port. A port where the cargo handled is merely |  |
| en routes to its destination and is forwarded by | two-way route. A route within defined limits inside |
| coasters, river craft, etc. The port itself is not the | which two-way traffic is established, aimed at |
| final destination before distribution. | providing safe passage of ships through waters |
|  | where navigation is difficult or dangerous. |
| transit shed. A structure or building on a wharf or |  |
| quay for the temporary storage of cargo and goods |  |
| between ship and rail or warehouse, and vice |  |
| versa. There is a legal difference between a transit |  |
| shed under the shipowner's control and a | uncovered. Exposed; not covered by water. |
| warehouse which may not be. |  |
|  | under current. A sub-surface current. cf surface |
| transporter. A type of travelling crane consisting of a | current. |
| movable bridge or gantry which runs on rails, | There is an implication that the under current |
| straddling a cargo (usually coal) dump and | is different either in rate or direction from the |
| projecting over the quay side. A small crane or | surface current. |
| grab runs along the gantry transporting the cargo |  |
| from dump to vessel or vice versa. | under way. Having way. |
|  | The term, however, is used in the International |
| transporter bridge. A type of bridge which may be | Regulations for Preventing Collisions at Sea (1972) |
| erected over a waterway consisting of a tower | to mean that a vessel is not at anchor, or made |
| either side of the water connected by a girder | fast to the shore, or aground. |
| system along which a carriage runs. A small |  |
| platform at road level is suspended from the | undercliff. A terrace or lower cliff formed by a landslip. |
| carriage and on this the road traffic is transported |  |
| across the waterway. | undertow. A sub-surface current setting into the |
|  | deeper water when waves are breaking. |
| trench. Oceanographically, a long characteristically |  |
| very deep and asymmetrical depression of the sea | underwater. See below-water. |
| floor, with relatively steep sides. |  |
|  | unexamined. A potential danger to navigation is |
| trend of a coast. The general direction in which it extends. | marked unexamined when the least depth of water |
|  | over it has not been rigorously determined. |
| triangulation. The measurement of a system of |  |
| triangles connecting control stations in an area to | unwatched light. A light without any personal |
| be surveyed, in order to ascertain the correct | permanently stationed to superintend it. |
| relative positions of those stations. |  |
| Also, the geometrical framework (also called | upstream. The opposite direction to downstream(qv). |
| horizontal control) thus obtained. |  |
| trilateration. The measurement of a system of triangles |  |
| connecting control stations in an area to be surveyed, | valley. Oceanographically, a relatively shallow wide |
| by measuring the sides of the triangles rather | depression, the bottom of which usually slopes |
| than their angles as in a triangulation. | continuously downward. The term is generally |
|  | not used for features that have canyon-like |
| trot. A line or system of mooring buoys between which | characteristics for a significant portion of their extent. |
| a number of small ships or craft can be secured, |  |
| head and stern. | variation. See magnetic variation. |
| trough. The hollow between two waves. | veer. The wind is said to veer when it changes |
| Oceanographically, a long depression of the sea | direction clockwise. |
| floor characteristically steep-sided and normally |  |
| shallower, than a trench. | vertical clearance. The height above the datum for |
|  | heights of the highest part of the underside of the |
| tufa. A porous concretionary or compact form of calcium | span of a bridge, or the lowest part of an overhead |
| carbonate, which is deposited from solution around springs. | cable. The vertical clearance of fixed bridges is |
|  | measured from the level of MHWS or MHHW |
| turning basin. See basin. | to the underside of the bridge. |
|  | Formerly termed Headway. cf safe overhead |
| turn-round. The turn-around of a vessel in a port is | clearance. |
| the complete operation comprising arrival, |  |
| discharge and loading of cargo, and departure. | vertical datum. A horizontal plane to which heights, |
|  | depths or levels art referred. See chart datum, |
| twenty-foot equivalent unit. See container. | depths or levels art referred. See chart datum, |

- 27 -

GLOSSARY

| datum, Land Survey datum. and Ordnance datum. | wave basin. A device to reduce the size of waves |
| --- | --- |
|  | which enter a harbour, consisting of a basin close |
| vessel traffic service. Any service implemented by a | to the inner entrance to the harbour in which the |
| competent authority designed to improve safety | waves from the outer entrance are absorbed. |
| and efficiency of traffic and the protection of the |  |
| environment. It may range from the provision of | wave trap. A device used to reduce the size of waves |
| simple information messages to extensive | which enter a harbour before they penetrate as far |
| management of traffic within a port or waterway. | as the quayage. Sometimes it take the form of |
|  | diverging breakwaters and sometimes of small |
| vigia. A reported danger, usually in deep water, whose | projecting breakwaters situated close within the entrance. |
| position is uncertain or whose existence is doubtful. |  |
| A warning on the chart to denote that undiscovered | wave-cut shore. A shore or bare rock formed by |
| dangers may exist in the neighbourhood. | wave erosion, or on a limestone or other soluble |
|  | rock by solution. Correctly, a shore which is not a |
| volcanic ash. Uncemented pyroclastic material | beach is wave-cut. |
| consisting of fragments mostly under 4mm in |  |
| diameter. Coarse ash is 0.25 to 4 mm in grain size; | way. The motion of a vessel through the water. |
| fine ash is less then 0.25. |  |
|  | ways. The timber sills upon which a ship is built. |
|  | way point. See reporting point. |
| waiting area. An area with designated limits within |  |
| which ships must wait for a pilot or representative | weather side. The side of a vessel towards which, or on the |
| of the shore authorities. | side of a channel from which, the wind is blowing. cf lee side. |
| walkway. See catwalk. | weather shore. That from which the wind is blowing. |
| warp. A hawser by which a ship can be moved when | weather tide. The opposite of lee tide (qv). |
| in harbour, port, etc. The warp is secured to a |  |
| buoy or some fixed object and brought inboard | wellhead. The head of the pipe drawing oil from an |
| and hauled upon to move the ship. | oilfield or gas from a field of gas. |
| to warp. To move a ship from one place to |  |
| another by means of a warp. | wet dock. A non-tidal basin. |
| warping buoy. Mooring buoys specially laid to |  |
| assist ships hauling off a quay, jetty, etc. | wharf. A structure similar to a quay alongside which |
|  | vessels can lie to discharge cargo. Usually |
| wash. The accumulation of silt and alluvium in an | constructed of wood, iron or concrete, or a |
| estuary. Soil carried away by water. | combination of them, and supported on piles. It |
| Also, the visible and audible motion of agitated | may be either in continuous contact with the land |
| water, especially that caused by the passage of a vessel. | or offset slightly from it, and may be connected |
|  | with it by one or more approach piers. |
| watch buoy. A buoy placed to mark a special position; |  |
| in particular, near a light-vessel, to check its position. | wharfage. In a general way, a charge made against cargo |
|  | passed on to or over a wharf, quay, or jetty. cf quayage. |
| water boat. A boat (usually self-propelled) fitted with |  |
| large water tanks and its own pump and hose | whirlpool. An eddy or vortex of water. |
| connections, used in harbours for supplying fresh | Any body of water having a more or less circular |
| water to sea-going ships. | motion caused by its flowing in an irregular |
|  | channel, or by conjunction of opposing currents. |
| water track. See track. |  |
|  | whistle-buoy. A buoy which emits a whistle, actuated |
| waterborne. Floating, particularly of a ship afloat | by compressed air or by the compression of air in |
| after being aground, or on being launched. | a tube by the action of the waves. |
| watercourse. A natural channel for water, which may | white horses. See breakers. |
| sometimes dry. |  |
|  | wind drift current. A horizontal movement in the |
| waterline. The actual junction of the land and water | upper layers of the sea, caused by wind. See 4.23. |
| at any instant. |  |
| Also, the line along which the surface of the | wind-rode. An anchored or moored vessel is wind- |
| water touches a vessel's hull. | rode when heading, or riding, into the wind. cf tide-rode. |
| waterway. A water feature (river, channel, etc.) | wire drag. See drag sweep. |
| which can be utilised for communication or transport. |  |
|  | wreck. Properly, a vessel that has been wrecked, ie |

- 28 -

GLOSSARY

| ruined or totally disabled, but the term is confined | yaw. Unavoidable oscillation of the ship's head either |
| --- | --- |
| in hydrography to mean a disabled vessel, either | side of the course being steered or when at anchor, |
| submerged or visible, which is attached to, or foul | due to wind and waves. |
| of, the bottom or cast up on the shore. |  |
|  | Zone Time. The system of time-keeping used by a |
| yard. A waterside area constructed and fitted-out for | vessel at sea in which the time kept is that of the |
| a specific purpose usually indicated by a prefix, | appropriate Time Zones (qv). |
| eg boat yard, dockyard, shipyard, etc. |  |
|  | zooplankton. The microscopic drifting animal life of |
| yard craft. See craft. | the oceans including the larvae of the larger |
|  | swimming animals and fish. |

- 29 -