M A I N E N G I N E M A I N T E N A N C E

500 HRS.

- TURBOCHARGER SUCTION FILTER CLEANING

- CYLINDER LUBRICATORS FILTER CLEANING

- ENGINE INDICATORCADS / PRESSURE CARDS DRAWING

- CRANKCASE INSPECTION

1000 HRS.

- TURBOCHARGER OIL CHANGE

- LUB. OIL ANALYSIS

- SAFETY CUTOUTS AND ALARMS CHECKING

- LOCAL START AND STOP CHECKING

2000 HRS

- ALL UNITS SCAVENGE SPACE CLEANING

- SCAVENGE TRUNKING CLEANING

- PISTON AND LINER INSPECTION THROUGH SCAVENGE PORTS

- TURBOCHARGER HOLDING DOWN BOLTS CHECK FOR TIGHTNESS

- GOVERNOR OIL CHANGE

- AUX.BLOWER IMPELLER AND CASING CLEANING

## 4000 HRS

- ALL UNITS FUEL VALVES – PRESSURE TEST / OVERHAUL

- AIR COOLER CLEANING

- DEFLECTION READINGS

- PRESSURE GAUGES AND PYROMETERS CHECKING

- TURNING GEAR OIL CHECK / REPLENISH

- PNUMATIC CUTOUT OVERHAULING

6000 HRS

- ALL UNITS EXHAUST VALVES OVERHAULING

- LUB OIL COOLER NO. 1 & NO. 2 CLEANING

- JACKET WATER COOLER CLEANING

- STERN TUBE LUB. OIL COOLER CLEANING

8000 HRS

- ALL UNITS CYLINDER COVER OVERHAULING

- CROSSHEAD BEARING CLEARENCES

- CROSSHEAD GUIDE CLEARENCES

- CRANKPIN BEARING CLEARENCES

- MAIN BEARING CLEARENCES

- ALL UNITS AIR STARTING VALVES TO O’HAUL

- ALL UNITS RELIEF VALVES TO O’HAUL

- ALL UNITS INDICATOR COCKS TO O’HAUL

- ALL FUEL PUMPS PUNCTURE VALVES TO O’HAUL

- ALL UNITS BOTTOM END BEARING BOLTS INSPECTION

- ALL UNITS CYL.LINER, PISTON WITH ROD AND STUFFING BOX

OVERHAUL

- SCAVENGE AIR FLAPS FUNCTIONAL CHECK

- STARTING AIR DISTRIBUTOR TO O’HAUL

- THRUST BEARING CLEARENCES

- C / CASE BOLTS AND NUTS TIGHTNESS CHECK

- CAMSHAFT DRIVING GEAR INSPECTION

- FUEL CAM INSPECTION

- FUEL CAM NUTS TIGHTNESS CHECK

- TIE ROD TENSION CHECK

- EXHAUST MANIFOLD INSPECTION

- CHAIN DRIVE INSPECTION

- TURNING GEAR OIL CHANGE

- SHUT DOWN SERVOMOTOR O’HAUL

- TURNING GEAR BRAKE LINING CHECK

- STARTING AIR CONTROL VALVE OVERHAUL

### 12000 HRS

- TURBOCHARGER OVERHAULING

16000 HRS

- CAMSHAFT DRIVING GEAR BACKLASH CHECK

- LUB. OIL SUMP TANK CLEANING

## 24000 HRS

- ALL UNITS FUEL PUMPS OVERHAUL

- ALL UNITS CROSS HEAD BEARINGS O’HAUL

- ALL UNITS CRANK PIN BEARINGS O’HAUL

- ALL MAIN BEARINGS O’HAUL

- THRUST BEARINGS O’HAUL

- CLEAN FUEL OIL SERVICE TANK

AUX. ENGINE MAINTENANCE

## 500 HRS

- TURBOCHARGER INTEKE FILTER CLEANING

- FUEL CONTROL LINKS CLEAN / LUBRICATE

- FUEL OIL FILTERS CLEANING

- LUB OIL FILTERS CLEANING

- LUB OIL DROP TEST

- ROCKEARM LUB OIL FILTER CLEANING

## 1000 HRS

- ALLUNITS FUEL VALVES PRESSURE TEST / OVERHAUL

- CHECK AND ADJUST TAPPETS CLEARENCES

- TURBOCHARGER OIL CHANGE

- CRANKCASE INSPECTION

- LUB OIL ANALYSIS

- FUELCAM, TAPPETGUIDES AND ROLLER CHECK

- ENGINE RUUNING GEAR CHECK

- REMOTE  START / STOP TEST

- LOCAL START / STOP TEST

- PEAK PRESSURE RECORDING

- CLEAN ROCKER ARM OIL TANK

- RENEW ROCKER ARM OIL

## 1500 HRS

- CHECK SAFETY AND ALARMS

3000 HRS

- ALL UNITS CRANKPIN BEARING BOLTS CHECK TIGHTNESS

- ALL UNITS EXHAUST VELVES O’HAUL / CHECK SPRINGS

- FUEL CAM FIXING NUTS TIGHTENING TORQUE CHECK

- STARTING AIR ROTORY VALVE INSPECTION

- HOLDING DOWN BOLTS CHECK

- STARTING AIR MAIN VALVE INSPECTION

- FUEL INJECTIONTIMING CHECK

- GOVERNOR OILCHANGE

- CRANKWEB DEFLECTION

- STARTING AIR CONTROL VALVE CHECK

## 6000 HRS

- ALL UNITS CYLINDER COVER OVERHAULING

- ALL UNITS PISTON, CON. ROD.CRANKPIN BEARING O’HAUL

- ALL UNITS CRANK PIN BEARING HOUSING CHECK

OVALITY / SERRATION

- ALL UNITS CRANKPIN BEARING BOLTS INSPECTION

- ALL UNITS INTEKE VALVE O’HAUL / SPRING INSPECTION

- ALL UNITS AIR STARTING VALVES

- ALL UNITS RELIEF VALVES

- MAIN BEARING BOLTS CHECK TORQUE

- BALANCE WEIGHT FIXING BOLTS CHCK TORQUE

- GEARS INSPECT / CHECK BOLTS / BACKLASH

- TURBOCHARGER OVERHAUL

- AIRCOOLER CLEANING

- S.W. AUTO VLAVE OVERHAUL

- CHECK GOVERNOR DRIVE

- SCAVENGE AIR MANIFOLD CLEANING

- ATTACHED L. O. PUMP O’HAUL

- ATTACHED F.W. PUMP O’HAUL

- ROCKER ARM L O PUMP O’HAUL

- LUB OIL COOLER CLEANING

8000 HRS

- ALL UNITS FUEL OIL PUMPS O’HAUL

12000 HRS

- ALL MAIN BEARINGS INSPECTION

- TIMING GEAR CONDITION OF TEETH / BACKLASH

- TIMING GEAR BOLTS TIGHTENING CHECK

- OVERHAULING OF GOVERNOR

16000 HRS

- TURBOCHARGER OVERHAULING / BEARING RENEWAL

- CAMSHAFT BEARING INSPECTION

24000 HRS

1.        ALL UNITS CRANK PIN BEARING BOLTS RENEWAL