NAVIGATION AND WATCHKEEPING

SCOPE

To ensure an adequate watch is maintained at all times so as to monitor safe and efficient ship operation and navigation.

2. ACTIONS

2.1	CERTIEFICATION

The officer in charge of the navigational or deck watch shall be duly qualified appropriate to the duties related to navigational or deck watchkeeping.

The officer in charge of the engineering watch shall be duly qualified appropriate to the duties related to engineering watchkeeping.

Booklet form licenses must be available for inspection proper authorities.

2.2	VOYAGE PLANNING

The intended voyage shall be planned in advance, taking into consideration all pertinent information, and any course laid down shall be checked before the voyage commences.

The chief engineer officer shall, in consultation with the master, determine in advance the needs of the intended voyage, taking into consideration the requirements for fuel, water, lubricants, chemicals, expendable and other spare parts, tools, supplies and any other requirements.

2.2.1	Planning prior to each voyage

Prior to each voyage the master shall ensure that the intended route from the port of departure to the first Port of call is planned using adequate and appropriate charts and other nautical publications necessary for the intended voyage, containing accurate, complete and up-to-date information regarding those navigational limitations and hazards which are of a permanent or predictable nature and which irrelevant to the safe navigation of the ship.

.1	Passage Planning

Thorough passage planning is vital to safe navigation.

Passage planning is the formulation of a comprehensive plan accounting for safe and efficient transit of the vessel from berth to berth.  The planning process, the plan itself , the execution, and the Monitoring of the plan all safeguard against undetected errors and enhance safe navigation.

When voyage orders are received, the master must establish a detailed plan for the voyage.  The planned route should embrace the entire transit, from berth to berth, including those waters where a pilot will be on board.

The master must determine that the vessel is fit and prepared in all respects to undertake the given voyage, and that the depth of water at both origin and destination ports and route is sufficient for her to always remain afloat.

The guidelines and principals outlined in this manual, in applicable company directives, as well as the principals and practice of good sea ship are to be adhered to in the preparation of the passage plan.  The following must be taken into consideration when planning, routes:

a.	Depth of water relative to draft, making due allowance for squat.

b.	Established traffic separation schemes.

C.	Availability and reliability of navigational aids, both conventional and electronic.

d.	Capability and condition of the vessel and her equipment.

e.	Potential situation in event of breakdown (in relation to the possibility of such occurrence on a lee shore etc.).

f.	Current and tides.

g.	Anticipated traffic conditions.

h.	Weather including areas where reduced visibility may be expected.

i.	Advice and recommendations.

j	. Navigational warnings affecting the area.

The above listing is not intended to be all-inclusive.  Other factors pertinent to the voyage in questions are to be given due consideration.

The passage plan is to be clearly established and so written and depicted that it is fully understood by all the navigating officers.

Prior to commencing a voyage, courses and appropriate informational notations are to be drawn on the most suitable charts.  They form an important part of the passage plan, are to be thoroughly checked and approved by the master, and are not to be altered without the master's authorization.  Voyage plan route waypoints are to be entered in electronic navigational equipment as appropriate.

On vessels equipped with Integrated Bridge System (IBS) equipment, appropriate data entries relating to the planned route and safety margins are to be made and reviewed such entries shall include but not be limited to:

a.	Voyage plan route waypoints.

b.	Electronic chart display (ECDIS) and electronic charts with appropriate corrections.

c.	Voyage graphics with appropriate corrections.

d.	Safety Margins and alarm settings.

e.	Turn data for waypoint course changes [rate/radius].

f	Electronic chart data and referencing registration entries or digitizer use (made for the paper charts to be used enroute).

On Integrated Bridge System equipped vessels the planned route data is to be entered prior to sailing and a "test run" made as practicable; with attention paid to safety margins, boundaries off-alarm settings etc.

The plan is not to be inflexible and may be amended by the master at any time in the interests of safety and efficiency.

Records of passage plans used previously are to be carefully maintained , as they are a valuable source of reference information for future plan preparation.

.2	Route Determination

Consistent with the safety of the vessel, and in compliance with applicable company and governmental routing requirements for specific areas, the master is responsible for the selection of routes so that the vessel is navigated in the most efficient and economical manner.  Safe navigation is to be the paramount consideration and time and distance saving secondary to it.

.3	Weather Routing

The company encourages the careful use of weather routing services for ocean voyages or when navigating in typhoon or hurricane areas.  The master is always at liberty to disregard advice received from a weather routing service if, in his judgment there is no advantage in following such advice.

The use of these services does not relieve the master of the normal responsibility for safe navigations nor does it permit discontinuation of the reception and analysis of normal weather reports.

.4	Traffic Separation Schemes

Established traffic separation schemes whether mandatory or voluntary are to be followed unless special circumstances preclude this.  Except in emergent circumstances, a vessel shall not be navigated against the flow of traffic in a separation scheme.

Tanker Vessels shall avoid those areas which are designated to be avoided by tankers.

Locations, terms, definitions and general principles of traffic separation and routing are contained in International Maritime Organization (IMO) publications which are on board of company vessels.

Information on new schemes or revisions to existing schemes will e forwarded to vessels and shall be noted on the charts.

.5	Course and Speed

At all times course and speed shall be set so as to provide an adequate margin a safe maneuver in the event of an unanticipated emergency situation.

The economic objectives of time and distance saving are to be secondary to safe navigation, and are to be disregarded whenever the master deems it necessary, prudent and seaman like to do so.

.6	Selecting Charts, Publications and Hydrographic Information

When selecting charts for navigation, the largest suitable scale should be used.  Only the latest editions and fully corrected charts and publications are to be used.  An up-to-date index of all charts and publications on board must be maintained.  The requirements for the forthcoming voyage shall be carefully checked and any necessary charts or publications must be acquired before sailing.

If in exceptional circumstances, such as due to a change of orders, the best chart for use in a pilotage area is not on board, the chart must be ordered through the local agent and placed aboard with the pilot.

Masters must ensure that charts and hydrographic publications are kept fully corrected from current Notices to Mariners, navigational warnings and other sources.

Extreme care is to be used in the preparation, modification, and correction of electronic charts (ECDIS), electronic ARPA navigational line overlays, due to the potential for grave consequences in event of error.  Prior to utilization, such vessel produced material is to be

carefully checked for accuracy an officer other than the originator Records of correction of such materials are to be maintained in a manner similar to those used for paper charts.

Hydrographic information is to be obtained via NAV-TEX equipment if installed.  Radio officers are to copy radio hydrographic information as broadcast.

The master, trough the designated navigating officer, must ensure that all navigating watch officers are provided with updated information relative to the performance of their duties.

2.2.2	Verification and display of planned route

When the route planning is verified taking into consideration all pertinent information, the planned route shall be clearly displayed on appropriate charts and shall be continuously available to the officer in charge of the watch, who shall verify each course to be followed prior to using it during the voyage.

2.2.3	Deviation from planned route

If a decision is made, during a voyage, to change the next port of call of the planned route, or if it is necessary for the ship to deviate substantially from the planned route for other reasons, then an amended route shall be planned prior to deviating substantially from the route originally planned.

2.2.4	Navigation in Heavy Weather

The master shall observe present and forecast weather conditions closely at all times and shall, if necessary, alter course and speed to avoid heavy weather that might damage the vessel or endanger those on board.  They of the vessel, cargo, personnel, and environment always take priority over any other consideration.

The master shall obtain all available pertinent weather reports and facsimile maps.  A close study of this information is to be made in connections with local weather conditions as observed on the vessel, in order that the track of approaching storms or dangerous conditions may be determined and avoided if deemed advisable.

2.2.5	Very Large Waves Due to Wind and Current Effects

Masters must consider the effect on sea conditions when winds are contrary to currents.  For example, the very large waves sometimes experienced in the Agulhas current and the Gulf Stream occur when wind and current are opposed.  Many ships have been severely damaged or lost due to these waves.  When conditions are conducive to the formation of such waves immediate action must be taken to lead out the ship of the flow of the current.

2.2.6	Sea Passage

Sea passage begins at the point where in the judgment of the master the engines can be safely taken off "stand by" following port maneuvering.

Sea passage ends at the point where engines are placed on "stand by" for the approach to a port.

The engine room shall be given one more hour's notice prior to the ending of sea passage and ample notice prior to commencing sea passage.

2.2.7	Speed in Restricted Waters

When underway in rivers, harbours or other restricted waters, the vessel's speed shall be regulated so as to comply with local speed restrictions and to avoid damage to shore installations, moored vessels, and tows.

2.2.8 Bunkers

Voyage orders to the vessel will indicate whether one-way or round-trip bunkers are to be taken, or whether any limitations as to bunker requirements are needed due to the vessel arriving at shipyard, or other special reasons.

Prior to sailing, the master is to ensure that there are adequate bunkers aboard for the planned voyage plus a safe margin of reserve.

A guideline in calculating a safe margin of reserve is 20% of the bunkers.

The safe margin of reserve should not be less than 3 days consumption, but only in exceptional circumstances should more than 7 days be necessary..

Due allowance shall also be made for bunkers which will be consumed tank cleaning, ballast changing, cargo heating, and during anticipated port delays.

If bunker inventory upon sailing varies significantly from voyage order recommendations, the official issuing the voyage orders must be advised.

2.4 WATCHKEEPING AT SEA

2.4.1 General

.1	Principles

The master of every ship is bound to ensure that watch keeping arrangements are adequate for maintaining a safe navigational watch.  Under the master's general direction, the officers of the navigational watch are responsible for navigating the ship safely during their periods of duty, when they will be particularly concerned with avoiding collision and stranding.  The safe watches are maintained at all times.

The chief engineer officer of every ship is bound, in consultation with the master, to ensure that watch keeping arrangements are adequate to maintain a safe engineering watch at all time.

.2	Protection of marine environment

The master, officers and ratings shall be aware of the serious effects of operational or accidental pollution of the marine environment and shall take all possible precautions to prevent such pollution, particularly within the framework of relevant international and port regulations.

2.4.2	NAVIGATIONAL WATCH

.1	General

The officer on watch is the master's representative and is responsible to him for the safe navigation of the vessel, and for strict compliance With the International Regulations for Preventing Collisions at Sea, 1972, pertinent laws and regulations, and the master's standing and night orders.

The safety of crew, ship, cargo and environment is dependent upon the alertness and conduct of those on watch.  It is the officer's duty to ensure that the highest standards and requirements of good seamanship are maintained at all times.  This is particularly relevant to the keeping of a proper lookout.

Watch officers must fully understand the various underway watch conditions, and their required duties under these conditions as specified in this manual.  In cases of doubt, the master is to be consulted promptly.

Responsibility of Conn.

The officer of the watch continues to be responsible for the safe navigation of the vessel, despite the presence of the master on the bridge, until the master informs him specifically that he has assumed responsibility.  When the master so informs the watch officer, the watch officer shall verbally the transfer of responsibility to the master.  Such change of Conn. shall be recorded in the Deck Logbook.

Familiarization

Deck Officers when joining a vessel and prior to standing a watch should be read this Guidance and the standing orders, as well as familiar with the use and proper operation of all the navigational equipment on board with the advantages and limitations of each piece of navigational equipment and with maneuvering characteristics of the vessel, and they shall then sign their names to signify that they have read the Guidance and standing orders and familiar with all of above.

A good watch keeper is someone who:

-	has a sound knowledge of the principles involved;

-	is guided by the appropriate rules and regulations;

-	looks out for, and recognizes when operations go wrong way;

-	is capable of acting on his own initiative;

-	knows when to call assistance.

Instructions

The officer on watch is to carry out his duties in accordance with this Manual, the company standing orders, and the master's orders given verbally or in writing.

The master shall determine the courses to be made good and shall instruct the watch officer accordingly.

The standing orders signed by the master shall be signed by each officer before taking his first watch on a company vessel to signify that the officer has read the standing orders and is familiar with them.

The master may add to the standing orders at his discretion,

I

A night order book shall be kept in which the master will enter his orders to the watch officer before turning in.  Each officer shall read and sign the orders before taking over the watch.

.3	Lookout

Company policy as well as law requires that every vessel shall at all times maintain a proper lookout in compliance with rule 5 of the International Regulations for Preventing Collisions at Sea, 1972 and shall serve the purpose of

-	maintaining a continuous state of vigilance by sight and hearing, as well as by all available means appropriate in the prevailing circumstances and conditions;

-	so as to make full appraisal of the situation and of the risk of collision, stranding and other hazards to navigation;

-	and additionally, the duties of the lookout shall include the detection of ships or aircraft in distress, shipwrecked persons, wrecks, debris and other hazards to safe navigation.

The look-out must be able to give full attention to the keeping of a proper look-out and no other duties shall be undertaken or assigned which could interfere with that task.

A proper lookout is to be maintained by making intelligent use of people and equipment.  Reliance on radar alone is not sufficient.

The duties of the look-out and helms person are separate and the helms person shall not be considered to be the look-out while steering, except in small ships where an unobstructed all-round view is provided at the steering position and there is no impairment of night vision or other impediment to the keeping of a proper look-out.

The officer in charge of the navigational watch may be the sole lookout in daylight provided that on each such occasion:

a)	the situation has been carefully assessed and it has been established without doubt that it is safe to do so-,

b)	full account has been taken of all relevant factors, including, but not limited to:

-     state of weather,

-     visibility,

-     traffic density,

-     proximity of dangers to navigation, and the attention necessary when navigating in or near traffic separation schemes; and

c)	assistance is immediately available to be summoned to the bridge when any change in the situation so requires.

A	lookout, having no other duties, will be posted:

-	In or approaching heavy traffic.

-	In or approaching areas of low visibility.

-	Arriving at or departing from a port or in restricted waters passage.

From sunset to sunrise and during any other periods as directed by the master or officer on the watch.

When circumstances warrant, additional lookouts shall be posted in accordance with the master's best judgement.

In determining that the composition of the navigational watch is adequate to ensure that a proper look-out can continuously be maintained, the master shall take into account all relevant factors such as:

-	visibility, state of weather and sea;

-	traffic density, and other activities occurring in the area in which the vessel is navigating;

-	the attention necessary when navigating in or near traffic separation schemes or other routing measures;

-	the additional workload caused by the nature of the ship's functions, immediate operating requirements and anticipated maneuvers;

-	the fitness for duty of any crew members on call who are assigned as members of the watch;

-	knowledge of and confidence in the profession competence of the ship's officers and crew;

-        the experience of each officer of the navigational watch, and the familiarity of that officer with the ship's equipment, procedures, and maneuvering capability;

-   activities taking place on board the ship at any particular time, including radio communication activities, and the availability of assistance to be summoned immediately to the bridge when necessary;

-   the operational status of bridge instrumentation and controls, including alarm systems,

-  rudder and propeller control and ship maneuvering characteristics;

- the size of the ship and the field of vision available from the conning position;

- the configuration of the bridge, to the extent such configuration might inhibit a member of the watch from detecting by sight or hearing any external development; and

- any other relevant standard, procedure or guidance relating to watch-keeping arrangements and fitness for duty.

Lookouts shall be posted where they can best perform under the existing circumstances, preferably as far forward as possible.

The watch officer must see that the lookouts are alert, properly clothed, relieved or rotated on station as necessary, and properly trained and instructed as necessary with regard to what to look for and how to report.

When ratings stand lookout for the first time, they should be accompanied by an experienced lookout until affirmatively demonstrating to the master's satisfaction their ability to stand lookout alone.

The lookout shall report to the officer of the watch the condition of the running lights every half hour from sunset to sunrise.

.5	Officer Leaving Bridge

The officer in charge of the navigational watch is on no account to leave the navigating bridge when the vessel is under way unless properly relieved by the master or another licensed officer.

The officer in charge of the navigational watch shall not hand over the watch to the relieving officer if there is reason to believe that the latter is not capable of carrying out the watch keeping duties effectively, in which case the master shall be notified.

6	Relieving the watch

The officer coming on watch must be sober, fully alert and fit in all respects to make over the watch, including having adjusted to night vision during hours of darkness.  Relieving officers shall not take over the watch until their vision fully adjusted to the light conditions.

The officer coming on watch shall:

a.	Arrive on the bridge at least 10 minutes before bell.

b.	Examine the chart and the passage plan, checking:

1)	Ship's position, which is to be confirmed by personal when possible.

2)	Present course and speed.

3)	Progress of the ship throughout the previous watch.

4)	Courses to steer throughout the coming watch and two hours thereafter.

5)	Navigation marks in sight or expected to be sighted during the watch and two hours thereafter. Navigation marks in sight are to be checked by personal observation using a stopwatch to confirm characteristics of lights.

6)	Navigational hazards or potential dangers which the ship is expected to pass during the forthcoming watch and the two hours thereafter.

C.	Be aware of the total navigational and traffic circumstances, particularly with regard to the closest point of approach (CPA), time to CPA and course and speed of other ships in the vicinity.

d.	Read and sign the master's night order book or other written instructions.

e.	Familiarize with:

1)	The passage plan in effect (for the period of the forthcoming watch plus two hours).

2)	Tides and currents anticipated during the same period.

3)	Existing and forecast weather conditions.

4)	Prevailing visibility.

5)	Current radio and other navigation warnings.

6)	Work on deck which may require action to assure of personnel.

7)	Vessel's trim and draft and any operations in progress which may cause a change.

8)	Vessel status with regard to machinery or any item which may affect the ability to maneuver.

9)	Status of electronic navigation equipment.

10)	Status and mode of operation of the following as they relate to integrated Bridge System:

a)	steering mode / autopilot.

b)	Route tracking mode.

c)	Electronic chart in use / route in use.

d)	Speed input source.

e)	Position fixing equipment in use.

f)	Safety margin / warning alarm settings.

g)	Turning mode in use and settings if active.

h)	Data logging intervals.

1)	ARPA status and settings, traffic being monitored.

Check the compasses and course recorder as follows:

1)	Check the navigating compass against the gyro compass.

2)	Check the navigating gyro against steering repeater.

3)	Check the steering repeater against all other repeaters, including the course recorder, radar and D.F.

4)	Check the steering repeater against the magnetic standard and steering compasses.

5)	Check that all the compass courses are as shown on the wheelhouse blackboard/indicator board and accordance with the track checked on the chart.

6)	Check that the course recorder is operating, that the clock is correct (on GMT), and note any adjustment made in the logbook and the recorder roll.

When all the foregoing has been completed, and the relieving officer is satisfied that he is familiar with the situation and that all is in order, the watch shall be formally relieved by a verbal exchange of gyro and standard compass courses.

If at any time, an officer in charge of a navigational watch is to be relieved when a maneuver or other action to avoid any hazard is taking place, the relief of that officer be deferred until such action has been completed.

The! officer going off watch shall:

a.	Never leave the bridge until the watch has been formally relieved.

b.    After compasses have been checked and the watch officer has been formally relieved, write up and sign the log, transcribing any appropriate entries from the bellbook and noting "compasses checked" to indicate that the required compass checking routine has been followed.

C.	Be sure that the relieving officer is familiar with the situation at the time of relief and is in all respects fit and capable of taking over the watch.

d.	Pass all pertinent information to the relieving officer.

e.	Assist the relieving officer in the required compass checks.

E	Sign the course recorder roll and make notations for the past watch with brief explanation for deviations from planned course.

If for any reason the relieving officer refuses to take over a watch, or the officer on watch thinks the relieving officer unfit to safely accept the watch, the master is to be called immediately.  The master will take appropriate action in such circumstances.

.7	Performing a navigational watch

The officer in charge of the navigational watch shall:

-	keep the watch on the bridge;

-	in no circumstances leave the bridge until properly relieved;

-	continue to be responsible for the safe navigation of the ship, despite the presence of the master on the bridge, until informed specifically that the master has assumed that responsibility and this is mutually understood; and

-	notify the master when in any doubt as to what action to take in the interest of safety.

During the watch the course steered, position and speed shall be checked at sufficiently frequent intervals, using any available navigational aids necessary, to ensure that the ship follows the planned course.

a)	Posting Courses

Steering compass courses are to be kept posted on the blackboard/ indicator board in the wheelhouse and entered in the deck logbook for each change of course and for each hour of the watch.

b)	Ship's Position

1	Whenever potential dangers to navigation exist frequent fixes shall be taken to assure

that the position of the ship is positively known and is in conformity with the planned track.

.2	Such fixes shall be cross-checked trough the use of more than one fixing method, thus reducing the risk of grounding as a result of error or failure of navigational equipment.

.3	Soundings must be taken when making a landfall, when the vessel is in restricted or shoal waters and at any other time when they may assist in establishing the position of the vessel.

.4	When electronic fixing is in use, either directly, or via Integrated Bridge System equipment if installed, frequent cross-checking or confirmation of position shall be made by other available means and based upon other data.  When possible such verification shall be by visual means.  Otherwise alternative means available such as: visual bearing/radar range, multiple radar ranges,

.5	When in or approaching areas of possible navigational hazard, the master must determine a point in time or soundings at which, in the absence of a reliable 1.9x, the vessel will be stopped until such time as the vessel's position is determined and it is found safe to proceed.

.6	When out of sight of land, the ship's position must be fixed by every available means and when possible, be fixed by morning and evening star sights and daily sun sights.  Such fixes must be cross-checked with whatever other means are available such as: GPS, Loran C, Decca, Transit SATNAV, Radio Direction Finder (RDF).

.7	The designated navigating officer is to actively participate in obtaining the noon position.

.8	Any significant discrepancy between the observed positions and the dead reckoning position of the ship must he brought to the attention of the master, the conning officer, and (if present on the bridge) the pilot.

.9	A buoy should not be relied on as the sole means of fixing a position, nor used in a range, unless there is no other choice or its position has been confirmed by other observations.  Extreme caution is to be exercised in areas where ice flows or other forces may displace buoys from their charted positions.

.10	Fixes obtained by multiple radar ranges are generally to be preferred to those utilizing radar bearings due to the inherent accuracy of radar ranging and limited accuracy of radar bearing.

Targets for position-fixing by radar must be carefully selected.  Isolated rocks, beacons and the like which are clearly defined and not subject to shift with wind and current are preferred.

c)	Danger Bearings and Safety limits

1	Danger bearings, sextant safety angles and similar methods are to be used in those circumstances where such use will ensure safe navigating limits for the vessel's track.

.2	Where the installed electronic navigation equipment, including radar, ARPA, and Integrated Bridge Navigation Systems have capability to define safety limits and guard zones, such features are to be utilized to the fullest extent possible to ensure safe transit.

.3	Practices such as parallel indexing, defining alarm proximity to depth curves on ECDIS chart equipment, and the implementation of guard zones are to be used as a matter of routine.

.4	On IBS equipped vessels, "what if' simulations are to be run through the planned voyage to the extent possible, with particular attention paid to track limits and grounding avoidance limits and settings.

d)	Identification of Navigational Lights

Positive identification of navigation lights (lighthouses, buoys, beacons, etc.) shall be made using a stopwatch and not by visual associations only.

The officer in charge of the navigational watch shall have full knowledge of the location and operation of all safety and navigational equipment on board the ship and shall be aware and take account of the operating limitations of such equipment.

The officer in charge of the navigational watch shall not be assigned or under- take any duties which would interfere with the safe navigation of the ship.

No talking shall be permitted with the man at the wheel or the lookout in the line of duty.

Officers of the navigational watch shall make the most effective use of all navigational equipment at their disposal.

When using radar, the officer in charge of the navigational watch shall bear in mind the necessity to comply at all times with the provisions on the use of radar contained in the International Regulations for Preventing Collisions at Sea, in force.

In cases of need, the officer in charge of the navigational watch shall not hesitate to use the helm, engines and sound signaling apparatus.  However, timely notice of intended variations of engine speed shall be given where possible or effective use made of UMS engine controls provided on the bridge in accordance with the applicable procedures.

The engineer on watch is to be notified in the followings, circumstances:

a.	As soon as it appears the engine maneuvers may be required.  Notice one or more hours in advance is desirable.

b.	One hour or more before end of sea passage.

C.	Before commencement of sea passage.

d.     One or more hours before requiring an additional steering power unit

unit.

e.	One hour before requiring an additional generator unit.

(f) When reduction of visibility threatens.

g.	When air temperature drops to 0o C.

h.	One or more hours before the inert gas system is required.

i.	One or more hours before the hydraulic power pack unit is required.

j.	One or more hours before the deck cargo crane is required.

k.	Whenever the vessel's machinery operation may be affected by weather or other external condition changes.

Officers of the navigational watch shall know the maneuvering characteristics of their ship, including its stopping distances, and should appreciate that other ships may have different handling characteristics.

Details of the maneuvering characteristics of each ship are to lie prominently displayed in the wheelhouse.  Maneuvering information is to be given for both light and loaded conditions, and is to show the lowest constant engine RPM at which the ship can safely steer, and details of turning circles and stopping distances as may currently be required by national regulations and international recommendations.

All information posted should be for calm weather, no current and deep water conditions with a clean hull.  These facts should be clearly noted on the data displayed with a warming that the vessel's response may significantly change under different conditions, including shallow water.

The company offices issue instructions concerning trials to obtain maneuvering data pertinent to their particular fleets.

A proper record shall be kept during the watch of the movements and activities relating to the navigation of the ship.

It is of special importance that at all times the officer in charge of the navigational watch ensures that a proper look-out is maintained.  In a ship with a separate chartroom the officer in charge of the navigational watch may visit the chart room when essential, for a short period for

the necessary performance of navigational duties, but shall fist ensure that it is safe to do so and that proper lookout is maintained.

Operational tests of shipboard navigational equipment shall be carried out at sea as frequently as practicable and as circumstances permit, in particular before hazardous conditions affecting navigation are expected.  Whenever appropriate, these tests shall be recorded.  Such tests shall also be carried out prior to Port arrival and departure.

The officer in charge of the navigational watch shall make regular checks to ensure that:

I	title person steering the ship or title automatic pilot is steering the correct course;

.2	the magnetic and gyro compasses are to be compared at the change of the watch at sea and at least once every 30 minutes thereafter, as well as after each change of course.  The compasses shall be checked frequently by observation, and the error determined after each change of course, or at least once each watch, if possible, when there is no change of course.

Full data regarding each observation shall be entered in the compass observation book.  The error of all compasses and the deviation of the magnetic compasses shall be entered in the deck logbook, and due allowance made for courses steered and in the application of bearings;

.3	the automatic pilot is tested manually at least 10 minutes once a watch; before entering waters where navigation may require special caution the manual steering system shall be tested;

.4	the navigation and signal lights and other navigational equipment are functioning properly.  The running lights shall be tested one half hour before sunset;

.5	the Unmanned Machinery Space controls, alarms and indicators are functioning properly.  Tests of whistle, telegraph, telephones and general alarm bells shall be making at noon each day before entering restricted water or as might be required by national or local regulations.  The whistle shall not be tested when the presence of other vessels might result in it being mistaken for a passing signal.

On ship fitted direct bridge control of engine systems, prompt and effective engine response shall be tested prior to entering restricted waters and at any time it is anticipated that maneuvering control may be needed.

The officer in charge of the navigational watch shall bear in mind the necessity to comply at all times with the requirements in force of the International Convention for the Safety of  Life at Sea.  The officer of the navigational watch shall take into account:

1	the need to station a person to steer the ship and to put the steering into manual control in good time to allow any potentially hazardous situation to be dealt with in a safe manner; and

.2	that with a ship under automatic steering it is highly dangerous to allow a situation to develop to the point where the officer in charge of the navigational watch is without assistance and has to break the continuity of the look-our in order to take emergency action.

.3	Automatic steering (gyro control) normally will be used during open sea passages.  The steering mode will be changed over automatic to manual steering:

a.	For any emergency situation.

b.	For all maneuvers to avoid ship traffic.

c.	Whenever the steering characteristics of the ship may be affected by shallow water and/or weather.

d.	For training purposes at the master's discretion.

e.	Whenever the master or officer on watch considers it necessary.

.4	All deck officers must be thoroughly familiar with the proper method of changing steering modes.

The changeover procedures for each vessel are to be posted for ready reference close to the steering position.  Any change of steering mode must be made or directly supervised by the officer on watch.

Helmsmen are not to make any steering mode changeover, or interfere with or operate the steering mode controls in any way, unless supervised by the officer on watch.  Change of steering mode is to be noted in the Deck Logbook and on the course recorder roll.

Officers of the navigational watch shall be thoroughly familiar with the use of all electronic navigational aids carried, including their capabilities and limitations, and shall use each of these aids when appropriate and shall bear in mind that the echo- sounder is a valuable navigational aid.

The officer in charge of the navigational watch shall use the radar whenever restricted visibility is encountered or expected, and at all times in congested waters, having due regard to its limitations.

The officer in charge of the navigational watch shall ensure that range scales employed are changed at sufficiently frequent intervals so that echoes are detected as early as possible.  It shall be borne in mind that small or poor echoes may escape detection.

Whenever radar is in use, the officer in charge of the navigational watch shall select an appropriate range scale and observe the display carefully, and shall ensure that plotting or systematic analysis is commenced in ample time.

Calling the Master

The master must keep the bridge watch officer advised of his whereabouts at all times when the vessel is at sea, The watch officer must not hesitate to call the master at any time when in doubt, or when assistance is required.

The master is to be called before a doubtful situation becomes an emergency, and early enough to ensure that he has sufficient time to analyze the problem.

The watch officer may sound two short rings on the general alarm bell to call the master when he is not available by normal communications.

The officer in charge of the navigational watch shall notify the master immediately:

1    if restricted visibility is encountered or expected;

.2	if the traffic conditions or the movements of other ships are causing concern;

.3   if difficulty is experienced in maintaining course;

.4	on failure to sight land, a navigation mark or to obtain soundings by the expected time;

.5	if, unexpectedly, land or a navigation mark is sighted or a change in soundings occurs;

.6	on breakdown or failure of the engines, propulsion machinery remote control, steering gear or any essential navigational equipment, alarm , indicator or if doubt exists with regard to the accuracy of such equipment;

.7	if the radio equipment malfunctions;

.8	in heavy weather, if in any doubt about the possibility of weather damage;

.9	if the ship meets any hazard to navigation, such as ice or a derelict;

.10	upon receipt of a distress call;

.11	if cross-checking of position reveals a significant disparity between position observation and electronically generated position in use; and

.12	in any other situation where the officer of the watch is in any doubt or requires assistance.

Despite the requirement to notify the master immediately in the foregoing circumstances, the officer in charge of the navigational watch shall in addition not hesitate to take immediate action for the safety of the ship, where circumstances so require .

The officer in charge of the navigational watch shall give watch keeping personnel all appropriate instructions and information which will ensure the keeping of a safe watch, including a proper look-out.

When the vessel is being conned the master with or without assistance of a pilot, watch officers are to assist to the fullest extent possible.  In keeping with the Bridge Team concept of bridge operation, at all times every deck officer on duty on the bridge must be aware of the intended track, the voyage plan in progress, and alert to the overall navigational and traffic situation to the maximum extent possible.  There must be a free exchange of information between bridge team members.

To this end the master must keep bridge team members apprised of intended maneuvers as fully as circumstances permit.  In the event of the master personally operating bridge controls, (such as making autopilot course changes, changing engine control settings, etc.), the practice of announcing the "order" to those present on the bridge is to be adhered to.  This is imperative to keep bridge team members informed and can also assist helmsman and lookout performance as well.

Bridge team members noticing factors pertaining to the safe navigation of the vessel must not hesitate to call them to the attention of the cognizant team member.

2.4.3 WATCH KEEPING UNDER DIFFERENT CONDITIONS AND

IN DIFFERENT AREAS

.1	Clear weather

The officer in charge of the navigational watch shall take frequent and accurate compass bearings of approaching ships as a means of early detection of risk of collision and bear in mind that such risk may sometimes exist even when an appreciable bearing change is evident, particularly when approaching a very large ship or a tow or when approaching a ship at close range.  The officer in charge of the navigational watch shall also take early and positive action in compliance with the applicable International Regulations for Preventing Collisions at Sea, 1972 and subsequently check that such action is having the desired effect.

In clear weather, whenever possible, the officer in charge of the navigational watch shall carry out radar practice.

.2	Restricted visibility

When restricted visibility is encountered or expected, the first responsibility of the officer in charge of the navigational watch is to comply with the relevant rules of the International Regulations for Preventing Collisions at Sea, with particular regard to the sounding of fog signals, proceeding at a safe speed and having the engines ready for immediate maneuver.

Definitions of Deteriorating and Restricted Visibility

For the purposes of this manual, and for reference when issuing Instructions to watch officers, the master shall establish and clearly define two conditions of low visibility.  These will be referred to as "deteriorating" and "restricted" visibility's.  "Deteriorating" visibility is a range of visibility from about 5 miles down to about 2.5 miles.

"Restricted" visibility is a range of visibility from about 2.5 miles down to zero.

Deteriorating and restricted visibility upper and lower limits will vary according to changing circumstances.

In setting visibility range limits, the following factors must be taken into consideration:

a.	The experience of the watch officer(s), both deck and engine.

b.	The status of the ship's plant.

c.	The maneuvering capabilities of the ship.

d.	The operating condition of the radar/ARPA equipment.

e.	Navigational restrictions which might restrict bold course alterations before the effect of speed reduction can be brought about by engine use.

f.	Traffic type, density and flow pattern(s) in the area.  It should be recognized that head-to-head closing speeds of upwards of 40 knots are not uncommon, coupled with increased ship inertia.

g.	The need for standby personnel and the time required before they are able to be on station and ready to assist.

By written order and verbal instruction, the master shall ensure that deck watch officers are completely aware of the actions to be taken when restricted visibility is expected or encountered.

Deteriorating Visibility - Actions by Watch Officer

When the range of visibility diminishes to the "deteriorating" state as set by the master, the watch officer shall:

a.	Inform the master.

b.	Ensure that all radar/ARPA equipment is in operation.  Check radar/ARPA operation and update plot.

c.	Call helmsman if not already present, engage hand steering.

d.    Instruct and post lookouts as required.

e.	Inform the engine room.

f.	Energize navigation lights if not on.

g.    Record actions taken in the Deck Logbook.

Restricted Visibility - Actions by Watch Officer

When the limit of visibility diminishes to the "restricted" state as set by the master, the watch officer shall:

a.	Place engines on stand by so as to have engine room preparations made for full range of orders, and reduce speed as required for safe navigation.

b.	Call the master promptly.  The master will set the appropriate steaming watch and will assign watch personnel to the duties required.  Any change of Conn. must be clearly stated and logged.

c.	Check that the radars/ARPA are operating property, and update plot.  When the master takes the Conn., with or without the assistance of a pilot, the watch officer will normally assume the radar watch.  If conditions warrant, the master may assign a different officer to this duty, but there must be no confusion as to duty assignments.

d.	Call personnel as required for the steaming watch set the master.

e.	Instruct and post additional lookouts as required.

f.     Sound appropriate signals as required by the Rules of Navigation to Avoid Collision at Sea.

g.	Engage hand steering, if still in automatic.

h.	Comply with the Rules of Navigation to Avoid Collision at Sea.

i.	Record steaming watch set and other actions taken in the deck logbook.

Sudden Reduction of visibility

When visibility suddenly becomes "restricted" without prior indications of deterioration, the watch officer shall:

a.	Take action promptly as required by the circumstances.  The conning officer must know which method will most quickly and safely bring the ship to a stop if this emergency action is required.

b.    Comply with the provisions of section above.

Radar/ARPA

The use of radar does not license a vessel to proceed at speeds immoderate for the circumstances or to neglect to keep a proper lookout.  Information obtained from radar may indicate a lesser speed than if no such data were available.

Proper radar plots and use of ARPA are to be made at all times when navigating in restricted visibility.  Courses/speed changes are dangerous without detailed information as to the target CPA (closet point of approach), time to CPA, course and speed.  These factors must be determined if the bearings of closing targets are not altering sufficiently to assure passing.

If these factors cannot be ascertained for any reason, extreme care must be exercised and speed reduced or the vessel stopped as required.  The conning officer must not hesitate to take all way off the ship if necessary in these circumstances.

ARPA equipment shall always be utilized when its use will contribute toward the safe navigation of the vessel.  Caution is to be taken that own ship heading and speed data input is maintained current at all times to preclude the generation of erroneous information.  The "Trial maneuver" capability of installed ARPA equipment is to be utilized to provide projected target information for proposed course alternations.

Radar must not be used as a means of edging a vessel into port under conditions which are normally prohibitive.  In such conditions, it should be used as an aid in taking the vessel to a safe anchorage.  Similarly, radar must not be used to sail from a port conditions which would otherwise be prohibitive.

It should be recognized that the reduction of speed in restricted visibility provides additional time for the assessment of radar plots and the determination of required action.

Anchoring Due to Restricted Visibility

When in the master's opinion circumstances justify it, the vessel may be brought to anchor until such time as conditions improve and the voyage can be safely resumed.

.3	In hours of darkness

The master and the officer in charge of the navigational watch, when arranging look-out duty, shall have due regard to the bridge equipment and navigational aids available for use, their Mutations; procedures and safeguards implemented.

.4	Coastal and congested waters

The largest scale chart on board, suitable for the area and corrected with the latest available information, shall be used.  Fixes shall be taken at frequent intervals, and shall be carried out by more than one method whenever circumstances allow.

The officer in charge of the navigational watch shall positively identify all relevant navigation marks.

Navigation with Pilot on board

General Policy

The master must employ a pilot whenever the safe navigation of the vessel or local regulations make this necessary or advisable.

The presence of a pilot aboard in no way relieves the master of responsibility for the safe navigation of the vessel which he must continue to oversee.

Pilot - Monitoring Actions

The master and watch officers must remain and attentive to the pilot's handling of the vessel.  They must counsel the pilot at any time they judge the pilot to be in error or otherwise neglecting the safe navigation of the vessel.

On some occasions the pilot may issue instructions relative to conning the ship to the helmsman, the watch officer, and the tugboats.  The master must be in a position to hear all of these instructions which are deemed to be instructions of the master unless modified or rescinded by the master.

The silence of the master is equivalent to an approval of the pilot's instructions.

Should the pilot fail to act on the master's counsel when the master judges the safety of the vessel to be jeopardized, the master must take action as appropriate to secure the safety of the vessel.  Full details must be entered in the Deck Logbook.

The watch navigation officer check all courses ordered and shall constantly monitor the vessel's progress through pilotage waters by frequently plotting on the chart.

The master must insist that the pilot comply with the appropriate Rules of Navigation to Avoid Collision at Sea observe speed restrictions when navigating rivers and narrow channels and when passing close to piers, small craft underway or at anchor, vessels with tows and moored vessels.

Pilot - Order Communications

The telegraph or bridge engine control must always be operated by the watch navigation officer or the master.  Engine orders must be repeated and their execution checked by the watch navigation officer.

Helm orders must be repeated by the helmsman and checked for proper execution by the watch navigation officer or master.

It is of special importance that extra care is taken by the master and deck watch officers when the pilot's native language is different from that of the helmsman or themselves.

Pilot - Action in Case of Doubtful Competence

If any doubt exists as to the pilot's competence in local navigation or expertise in handling the vessel, the master must take positive action to obtain a licensed pilot.  Such action includes proceeding to a suitable anchorage and waiting until another pilot is available.

If no alternative exists, the master must take extraordinary precautions to monitor and verify the pilot's actions.

Pilot/Master Data Exchange

When the pilot/mooring master boards, he shall be advised by the master:

a.	If at sea:

1)	Vessel's present heading and compass error, if any.

2)	Ground speed and speed of this through the water.

3)	Position of helm.

4)	Position of vessel by bearing and distance from a prominent navigation mark.

5)	Details of close-by traffic.

6)	Draft, trim, and depth of water below keel.

7)	Pertinent details of the vessels' handling characteristics.

8)	Any limitations in operating ability, whatever the cause.

b.	If in port:

1)	Vessel's state of readiness.

12)	Draft, trim, and depth below keel.

3)	Pertinent details of vessel's handling characteristics.

4)	Any limitations in operating ability, whether due to malfunction or any other cause.

The pilot can then assume his duties on the vessel.

The master and the pilot shall then discuss the Forthcoming operation and both must have a clear understanding and agreement of all aspects of it.

The following shall be among the points they consider:

-	Planned navigational route.

-	State of tide along route and at berth.

-	Depth of water along route, making due allowance for squat.

-	Speed at various points along route.

-	Limiting conditions which would cause operation to be abandoned.  For example, reduced visibility or wind.

-	Alternative action if operation is abandoned.

-	Use of anchors (planned and emergency).

-	Maneuvers requiring tugs.

-	Number and power of tugs.

-	Disposition of tugs.

-	Use of ship or tug lines?

-	Communications procedures, from ship to shore, and from ship to tug.

-	Crew standby requirements.

-	The side of the vessel to be against the deck when moored,

-	Maximum wind force acceptable during mooring and unmooring.

-	Details of the mooring arrangement.

-	Sequence and method of line handling during mooring and unmooring.

-	Whether pilot is to be changed, together with the method and position when changing pilot.

-	Disembarkation position.

-	Method of disembarkation.

Pilots - Embarking/Disembarking - Pilot Ladders/Pilot Hoists

A deck officer and an unlicensed crew member must be standing by at the boarding point whenever pilots board or leave the ship.  An unlicensed crew member standing by along is not sufficient.

Pilots ladders must always be maintained in a good, clean condition and every precaution shall be taken to ensure the safety of the embarking/disembarking pilot.

Pilot ladders shall:

-	Be in one length: two or more lengths shackled or lashed together are not acceptable.

-	Be kept solely for embarkation/disembarkation of pilots.

-	Be fitted with spreaders min. 180 cm long apart to prevent twisting.

-	Be rigged so that each step rests firmly against the side of the ship with the lowest step 2 feet (60 cm) above the water or to height required by pilot.

-	Be rigged well clear of all discharges and water outlets.

-	Be rigged at a place where a good lee can be given.

-	Be rigged with man-ropes with knots min. diameter 28 mm if required by pilot.

When the distance from sea level to the point of access to the ship is more than 9 meters, then the pilot ladder shall be so rigged that the pilot can transfer from it to an accommodation ladder to gain access, or some other equally safe means of access must be provided.

Accommodation ladder should lead aft. max. 55o slope lower platform horizontal rigging handrails preferred.  Pilot ladder must extend at least 2m above lower platform.

The heaving lines are always to be provided.

A life buoy with self-igniting light and 27 meters of buoyant line must always be at hand at the point of embarkation when embarking/disembarking pilots.

When a pilot hoist is used, an additional ladder must be rigged in the immediate vicinity of the hoist to within about 60 cm of the water.

Pilot hoists are to be maintained in a good condition at all times.  Particular attention is to be paid to the condition of the falls and the power unit.

Pilot hoists are to be thoroughly checked by a licensed officer prior to use each time they are used.

.6	Ship at anchor

A licensed deck officer shall supervise the letting go and weighing of anchors.

This officer will keep conning officer constantly informed as to the amount of chain out, its direction, and tension.

The anchor windlass is to be inspected regularly by the chief officer and the chief engineer, and maintained to the highest possible standards,

Anchors shall be kept ready for immediate use at all times while the vessel is underway in restricted waters, but the riding pawls are to be left dawn until just before letting go.

Each anchor shall be fitted with a suitable anchor buoy.  Anchor chains, shackles and pins shall be inspected when anchors are being heaved in.  Any deficiencies discovered shall be corrected at the earliest opportunity.  Chains shall be marked with the customary turns of wire and painted links indicate the amount of chain in use.

While at anchor, the officer in charge of the navigational watch shall:

I	determine and plot the ship's position on the appropriate chart as soon as practicable;

.2	when circumstances permit, check at sufficiently frequent intervals whether the ship is remaining securely at anchor by taking bearings of fixed navigation marks or readily

identifiable shore objects but shall never be greater than one per hour to detect any dragging.  A log entry shall be made in each instance;

.3	ensure that proper look-out is maintained;

.4	ensure that inspection rounds of the ship are made periodically;

5	observe meteorological and tidal conditions and the state of the sea;

.6	notify the master and undertake all necessary measures if the ship drags anchor;

.7	ensure that the state of readiness of the main engines and other machinery is in accordance with the master's instructions;

.8	if visibility deteriorates, notify the master,,

.9	ensure that the ship exhibits the appropriate lights and shapes and that appropriate sound signals are made in accordance with all applicable regulations; and

.10	take measures to Protect the environment from pollution by the ship and comply with applicable pollution regulations.

Anchoring in ice

Unless no alternative is available, masters should not attempt to anchor in or near ice, especially in strong currents.  Ice can cause very large strains on the anchor chains or the loss of anchor and chains.

.7	Helicopter Operations

General

Except as modified by this manual helicopter operations shall be conducted in accordance with the recommendations contained in the International Chamber of Shipping document: Guide to

Helicopter/Ship Operations> Revised Edition: 1987, or the latest edition.

Policy on Helicopter Use

The use of helicopter services to company vessels for routine operational purposes is approved by LSC subject to the service being judged, cost effective, beneficial.  The company office will advise on the status of approved helicopter services.

In addition, helicopters may be used in an emergency situation or when it is an operational necessity such as when embarking and disembarking pilots at such ports where helicopters are the only means for carrying out embarkation/disembarkation of pilots for certain type/size of vessel.

Shipboard Sites and Markings

Shipboard sites and markings for helicopter operations should be in accordance with and as detailed in the International Chamber of  Slipping (I.C.S.) Guide to Helicopter/Ship Operations.

Shipboard Procedure During Helicopter Operations

When engaged in helicopter operations, vessels must always be on standby conditions, whether at anchor or underway.  Should it become necessary to alter course or speed during an operation, the helicopter pilot must be informed immediately by V.H.F. Radio.

Tanks must be vented to atmospheric pressure about one hour before operations and then the vents must be closed.  All valves openings in the cargo system must be tightly closed and no trace of gas must be evident when permission is given for the helicopter to take up position over the vessel.  This condition must be rigidly maintained irrespective of dispersal conditions from wind and rotor down draft.

All aerials together with standing and running rigging in the vicinity of helicopter operations are to be lowered or secured well clear of the maneuvering area.  Masters must, on every occasion, specifically check against this type of obstruction and advise the helicopter pilot accordingly.

Request for Helicopter Service

Request for emergency helicopter service, or routine helicopter service for which prior approval of the company office has been obtained, shall be sent through the ship's agent or appropriate body.

.8	Arrival Preparations

All preparations for entering port shall be made sufficiently in advance so that there is no delay in vessel docking , cargo handling, or transaction of ship's business.

Such preparations include but are not limited to the following items:

. 1  Having mooring lines on deck and ready for use.

.2	Having fire-fighting equipment ready for use.

·	3 Rigging derricks to handle cargo and/or bunker/cargo hoses.

.4	Having ullage measuring equipment at hand on tank tops for tanker

5	Having all port papers prepared.

6	Informing the agent, as appropriate, of requirements in advance by

7	Fitting correct size reducers to manifolds for tankers.

8	Having notices indicating grades to be handled, in position on cargo  for tankers.

Port and terminal information issued to vessels indicates the size of the shore loading arm, or hose connections.  For terminals where loading arm or hose connection data is lacking or whenever any doubt exists, the master should communicate by radio with the agent and request such information sufficiently in advance of arrival to ensure that the correct reducers are properly fitted prior to berthing - (for tankers).

Prior to port arrival or departure, all navigation equipment, communications equipment including lights and whistles, the engine telegraph or bridge control unit, and the steering gear are to be tested.  Notations to this effect shall be made in the Deck Logbook and Engine Logbook.,

The arrival and departure checklists in this Manual detail items to be checked.

Prior to entering or leaving port, all department heads must be notified so that they can make the necessary preparations.

The chief officer is responsible to the master for securing the vessel for sea and preparing for arrival and shall report pertinent facts to the master and the bridge watch officer.  An inspection is to be made to ensure that hatches to peak tanks, double bottoms and similar watertight closures are secured before navigating in restricted waters.

Hydraulic Power shall be kept on deck machinery whenever the vessel is moored, anchored, or underway in port.

The master is responsible for the prevention of smuggling of goods, carriage of banned substances and illegal entry of individuals carried on board his vessel.

Prior arrival at a port the master must search the ship for stowaways, contraband, narcotics, and other materials restricted by national law at the next port of call.  All instances where contraband, narcotics or stowaways have been found shall be reported to the Local Custom's or Port Authorities on arrival.  The master shall retain evidence for Custom's action and shall cooperate with any further Custom's search requirements.

The Master must inform the company office whenever any illegal substances are found aboard his ship.  All events are to be recorded in the Deck Logbook.

2.4.6 BRIDGE BELLBOOKS AND AUTOMATIC LOGGER SYSTEMS

The bellbook is to be kept by the officers on watch when leaving and entering port, when navigating in close waters, when maneuvering in restricted visibility and at any other time when maneuvering.  The officer keeping the bellbook will initial the entries.

The following items are to be recorded in the bridge bellbook:

a.	Signals given to engine room and exact time.  On vessels fitted with automatic engine order/revolution logger systems, the only orders to the engine room that need to be recorded are "Stand-by Engines", "Finished with Engines", "Full Away on Sea Passage" and "End of Sea Passage".  Certain concise notations as to why engine orders where given are required, even when automatic engine order/revolution logger systems are in use , such as "reduced speed to pass dredger".

b.	Time and distance of each navigational aid and landmark when abeam.

c.	Courses steered when piloting by compass.

d.	Name of pilot and time of boarding and leaving.

e.	Name of each tug used and the time it arrives alongside and departs.

f.	RPM to be developed for each telegraph signal.

g.	All other information pertinent to the vessel's movement.

2.4.7 DECK LOGBOOK

The Deck Logbook shall be a full and accurate account, by watches of the navigation and activities of the vessel at sea and in port.

At sea it shall indicate conditions of the wind, sea and weather, and navigational information which will permit the track of the vessel to be plotted from the information contained.  All tests of navigational and emergency, equipment, drills, inspections, changes of time; cargo, ballast or bunker operations; casualties, and unusual occurrences shall also be recorded.,

In order to avoid financial loss by owners if cargo is damaged the carrier will have to demonstrate that he has fully and properly cared the cargo and all commercial records must be accurately done during loading, carrying and discharging of cargo.

In port it shall be kept in a similar manner insofar as applicable, and shall also show cargo, ballast or bunker loaded or discharged, and drafts, deadweight, trim and list arriving and sailing.

The Deck Logbook is to be sighed by the officer on watch at the conclusion of the watch.

The master is to sign the Deck Logbook each day.

2.4.8	BOTTOM DAMAGE

In the event of it being necessary to inspect double bottom and/or peak tanks to determine the existence or the extent of bottom damage, great care must be taken to eliminate the possibility of unnecessary additional flooding.  The tank should always be sounded prior to opening, and the cover must be slacked off slowly.  Company safe tank entry procedures are to be followed.

.3	Radio Direction Finder

The accuracy of the radio direction finder (RDF) should be checked at intervals by comparison of radio direction finder bearings with visual bearings, and the results recorded in the radio direction finder logbook.

The radio direction finder shall be calibrated at least after each dry dock repair period, or more frequently as the master thinks fit.  The calibration/correction scale shall be posted close to the radio direction finder set.

.4	Electronic Position Fixing Systems

Masters and navigating officers are expected to make full and proper use of the GPS, Loran C, Decca, Transit SATNAV and other similar systems.  This will require familiarity with the operating procedures for each equipment installed.

Separate performance/ repair history logs are to be maintained for each equipment .

The accuracy of the navigation systems is to be periodically checked by using positions of known accuracy and the results are to be entered in the performance and deck logbooks.

The electronic navigation systems are to be left operating continuously whenever possible and they are to be checked for function and accuracy prior to sailing.

.5	Gyro Compass

The third officer is responsible for the operation and maintenance of the gyro compass and related equipment.

Gyro equipment shall be used and serviced strictly in accordance with the manufacturer's instructions.

The master gyro compass is to be left operating unless there is cause to secure it.  If secured, it is to be started in sufficient time to permit settling on the Meridian before getting underway.

The master gyro, repeaters and course recorders are to be synchronized and checked before getting underway.

Any malfunction in the gyro equipment is to be immediately reported to the master, as well as being noted in the deck logbook.

Strict attention is to be paid to the compass checking procedures specified in corresponding instructions.

.6	Course Recorder

Course recorders are to be operated on Greenwich Mean Time (GMT) and will be kept in operation whenever the vessel is underway or at anchor.

Any course recorder failure must be immediately noted in the deck logbook and the company office is to be notified by the fastest means possible.

Roll Notations and Retention

The following notations shall be made and initialed on the course recorder chart roll:

-	Each day the ship's noon position, whether by fix or dead reckoning, together with the date and a notation that the recorder clock and settings have been checked.

-	Important deviations from the ship's course as planned by the master, as made to avoid traffic, navigation hazards or emergency situations.

-	Other important data, such as the time when passing headlands and fights when coasting.  Used course recorder rolls are to be stored aboard for 3 years.  If removed prior to this, a record is to be kept of their removal, disposition, and return.

In case of an accident to the vessel, the entire course recorder roll shall be removed from the recorder even if only partly used, properly identified with the ship's name and date in ink, signed by the master, and the officers on watch at the time of the accident, and shall be retained on board pending instructions from the company office.

.7	Magnetic Compass

The third officer is responsible for care of the magnetic compasses.  If any doubt exists as to the accuracy of the magnetic compasses, the vessel must be swung to determine the errors and new deviation tables prepared.

If assistance is required for the adjustment of magnetic compasses, the master, when the permission from company office is received, has to request the services of a compass adjuster as soon as practicable.

Particular attention should be given to the condition of the magnetic compasses after extensive repairs or when the vessel has been on one heading for a considerable period of time.

The magnetic compasses should be adjusted after each dry dock repair period, or more frequently as the company requirements or the master thinks fit.  Magnetic compass binnacles are to be kept covered when not in use.  Binnacle foundations are to be inspected periodically.

Off Course Alarm

In vessels so equipped, the "off-course alarm" must always be set to give timely warning of undesired course variations.

.8	Sextants

Officers are expected to maintain the sextant which they are using in a proper error free condition, regardless of whether it is personal or company property.

The third officer is responsible for seeing that company owned sextants are sent ashore for maintenance when necessary.

.9	Chronometers

The third officer is responsible for the care of the ship's chronometers.  Manual chronometers shall be wound with extreme care at the same time each day.  Batteries of quartz chronometers are to be changed at the manufacturers recommended intervals.  Chronometers are to be serviced in accordance with manufacturer's recommendations.

Chronometers shall be kept on Greenwich Mean Time (GMT).

Each chronometer shall be compared with time signals daily and the error on Greenwich Mean Time (GMT) determined and entered in the chronometer rate book.  When time checks cannot be obtained for any reason, the error shall be calculated and noted accordingly.

.10	Ships' Clocks

The third officer is responsible for the winding, setting and care of all ship’s clocks except those in the radio room and machinery spaces.

Clocks on the bridge and in the engine room shall be synchronized at noon each day and also prior to getting underway and at the end of sea passage.

All ship's clocks except the radio room clock are to be kept on ship's time.  The radio room clock shall be kept on Greenwich Mean Time (GMT).

.11	Echo Sounder and Hand Lead

The third officer is responsible for the care of the echo sounder, shallow water indicators and hand lead.

The accuracy of echo sounder and shallow water indicators should be checked against the handle lead line when the opportunity arises while the vessel is at anchor.

The radio officer may be called upon to assist in the repair and maintenance of echo sounder equipment.

.12	Meteorological Instruments and Hydrometers

The third officer is responsible for the care of all meteorological instruments and hydrometers.  Barometer accuracy shall be checked at least every two years against known standards.

.13	Binoculars

The third officer is responsible for the care of the ship's binoculars.

At least two pair of binoculars are to be kept on the bridge in good condition at all times while the vessel is underway.

Binoculars are not to be opened by vessel personnel.  If internal cleaning or adjustment is necessary, they are to be sent to a reputable instrument maker or exchanged through the company office.

.14	Searchlights

The third officer shall be responsible for the care of the ship's searchlights.  They shall be tested at frequent intervals to ensure their readiness for immediate use.

.15	Flags and Signals Equipment

The third officer is responsible for care of the vessel's visual signaling equipment, distress lights and pyrotechnics.  At least one full set of international code flags shall be on board at all times ready for immediate use.

National ensigns, required for the trade in which the vessel is engaged, are to be kept on hand in good condition.

The national ensign of the vessel's country of registry is to be flown from the stem or gaff from 08.00 to sunset while in territorial waters.  In certain waters it may be obligatory for the vessel's national ensign to be flown day and night in which case such requirements shall be met.

When in foreign ports vessels shall fly the national ensign of the country in which the port is located at the fore truck, in accordance with that country's regulations.  If no regulation exists, it shall be displayed during the same hours as the vessel's national ensign while the vessel is in port.

Soiled or torn flags should be replaced at the first opportunity.

International custom shall be followed with respect to dipping the ensign to naval vessels of all nationalities.

Aldis lamp batteries shall be kept fully charged at all times and a supply of spare lamps shall be maintained on board.

.16	Deck Flood Lights

Deck flood lights are to be tested regularly and operated as necessary to dry out.

Deck flood lights shall not be covered due to fire hazard.

.17 Pyrotechnics and Distress Signals

Pyrotechnics and Distress Signals shall be always maintained in good condition according to the appropriate standards.

Out of date line throwing rockets and pyrotechnic distress signals shall never be used for practice purposes.

.18	VHF Bridge Radio

Bridge radio equipment use should be restricted to the ship's navigational requirements and communications for official company business.

Bridge-to-bridge VHF use is mandatory for all vessels in United States waters.

The bridge VBF radio must be operating and properly monitored when the vessel is underway or at anchor.

The watch officer must feel free to use this equipment as needed, especially to determine the maneuvering intentions of other vessels.

The watch officers are expected to know  the proper channels to be used.  For the services required a proper VHF radio telephone log is to be kept.

The radio officer is responsible for the care and maintenance of this equipment, and for the administration of any charges associated with its use.

.19	Portable walkie-talkie Radios

The radio officer is responsible for the maintenance of the intrinsically safe portable VHF/UHF radio equipment.  The VHF/UHF sets and spare batteries are to be kept fully charged.  It is the responsibility of each officer to look after the set he is using and report any defects to the radio officer, When no radio officer is assigned and officer is to be appointed by the master to maintain the portable radio equipment.

.20	Testing prior to getting underway

About one hour before sailing time the third officer shall test the navigation and communications equipment.

.21	Steering Gear

Additional Power Units

When operating in or approaching port limits, in restricted water, in areas of heavy traffic, in areas of reduced visibility and at any time when the master calls for a standby condition, an additional steering gear power unit shall be placed in operation while units may be operated in parallel.

On vessels where this cannot be done, the valves and switches should be lined up so that the standby steering gear power unit can be put into operation with the least delay.

The additional steering gear power unit shall be placed in operation in good time, and while the vessel is still clear of close traffic and navigational hazards.

The bringing into operation of additional steering gear units shall be recorded in the Deck Logbook.

Testing

Steering gear shall always be tested prior to getting underway, and after the starting of an additional power unit, when it is safe to do so, by putting the rudder hard over both ways.

Engineer on watch visually check position of rudder and cross check with Watch Officer, on bridge direction of rudder movement and angle achieved.

Prior to departure from port, the test shall include, as appropriate, the following:

(a)	Main steering gear

(b)	Auxiliary steering gear

(c)	All remote steering gear control systems

(d)	Rudder angle indicators

(e)	Power failure alarms

Such tests	shall be recorded in the Deck and Engine Logbooks.

Emergency	Steering Stations

The vessel shall be steering from the after steering station at least once every three months.  A record of this test is to be made in the deck officers' logbook.

The test is to include direct control from within the steering gear compartment, the communications procedure with the bridge and, where applicable, the operation of alternative power supplies.

.22	Additional Generators

When maneuvering in restricted waters or when, the master calls for a standby condition, additional generators shall be placed in operation to provide a steady source of power available on the failure of generator unit.

2.5	WATCH KEEPING IN PORT

2.5.1 GENERAL

On any ship safely moored or safely at anchor under normal circumstances in port, the master shall arrange for an appropriate and effective watch to be maintained for the purpose of safety.  Special requirements may be necessary for special types of ships' propulsion systems or ancillary equipment and for ships carrying hazardous, dangerous, toxic or highly flammable materials or other special types of cargo.

When vessels are laid up special instructions will be issued by the company office.

Whenever a vessel is berthed, the master should develop a contingency plan on how best to take the ship off the berth in the event of an emergency, such as a fire at the shore installation.  Such a plan should allow for the possibility that no tugs or pilots may be available at the time when the emergency makes it necessary to take the ship out of the berth.

A Night Order Book shall be maintained in which the Master or Chief Officer shall enter any orders relative to handling cargo, ballasting ship, or any other matters requiring special attention.

When vessel is in port, a Night Order Book shall be read and signed by Deck Officer before the watch.

A port directory shall be maintained and kept available to the officer on watch in port.  It shall indicate telephone numbers or other means of contacting firefighters, police, physicians, hospitals, the Coast Guard, the agent, and others needed for emergency assistance without delay, together with details of any special procedures for emergency notification required by local authorities.

The vessel must be searched for contraband, narcotics and stowaways before sailing from a port.  The results of the search must be recorded in the Deck Logbook.,

2.5.2	WATCH ARRANGEMENTS

.1	General

Arrangements for keeping a deck watch when the ship is in port shall at all times be adequate to:

1.   ensure the safety of life, of the ship, the port and the environment, and the safe operation of all machinery related to cargo operation;

.2	observe international, national and local rules; and

.3   maintain order and the normal routine of the ship.

The master shall decide the composition and duration of the deck watch depending on the conditions of mooring, type of the ship and character of duties.

If the master considers it necessary, a qualified officer shall be in charge of the deck watch.

The necessary equipment shall be so arranged as to provide for efficient watchkeeping.

The chief engineer officer, in consultation with the master, shall ensure that engineering watchkeeping arrangements are adequate to maintain a safe engineering watch while in port.  When deciding the composition of the engineering watch, which may include appropriate engine-room ratings, the following points are among those to be taken into account:

I	on all ships of 3,000 kW propulsion power and over there shall always be an officer in charge of the engineering watch;

.2	on ships of less than 3,000 kW propulsion power there may be, at the masters discretion and in consultation with the chief engineer officer, no officer in charge of the engineering watch; and

.3	officers, while in charge of an engineering watch, shall not be assigned or undertake any task or duty which would interfere with their supervisory duty in respect of the ship's machinery system.

.2	Taking over the watch

General

Officers in charge of the deck or engineering watch shall not hand over the watch to their relieving officer if they have any reason to believe that the latter is obviously not capable of carrying out watchkeeping duties effectively, in which case the master or chief engineer shall be

notified accordingly.  Relieving officers of the deck or engineering watch shall ensure that all members of their watch are apparently fully capable of performing their duties effectively.

If, at the moment of handing over the deck or engineering watch, an important operation is being performed it shall be concluded by the officer being relieved, except when ordered otherwise by the master or chief engineer officer.

The master shall determine the vessel's sailing time, and this is to be conspicuously posted at the gangway as soon as possible after arrival at a berth.

Taking over deck watch

Prior to taking over the deck watch, the relieving officer shall be informed of the following by the officer in charge of the deck watch as to:

I	the minimum depth of the water at the berth or anchorage during the watch and the following two hours, the ship's draught, the level and time of high and low waters; the securing of the moorings, the arrangement of anchors and the scope of the anchor chain, and other mooring features important to the safety of the ship; the state of main engines and their availability for emergency use;

.2	If the vessel is at anchor, determine the position of the vessel by means of visual cross bearing or by the prudent use of electronic navigational aids including echo sounder, if visual bearings are not possible, and compare it to the original ship's and anchor position.

.3	all work to be performed on board the ship; the nature, amount and disposition of cargo loaded or remaining, and any residue on board after unloading the ship;

.4	the level of water in bilges and ballast tanks;

.5	the signals or lights being exhibited or sounded,

6	the number of crew members required to be on board and the presence of any other persons on board;

.7	the state of fire-fighting appliances;-,

.8   any special port regulations;

.9	the master's standing and special orders;

.10	check the weather forecast;

.11	ascertain that the appropriate signals are being displayed;

.12	ascertain which officers are aboard;

.13	check the posted sailing time;

.14	determine the availability of keys to locked spaces;

.15	the lines of communication available between the ship and shore personnel, including port authorities, in the event of an emergency arising or assistance. being required;

.16	any other circumstances of importance to the safety of the ship, its crew, cargo or protection of the environment from pollution; and

.17	the procedures for notifying the appropriate authority of any environmental pollution resulting from ship activities.

Relieving officers, before assuming charge of the deck watch, shall verify that:

. I   the securing of moorings and anchor chain is adequate-,

.2	the appropriate signals or lights are properly exhibited or sounded;

.3	safety measures and fire protection regulations are being maintained;

.4	they are aware of the nature of any hazardous or dangerous cargo being loaded or discharged and the appropriate action to be taken in the event of any spillage or fire;

:.5	no external conditions or circumstances imperil the ship and that it does not imperil others.

.3	Performing the deck watch

The officer in charge of the deck watch shall:

.1	make rounds to inspect the ship at appropriate intervals (one per hour);

.2	pay particular attention to:

.2.1	the condition and securing of the gangway, anchor chain and moorings, especially at the turn of the tide and in berths with a large rise and fall, if necessary, taking measures to ensure that they are in normal working condition,

.2.2	the draught, under-keel clearance and the general state of the ship, to avoid dangerous listing or trim during cargo handling or ballasting,

.2.3	the  weather and sea state,

.2.4	the observance of all regulations concerning safety and fire protection,

.2.5	the water level in bilges and tanks,

.2.6	all persons on board and their location, especially those in remote or enclosed spaces, and

.2.7	the exhibition and sounding, where appropriate, of lights and signals;

.3	in bad weather, or on receiving a storm warning, take the necessary measures to protect the ship, persons on board and cargo;

.4	take every precaution to prevent pollution of the environment by the ship;

.5	in an emergency threatening the safety of the ship, raise the alarm, inform the master, take all possible measures to prevent any damage to the ship, its cargo and persons on board, and, if necessary, request assistance from the shore authorities or neighboring ships;

.6	be aware of the ship's stability condition so that, in the event of fire the shore fire-fighting authority may be advised of the approximate quantity of water that can be pumped on board without endangering the ship;

.7	offer assistance to ships or persons in distress;

.8	take necessary precautions to prevent accidents or damage when propellers are to be turned; and

.9	enter in the appropriate log-book all important events affecting the ship such as:

.9.1	all tests of equipment;

.9.2	drafts and deadweight arriving and sailing;

.9.3	details of cargo/ballast handled with pertinent details of the operation;

.9.4	water salinity on arrival at and prior to departure from a berth;

.9.5	weather information;

.9.6	cargo segregation, type and loading rate;

.9.7	inspection of ship's condition to confirm of seaworthiness;

.9.8	Notice of Readiness to load;

.9.9	tanks (holds) inspection by surveyors;

.9.10	any specific instructions concerning the cargo;

.9.11	any notice of protest issued by vessel or received;

.9.12	precaution to minimize the risk of oil spills;

.9.13	any information pertinent to the operation of the vessel or its personnel;

.9.14	notation of security inspections;

.9.15	details of maximum Bending Moment and Shear Force on sailing.

The officer on watch shall careful attention as to be given to ensure that:

1	the gangways, gangway safety nets, accommodation ladders, and pilot ladders are properly rigged, illuminated during darkness, and kept at safe condition at all times when the vessel is at a berth or at anchor;

.2	the gangway, accommodation ladder, or pilot ladder is adjusted to meet with the changes in the ship's draft or tidal conditions and that it is kept clear of obstructions;

.3	a life ring with 27 meters of buoyant line with a light attached shall be kept at hand the gangway, accommodation ladder, or pilot ladder;

.4	adequate lighting is to be provided at night, either by means of a spotlight or by portable floodlights of an approved type;

.5	the gangways, accommodation ladders, and pilot ladders shall be repaired as necessary and shall be taken out of service immediately if damaged.  Non-skid treads shall be replaced when wont.  An approved safety net shall be used with all ships gangways and other similar gangways.

.6	all persons boarding or leaving the vessel must do so by way of the gangway, accommodation ladder, or pilot ladder.  No person shall be permitted to board or leave the vessel until a proper means of access is available.

Security Patrols and following precautions are to be taken:

1	when the vessel is at a berth, the officer of the watch shall make a careful inspection of the vessel at least once during each hour.  If the officer of the watch is unable to make this inspection, then another member of the watch shall be assigned to do so;

.2	In addition to the foregoing, during the night, watch personnel shall make a security inspection of unfrequented parts of the vessel, at one hour intervals of not more than two hours to detest any outbreak of fire or other dangerous condition;

.3	On completion of each of the foregoing inspections, an appropriate entry shall be made in the Deck Logbook;

.4	All precautions are to be taken to prevent unauthorized persons boarding the ship;

..5	The possibility that a hijack or sabotage attempt may be made against a vessel cannot be entirely disregarded.  The probability of such an attack varies and is largely dependent upon the area in which the vessel is trading, current world political activities and the vessel's registry;

.6	The master is to take any steps he considers necessary including employing shore-based security guards to assist vessel personnel in maintaining security;

.7	Security guards, when employed, should be from a reputable security organization and be selected with the advice of the local agent;

.8	In the event of an attack on the ship or a hijack attempt, the preservation of the lives of vessel personnel is to be placed above all other considerations;

.9	Visitors shall be permitted aboard company vessels only in accordance with governmental and terminal regulations, company instructions, and with the permission of the master;

.10 The company office will issue further information and direction with regard to security when necessary.

All unoccupied spaces, including the bridge, the radio room, an d personnel quarters are to be locked in port.

This is particularly important with regard to those places which contain valuable property.

The third officer is responsible for the security of the binoculars and navigational and meteorological instruments in port.

The officer on watch shall measure the density of the water immediately following arrival at, and prior to departure from, a berth.  The measurement taken prior to sailing shall be taken shortly before completion of cargo operations, if loading so that the proper adjustments can be made to the draft.

The measurements are to be recorded in the Deck Logbook.

Before testing the engines when the vessel is at a berth or at anchor, the engineer officer on watch must obtain the permission of the deck officer on watch.

Prior to granting such permission, the deck officer on watch shall see that all the mooring lines are tight, the gangway is secure, and the propeller is clear.

During engine testing the Chief Officer must be on bridge and orders to engine have to be done by him.

2.5.3	Watch in port on ships carrying hazardous cargo and on tankers

(on top of previous requirements)

.1	General

The master of every ship carrying cargo that is hazardous, whether explosive, flammable, toxic, health-threatening or environment polluting, shall ensure that safe watchkeeping arrangements are maintained.  On ships carrying hazardous cargo in bulk, this will be achieved by the ready availability on board of a duty qualified officer or officers, and ratings where appropriate, even when the ship is safely moored or safely at anchor in port.

On ships carrying hazardous car-o other than in bulk, the master shall take full account of the nature, quantity, packing, and stowage of the hazardous cargo and of any special conditions on board, afloat and ashore.

.2	Watch arrangements

A licensed deck officer shall be on duty at all times while the vessel is in port, except when the vessel is an a laid- up status.

The officer on watch shah be up and about the decks during the watch and shall not leave the vessel, except on duty in the immediate vicinity, until property relieved.

The officer on watch in port is to be guided by the International Safety Guide for Oil Tankers & Terminals (I.S.G.O.T.T.) and is to follow Master's orders, Senior Officer's instructions, the requirements of this Manual and other related company Standing Orders for Deck Officers.

No officer shall be assigned sole watch duties appertaining to cargo handling unless he is adjudged to be sufficiently conversant with the Master's and Company’s requirements in this regard.  Specific requirements are to be emphasized by the Head of the Department on the basis of this Manual, the International Safety Guide for Oil Tankers and Terminals, Company instructions, and Shore Terminal requirements when appropriate

Emergency towing off wires are to be rigged in accordance with the International Safety Guide for Oil Tankers & Terminals (I.S.G.O.T.T.) or as required by local regulations.

When in port, foam monitors, if fitted, are to be kept ready for use.  Foam monitors in proximity to the cargo manifold should be directed toward the manifold.

If foam monitors are not fitted, hoses and portable foam equipment are to be rigged to cover the manifold area.

Portable dry chemical fire extinguishers are to be placed on each side of the cargo Manifold.  The fire main should, when possible, be kept under pressure from ship or shore supply.  If the fire main is not under pressure, the fire pump is to be on standby and ready for immediate use.

.3	Performing the deck watch

During cargo or ballast operations make a round of the vessel to determine that all operations, pollution prevention, safety, and security requirements are being met.

The vessel shall be maintained in position alongside the dock as to avoid undue strain on hoses or rigid cargo arms.  In specific locations it may be necessary to take on ballast to maintain the proper freeboard for hoses and rigid cargo arms.

Mooring lines shall always be secured to bitts and should never be left on which drums except when secured to winches specially designed for this purpose.  The officer on watch shall make sure that mooring lines are attended to as necessary to ensure that they do not become excessively slack or taut.

Cargo hoses are to be carefully watched and tended as necessary to prevent their becoming nipped between the ship's side and the dock structure.

The officer on watch and officers and ratings engaged in bunker, ballast, or cargo handling operations must take all precautions to prevent any spills or leakage.

The officer on watch is to ensure that the requirements of this Manual are complied with and shall pay particular attention to the following:

.1	plugging of suppers;

2    operation of sea valves and cargo pumps when commencing to load ballast;

.3	closing and sealing of sea valves and overboard discharge valves.

The waters around the ship are to be kept under constant surveillance to detect any pollution.

When in port, a warning sign shall be posted at the gangway or accommodation ladder so as to be most visible to persons boarding the vessel.  The sign shall read:

WARNING:

NO OPEN LIGHTS

NO SMOKING

NO VISITORS

Before testing the engines the cargo hoses are to be disconnected.

3. REFERENCE

- SOLAS

- STCW-78/95

- ISM Code

- Bridge Procedures Guide

4. RECORDS

- Deck Log Book

- Navigational Operation Check Lists

-	Passage Planning Form with Check List

-	Maintenance record logs

-	Error Logs

1.	Scope: To describe response to human error.

2. Procedure

EFFECTIVE RESPONSE TO HUMAN ERROR

The officers in charge of the navigational watch must be remembered that a ship is moving and needs to be controlled with respect to navigation and collision avoidance.  Typical errors and faults can arise through the following omissions:

·	Failure to complete a task when required.

*	Ignorance of the ship's dimensions and behavior.

*	Undetected difference between intended track and track made good.

*	Not monitoring manual or auto helm wander, ruder indicators, compasses and course recorders.

·	Not monitoring engine controls or indicators.

·	Unresolved difference between ground speed and RPM.

·	Measuring by single technique.

·	Unresolved cross-track error.

·	Not monitoring visibility.

·	Not briefing the lookout.

·	Not searching visually.

*      Searching solely by radar.

·	No taking compass bearing.

·	Not making a radar /ARPA/ plot.

Making decisions on inadequate knowledge of target behavior.

·	Not displaying lights or sounding signals.

·	Wrongly applying the Colregs.

·	Omitting to inspect the ship.

·	Omitting to monitor the location and working of the crew.

·	Mistaking the correct identification of a light, landmark or navigational aid visually, on radar or on the chart.

The errors can be avoided:

* Plan ahead and know what to expect.

* Develop safe routines and habits to ensure most safe practices are covered under normal operations, whilst leaving time and energy to solve difficult problems.

*	Check and monitor others and expect others to decks and monitor you.

*	Apply self checking habits to all activities on the bridge:

a)	check workings after first results have been obtained;

b)	formulate approximate results before working out detailed calculation;

c)	plan ahead - estimate, at the time of taking over the watch, the position in which the ship will be at the end of the watch;

d)	check the distance between fixes to verity that the speed is as expected;

e)	check a parallel index with a position fix;

f)	do not rely on one method of fixing when additional methods are available;

g)  use check list.

SUMMARY

·	Be aware of what can go wrong.

·	Be aware of human mistakes.

·	Understand how errors occur.

·	Discipline yourself each watch to:

a)	plan ahead;

b)	set up safe routines;

c)	check yourself;

d)	check and monitor others.

·	Start each watch by adopting the above principles.

·	Avoid becoming too preoccupied with a particular instrument, particularly radar.

·	Maintain an outward vision and situational awareness.

·	Be prepared to admit a mistake, learn from the incident and work out a way to avoid repeating it in future.

*  Keep alert during ocean passages by moving around the bridge.

Annex I : Ordering, completing, storage and correction of charts and nautical publications procedures

GENERAL PROVISIONS

-1	Due to the constant changes in navigational situation charts and nautical publications become obsolete comparatively soon after their issue.  Hence it is necessary to keep charts and nautical publications update as safety of navigation depends to a great extent on their correctness.

1-2	Systematic correction and amendment of information in the charts and in nautical publications in order to keep them update, i.e. In conformity with actual situation at sea (location) is called correction.

1-3	Timely notification of seafarers of all changes in navigational situation and sailing conditions at seas and oceans shall be carried out by:

1-3-1	Transmission of navigational information by radio:

·	Navarea in accordance with World System of Navigational Warnings (WSNW).

·	Navtex (Coastal Warning) in accordance with regional systems of navigational warnings.

*	LOCAL WARNING - through VHF radio stations, and also through pilots-,

·	Some countries continue to broadcast information through their national systems such as HYDROPAC, HYDROLANT USA.

1-3-2	Reporting navigational information through the following publications:

Notices to Mariners by hydrographic offices (IM GUNIO MO RF, Notices to Mariners of the British Admiralty, The Defense Mapping Agency in the USA etc.)

1-3-3	publishing:

·	of additions and summary corrections to nautical publications

·	insets for separate sections of nautical charts

1-3-4	Republication of charts and nautical publications.

2	ORDERING OF CHARTS, BOOKS AND CORRECTIVE DOCUMENTS

2-1	Ordering of  British publications

2-1-1	Ordering of British charts, books and corrective documents by the ships of the shipping company shall be made from the company KELVIN HUGHES LTD with which the shipping company made an agreement telex 884934/KELHUE G/HAINAULT ESSEX ENGLAND Telephone - 0815006166, fax 08115598535 (the company has 6 service offices in Great Britain and 5 in Canada).

The order shall be made as preliminary agreed with the head of the chart division of the shipping company, with the exception of the ships which are automatically supplied by KELVIN HUGHES.

2-1-2	Delivery of the ordered navigational publications shall be made under control of KELVIN HUGHES to any port of the World ocean within 3 days.  It is necessary to state the port of destination and full address of the agent.

2-1-3	If the ship does not call at British ports but sails to other ports of the world, the order with KELVIN HUGHES shall not be less than 5 charts or books, otherwise it is advisable to order charts (corrective documents) from the agent directly in the port of destination, keeping the head of the chart division and technical superintendent of the Shipping Company informed of the order made without fail.

2-1-4	British charts of the regions of the Baltic and North seas, Western and Eastern coasts of England, Ireland and the Straits of Gibraltar may be ordered in the Chart division of the Shipping Company.  In this case prices for the Shipping Company's ships will be 15% lower than the starting prices for British charts as the Shipping Company is a distributor of K.H.

The delivery of the charts ordered in the Chart Division of the Shipping Company is made through Material and Technical Supply Service in a container with provision. - or jointly with the change of crew.

2-1-5	After receiving British charts/books ordered it is necessary to send by radio acknowledgement of the receipt of the charts/books to 2 addresses:

Riga Charts Division Mr. Tokarevitch and tech. superintendent of the vessel

Company KELVIN HUGHES indicating the number of Dispatch Note.

2-1-6	Any claims concerning the ships' supply with British charts/books against the company KELVIN HUGHES as well as return of publications sent by mistake shall be addressed to: KELVIN HUGHES LTD, HAINAULT ESSFX ENGLAND Telex 884934, Fax 08115598535, Phone - 0815006166 for Return Despatch Instructions, stating the reason.

2-2	Ordering of Russian publications

2-2-1	Russian navigational publications for the ships of the Shipping Company, which do not trade in the ports of  Riga, Ventspils shall be ordered ahead of time (5-10 days) in Riga Charts Division of LSC via tech. superintendent of the vessel.  Delivery of the charts, books and corrective documents ordered shall be made through Material and Technical Supply Service in a container with provision or with the change of crew.

2-2-2	The order of the Russian navigational publications in foreign ports (Klaipeda, Tallinn, Saint Petersburg, Murmansk, Archangelsk etc.) Is made only on agreement with the Head of Riga Charts Division of the Shipping Company via tech. superintendent of the vessel.

2-2-3	The ships calling at basic ports (Riga, Ventspils) shall make orders for necessary navigational publications not later than 2 days prior to arrival in the port with the indication of the agent.  Delivery of the order shall be carried out by the agents of the servicing companies or navigational mates of the master shall receive necessary publications directly in the Charts Division of the LSC.

2.2.4	After receiving navigational publication it is necessary to address the acknowledgement of the receipt of the charts/books by radio to: Riga Charts Division Tokarevich and to tech superintendent of the vessel, with the indication of the date and number.

3	COMPLETION OF THE SHIIP'S SET OF CHARTS AND NAUTICAL PUBLICATIONS.

3-1	The Compulsory list of charts and nautical publications comprising a ship's set is defined by the shipowner.

When completing the ship's set is it is necessary to take into account plans of carriages fixing the ship on a particular shipping line, possible variants of changing the area of sailing.

3-2	The Master of the ship has the right to complete the established ship's set.

3-3	The ship's set shall comprise the following charts and nautical publications:

3-3-1	Nautical navigational charts according to the set established by the shipowner.  General charts of the scale 1: 1 00000 for open region and 1: 500000 for coastal regions shall be kept for all possible variants of the ship's sailing,

3-3-2	Radionavigational charts if the relevant reception facilities are available on the ship.

3-3-3	Electronic charts if the appropriate equipment is available on the ship and with the permission of the shipowner.

3-3-4	Auxiliary charts and nomographs:

a)	charts for great-circle sailing

b)	boat charts meant for provision of life boats

c)	hydrometeorological charts for information on currents, high sea, tides, ice,

winds, fog and dangerous phenomena and other hydrometeorological elements.

d)	nomograph No 90199 to define initial course during great-circle sailing

3-3-5       Nautical publications and guides for sailing:

a)	sailing directions

b)	lights and signs

c)	radiotehnical facilities

d)	transmission schedule of navigational and hydrometeorological notices for seafarers.

e)	Navigation tables for fixing the ships position using radio navigational systems

f)	rules of sailing

9)	charts and books catalogues

h)	hydrometeorological atlases and tables

i)	reference books

4	REGISTRATION, STORAGE, WITHDRAWAL AND HANDING OVER OF CHARTS AND NAUTICAL PUBLICATIONS

4-1	Registration of charts, books and nautical publications is kept in Ship's Chart index.  Its first part contains numeration of folios (sets) and the regions they cover.  The availability of charts per each Folio is noted in the second part.  Two or three folios contain books and other publications.  In the third part all the charts, books and other publications with the dates of their issue are noted.  The ships automatically supplied by KELVIN HUGHES receive from it the ship's Charterindex already corrected.

4-2	Together with the Ship's Chartindex KELVIN HUGHES supplies Chart Correction Log which indicates all the charts and books of the ship's set in consecutive order.  This book allows the master to check quickly the condition of correction at the given moment.

4-3	All corrective documents shall be stored in a special place in the chart room and it is necessary to keep records of them with indication of place and date of receipt.

4-4	The following documents shall be kept accurately filed in separate files:

·	Copies of orders for charts and nautical publications

·	Waybills for the charts and nautical publications received

·	Protocols for the charts and nautical publications eliminated

·	Monthly statements in established form on the check of correction of the ship's set

Annual inventory reports of the ship's set with the indication of the date of issue

4-5	Charts from the ship's set shall be replaced by new ones:

* If  NTM declares them unsuitable for navigational purposes (in case of replacement with a new edition)

* In connection with wear and tear due to constant use when sailing in one and the same region.

4-6	Neglected correction is not the reason for the chart replacement by the new ones.

4-7	The charts and nautical publications which became unsuitable or declared unsuitable for navigational purposes shall be eliminated only after delivery to the ship of the new charts and publications instead of the eliminated ones.

4-8	the ship's set of the charts, nautical publications and corrective documents shall be transferred according to the report of the appropriate format (this Manual Appendix IV-I).

4-9	The person accepting the ship's set of charts and nautical publications is obliged:

·	To check actual availability of the charts and nautical publications on the ship

*	To make sure that the correction has been made according to the latest issues of NTM and other corrective documents

·	To report to the master of the ship on the state of correction of the charts and nautical publications

·	To check the availability on the ship of the corrective material, the registration log and the file of navigational information received

·	To become familiar with the previous acceptance reports

4-10	All remarks on the state of records, reporting, storage, correction of charts and nautical publications and also all infringements revealed during the check shall be reflected in the acceptance report.

4-11	After signing the acceptance report the navigating officer who took over shall bear full responsibility for the charts and nautical publications received and their correction.

4-12	When one master of the ship transfers command over the ship to another master the navigating officer reports to the master in writing on the availability of charts and nautical publications and the state of their correction.

4-13	Once a year a commission appointed by the master shall take stocks of the ship's set of charts, books and nautical publications, making a report, a copy of which shall be addressed to Riga Charts Division Mr. I.Tokarevich

5	CORRECTION OF THE SHIIP'S SET OF NAVIGATIONAL CHARTS AND GUIDES

5.1	Duties and responsibility of the master and navigators

5-1-1	The master of the ship shall

·	Check availability of the corrected navigational charts and nautical publications necessary for the voyage

·	Check availability of corrective documents

*	During the period of sailing exercise control over receiving of navigational information, transmitted by radio, NAVTFX and timely correction of the charts and nautical publications in accordance with it

·	If necessary involve other navigators to assist the navigating officer in correction of the charts and navigational guides.

5-1-2	The navigating officer (third or second mate) is obliged:

To make collection of charts and sailing instructions for the forthcoming voyage; to correct charts and sailing manuals according to the NTM NAVAREA and other navigational information transmitted by the radio; to keep records of the ship's set of charts and nautical publications and corrective documents.

5-1-3	on completion of correction the navigating officer is obliged to inform the ship's navigators about the most important changes in navigational situation, declared in NTM for the anticipated region of sailing.

5-1-4	taking into consideration the importance of information published in the first issues of NTM of Hydrographic Departments of fleets ship's navigators shall study carefully and sign the first issues of N7M and be guided by them in their practical activity.

5-1-5	Having completed the collection of charts and nautical publications as well as their correction the navigating officer is obliged to report to the master on the availability of

*	General charts for the whole region of forthcoming sailing

·	Plotting charts

*	Specific charts and plans of the ports of departure, arrival and planned ports of call

*	All necessary nautical publications and navigational guides

*	All major changes in navigational situation for the region of anticipated sailing

5-2	Chart correction

5-2-1	Sets of charts for the forthcoming voyage shall be corrected on receipt of NTM and other corrective documents.  Their correction shall be completed prior to the ship's sailing.

5-2-2	All other charts of the ship's set shall be corrected on completion of the correction of the set of charts for the Forthcoming voyage.  The ship's set is not subdivided into categories in respect of correction.

5-2-3	To facilitate and to speed up correction it is advisable to use:

Half yearly and annual Cumulative lists of NTM of Russian Federation and schedules to them or annual Cumulative List of Admiralty Notices to Mariners in which the charts and nautical publications are given in the ascending order of their admiralty numbers and the numbers of NTM are indicated according to which they must be corrected.

Weekly chart collection list for the ship's automatically supplied by KELVIN HUGHES where the numbers of notices according to which they must be corrected are marked.

Chart Correction Tracing (supplement to NTM. To the ship's automatically

supplied by KH delivered together with NTM.

5-2-4	Chart correction shall be started with the latest issue of N7M and be made in

descending order of numbers.

5-2-5	Correction shall be made in the following way:

On receipt of NTM all notices according to which the ship's set is to be

corrected shall be entered into Chart Correction Log in red ink

On completion of correction the notice shall be crossed by one line

New data shall be marked on the chart in red ink , the old data marked by dots

or lines shall be crossed out and the texts crossed by a thin line.

According to temporary NTM NAVIP, NAVAREA, NAVTFX the correction of

charts shall be made in the similar way but using an ordinary, black, well

sharpened pencil.

To make it more conspicuous if necessary the place of correction shall be

encircled in pencil and the number of the notice, date and signature of the

person who made the correction shall be written down as well. The chart

number corrected according to this notice, the date and the signature of the

person who made the correction shall be written down on the notice itself.

5-2-6	It is not allowed to mark on the charts any objects or correct the location of

objects marked on the chart according to the coordinates stated in sailing

directions, descriptions of lights and. signs or other nautical publications.

5-2-7	On the completion of correction according to NTM the name and the number

of NTM according to which the corrections on the chart were made shall be

written under the frame in the bottom left comer of the chart the date of the latest NTM issue examined and signature shall be put in the table placed on the free space of the chart.

the sample of inscriptions made during correction is shown in Fig. 1.

5-2-8	The chart correction according to radionavigational reports concerning the

change in navigational situation of the current voyage shall be made by the

watch officer immediately and shall be reported to the master. The navigating

officer shall reexamine the completeness of the correction made. The number

and date of the latest NAVAREA AND NAVTEX shall be indicated in pencil

under the bottom frame of the chart.

5-3	CORRECTION OF THE NAUTICAL PUBLICATIONS

5-3-1	The main scope of work on correction of nautical publications shall be carried

out during the ship's stay in the port.

If the stay in the port is short and it is impossible to make all the correction

prior to the ship's departure for the forthcoming voyage it is allowed to make

it according to the stages of the passage, so that the scope of the correction

made would ensure the passage of the ship for not less than three days.

5-3-2	The correction of the nautical publications shall be made by sticking text -

cuttings from NTM or by hand.

5-3-3	Note on correction shall be made on the correction records list placed in the

beginning of each manual.

The sample of inscriptions made during correction of charts

| NTM issue number |
| --- |
| No | Date | Signature |

Fig.  I

5-4	CONTROL OVER CORRECTION OF THE SHIP'S SET

5-4-1	To ensure control over correction of the ship's set of charts, books and nautical publications all ships of the shipping company shall send to Riga Charts Division the ship's set correction examination report every month in accordance with the form established as at the last day of the month.

5-4-2	If on the ship two charts sets are available - English and Russian, the set being used shall be corrected, but the corrective documents shall be consistently completed for both sets and have no omissions.

ANNEX IV : Company’s Information and Requirements while navigation in special areas

NAVIGATION IN STRAITS

1.1. The Sound, Little and Great Belts

- Navigation in Straits without a pilot's assistance is permitted to the Masters who

are well familiar with the area of sailing and have adequate experience in the ship's navigation.

- Masters having an interval in sailing in straits for 6 months or more shall take a

pilot for the first passage after such interval.

- Navigators newly appointed to the Master's position are obliged to take pilots, irrespective of their work experience on this ship.

Subsequently after the Master has gained adequate sailing experience every specific

-independent passage through straits shall be authorized by safety and quality

assurance department.

1.2.	The Dardanelles and the Bosphore.

In accordance with The Strait of Istambul, Sea of Marmara and the Strait of Canakkale Routening Guide, approved by the Maritime Safety Committee at 63rd Session in May, 1994 the Masters of foreign ships are strictly recommended to use pilot services in the Bosphorus and Dardanelles straits.  LSC firmly confirms that the compliance with these requirements is compulsory for the Masters.

2.	PASSAGE THROUGH THE KIEL CANAL

Passage planning, through the Kiel canal is carried out by Tanker, Dry Cargo and Reefer Fleet Departments . If the Master considers it reasonable in a given voyage to sail through the Kiel Canal due to sea and weather conditions the Master shall agree his intentions with the relevant and appropriate shipping company's departments.

The passage through the Kiel Canal is prohibited if any faults have been found on the ship which restrict the ship's manoeuvrability, so safety of passage cannot be assured and the Kiel Canal requirements and regulations are not compiled with.

3.	NAVIGATION IN ICE

When sailing to ports closed by ice it is not advisable to enter the ice area before receiving the appropriate instructions from the ice-breaker, Harbour Master or the relevant ice information service of the coastal state.

- In heavy ice conditions in the Baltic straits the management of the Shipping, company may take the decision prohibiting navigation in straits without pilotage, as ice-breakers render assistance in the first place to the ships having a pilot on board.

4.	NAVIGATION IN TERRITORIAL WATERS AND SPECIAL AREAS

The Master shall be confident that he has studied all regulations about sailing in territorial waters of the relevant state whose territorial waters the ship will pass.

- Any ship's stop in territorial waters, if it is not connected with the ship's call to the port of destination or with an emergency aboard ship, is prohibited ( for example: for carrying out drills).

- If the ship is stopped in territorial waters due to sea and weather conditions, accident aboard ship or entrance to territorial waters for rendering assistance to another ship, it is necessary to obtain permission of the appropriate authorities of

the coastal state.

- Entrance to the restricted areas and staying there is prohibited.  Passage through the restricted areas is permitted by definite fair-ways and under pilotage,.

5.	BAD SEA STATE AND HEAVY WEATHER CONDITIONS

In case of heavy storm, icing-up, heavy ice the Master's power to take the following decisions is not limited : whether to proceed to the place/port of shelter or to undertake other measures for ensuring safety of the crew, ship/cargo, but he is obliged to inform the shipping company immediately on the following : time, position, speed ship/cargo condition, intended actions aimed at improvement of situation on the ship.

6.	RECOMMENDATIONS FOR SAILING / NAVIGATION

When crossing the ocean and by the route English Channel-Gibraltar it is available to use recommendations and route forecasts of hydro meteorological service of the Republic of Latvia.

Request for service, if possible, is sent 24 hours prior to going out to the ocean to

the address: RIGA, WEATBER.

It should be noted that the service is not free and corresponding accounts when presented are paid by the shipping company.

7.	MASTER'S INSPECTION ROUNDS OF THE SHI[P

To exercise personal control over the state of affairs on the ship and its technical condition, the Master shall make rounds of the ship at least once a week. The fact of the ship rounds shall be registered in the ship's Log Book.

1 STANDING ORDERS FOR DECK OFFICERS IN CHARGE OF A WATCH IN PORT

The following principles and operational guidance should be taken into account by Master and Watchkeeping Officers.

WATCH ARRANGEMENTS

Arrangements for keeping a watch when the ship is in port should

- (a)	ensure the safety of life ship cargo and port ;

- (b)	observe international , national and local rules

- (c)	maintain order and the normal routine of the ship .

The ship's Master should decide the composition and duration of the watch depending on the conditions of mooring, type of the ship and character of duties .

A qualified Deck Officer should be in charge of the watch.

The necessary equipment should be so arranged as to provide for efficient watchkeeping.

TAKING OVER THE WATCH

The Officer of the watch should not hand over the watch to the relieving Officer if he has any reason to believe that the latter is obviously not capable of carrying out his duties effectively, in which case he should notify the Master accordingly .

The relieving Officer should be informed of the following by the officer being relieved

(a)	the depth of water at the berth, ship's draught, the level and time of high and low waters ; fastening of the mooring , arrangement of anchors and the slip of the chain, and other features of mooring important for the safety of the ship ; state of main engines and availability for emergency use ;

(b)	all work to be performed on board the ship , the nature, amount and disposition of cargo loaded or remaining , or any residue on board after unloading the ship

(c)	the level of water in bilges and ballast tanks

(d)	the signals: or lights being exhibited

(e)	the number of crew members required to be on board and the presence of any other persons on board

(f)  the state of fire - fighting appliances

(g)	any special port regulations ;

(h)	the Master's standing and special orders

(i)	the lines of communication that are available between the ship and the dock staff or port authorities in the event of an emergency arising or assistance being required ;

(j)   other circumstances of importance to the safety of the ship and protection of the environment from pollution.

The relieving Officer should satisfy himself that :

(a)	fastenings of moorings or anchor chain are adequate

(b)	the appropriate signals or lights are properly hoisted and exhibited

(c)	safely measures and fire protection regulations are being maintained

(d)	he is aware of the nature of any hazardous or dangerous cargo being loaded or discharged and the appropriate action in the event of any spillage or fire

(e)	no external conditions or circumstances imperil the ship and that his own ship does not imperil others .

If , at the moment of handing over the watch , an important operation is being, performed it should be concluded by the Officer being relieved , except when ordered otherwise by the Master.

KEEPING A WATCH

The Officer of the watch should:

(a)	make rounds to inspect the ship at appropriate intervals

(b)	pay particular attention to :

(i)	the condition and fastening of the gangway, anchor chain or moorings, especially at the turn of the tide or in berths with a large rise and fall and if necessary, take measures to ensure that they are in normal working condition;

(ii)	the draught , underkeel clearance and the state of the ship to avoid dangerous listing or trim during cargo handling or ballasting

(iii)	the state of the weather and sea;

(iv)	observance of all regulations concerning safety precautions and fire protection ;

(v)	water level in bilges and tanks

(vi)	all persons on board and their location , especially those in remote or enclosed spaces ;

(vii)	the exhibition of any signals or lights

(c)	in bad weather , or on receiving a storm warning , take the necessary measures to protect the ship , personnel and cargo ;

(d)	take every precaution to prevent pollution of the environment by his own ship ;

(e)	in an emergency threatening the safety of the ship , raise the alarm, inform the Master, take all possible measures to prevent any damage to the ship and, if necessary, request assistance from the shore authorities or neighbouring ship ;

(f)   be aware of the state of stability so that , in the event of fire , the shore fire-fighting authority may be advised of the approximate quantity of water that can be pumped on board without endangering the ship

(g)	offer assistance to ships or persons in distress ;

(h)	take necessary precautions to prevent accidents or damage when propellers are to be turned ;

(i)     enter in the appropriate log-book all important events affecting the ship

H.	STANDING ORDERS FOR OFFICERS IN CHARGE

OF NAVIGATIONAL WATCH

GENERAL

The officer of the watch is the master's representative and his primary responsibility at all times is the safe navigation of the ship.  He should at all times comply with the applicable regulations for preventing collisions at sea.

It is of special importance that at all times the officer of the watch may visit the chart room, when essential, for a short period for the necessary performance of his navigational duties, but he should previously satisfy himself that it is safe to do so and ensure that an efficient look-out is maintained.

The officer of the watch should bear in mind that the engines are at his disposal and he should not hesitate to use them in case of need.  However , timely notice of intended variation., of engine speed should be given where possible.  He should also know the handling characteristics of his ship, including its stopping distance, and should appreciate that other ships may have different handling characteristics.

The officer of the watch should also bear in mind that the sound signalling apparatus is at his disposal and he should not hesitate to use it in accordance with the applicable regulations for preventing collisions at sea.

TAKING OVER THE NAVIGATIONAL WATCH

The relieving officer of the watch should ensure that members of his watch are fully capable of performing their duties, particularly as regards their adjustment to night vision.

The relieving officer should not take over the watch until his vision is fully adjusted to the light conditions and he has personally satisfied himself regarding:

(a)	standing orders and other special instructions of the master relating to navigation of the ship;

(b)	position, course, speed and draught of the ship;

(c)	prevailing and predicted tides, currents, weather, visibility and the effect of these factors upon course and speed;

(d)	navigational situation, including but not limited to the following:

(i)	operational condition of all navigational and safety equipment being used or likely to be used during the watch;

(ii)	errors of gyro and magnetic compasses-,

(iii)	presence and movement of ships in sight or known to be in the vicinity-

(iv)	conditions and hazards likely to be encountered during his watch;

(v)	possible effects of heel, trim water density and squat on underkeel clearance.

If at the time the officer of the watch is to be relieved a manoeuvre or other action to avoid any hazard is taking place, the relief of the officer should be deferred until such action has been completed.

WATCH ARRANGEMENTS

(a)	The composition of the watch shall at all times be adequate and appropriate to the prevailing circumstances and conditions and shall take into account the need for maintaining a proper look-out.

(b)	When deciding the composition of the watch on the bridge which may include appropriate deck ratings, the following factors, inter alia, shall be taken into account

(i)	at no time shall the bridge be left unattended;

(ii)	weather conditions, visibility and whether there is daylight or darkness;

(iii)	proximity of navigational hazards which may make it necessary for the officer in charge of the watch to carry out additional navigational duties;

(iv)	use and operational condition of navigational aids such as radar or electronic position-indicating devices and other equipment affecting the safe navigation of the ship;

(v)	whether the ship is fitted with automatic steering;

(vi)	any unusual demands on the navigational watch that may arise as a result of special operational circumstances.

FITNESS FOR DUTY

The watch system shall be such that the efficiency of watchkeeping officers and watchkeeping ratings is not impaired by fatigue.  Duties shall be so organized that the first watch at the commencement of a voyage and the subsequent relieving watches are sufficiently rested and otherwise fit for duty.

NAVIGATION

(a)	The intended voyage shall be planned in advance taking into consideration all pertinent information and any course laid down shall be checked before the voyage commences.

(b)	During the watch the course steered, position and speed shall be checked at sufficiently frequent intervals, using any available navigational aids necessary, to ensure that the ship follows the planned course.

(c)	The officer of the watch shall have full knowledge of the location and operation of all safety and navigational equipment on board the ship and shall be aware and take account of the operation limitations of such equipment.

(d)	The officer in charge of a navigational watch shall not be assigned or undertake any duties which would interfere with the safe navigation of the ship.

NAVIGATIONAL EQUIPMENT

(a)	The officer of the watch shall make the most effective use of an navigational equipment at his disposal.

(b)	When using radar, the officer of the watch shall bear in mind the necessity to comply at all times with the provisions on the use of radar contained in the applicable regulations for preventing collisions at sea.

(c)	In cases of need the officer of the watch shall not hesitate to use the helm, engines and sound signalling apparatus.

NAVIGATIONAL DUTIES AND RESPONSIBELITIES

(a)	The officer in charge of the watch shall :

(i)	keep his watch on the bridge which he shall in no circumstances leave until properly relieved;

(ii)	continue to be responsible for the safe navigation of the ship, despite the presence of the master on the bridge, until the master informs him specially that he has assumed that responsibility and this is mutually understood-,

(iii)	notify the master when in any doubt as to what action to take in the interest of safety-

(iv)	not hand over the watch to the relieving officer if he has reason to believe that the latter is obviously not capable of carrying out his duties effectively, in which case he shall notify the master accordingly.

(b)	On taking over the watch the relieving officer shall satisfy himself as to the ship's estimated or true position and confirm its intended track, course and speed and shall note any dangers to navigation expected to be encountered during his watch.

(c)	A proper record shall be kept of the movements and activities during the watch relating to the navigation of the ship.

LOOK-OUT

In addition to maintaining a proper look-out for the purpose of fully appraising the situation and the risk of collision, stranding and other dangers to navigation, the duties of the look-out shall include the detection of ships or aircraft in distress, shipwrecked persons, wrecks and debris.  In maintaining a look-out the following shall be observed

(a)	the look-out must be able to give full attention to the keeping of a proper look-out and no other duties shall be undertaken or assigned which could interfere with that task;

(b)	the duties of the look-out and helmsman are separate and the helmsman shall not be considered to be the look-out while steering, except in small ships where an unobstructed all-round view is provided at the steering position and there is no impairment of night vision or other impediment to the keeping of a proper look-out.  The officer in charge of the watch may be the sole look-out in daylight provided that on each such occasion:

(i)	the situation has been carefully assessed and it has been established without doubt that it is safe to do so;

(ii)	full account has been taken of all relevant factors including, but not limited to:

- state of weather,,,

- visibility;

- traffic density;

- proximity of danger to navigation;

- the attention necessary when navigating in or near traffic separation schemes; :

(iii)	assistance is immediately available to be summoned to the bridge when any

change in the situation so requires.

PROTECTION OF THE MARINE ENVIRONMENT

The master and officer in charge of the watch shall be aware of the serious effects of operational or accidental pollution of the marine environment and shall take all possible precautions to prevent such pollution particularly within the framework of relevant international and port regulations.

This Recommendation contains operational guidance of general application for officers in charge of a navigational watch, which masters are expected to supplement as appropriate.  It is essential that officers of the watch appreciate that the efficient performance of their duties is necessary in the interests of the safety of life and property at sea and the prevention of pollution of the marine environment.

PERIODIC CHECKS OF NAVIGATIONAL EQUIPMENT

Operational tests of shipboard navigational equipment should be carried out at sea as frequently as practicable and as circumstances permit, in particular when hazardous conditions affecting navigation are expected; where appropriate these tests should be recorded.

The officer of the watch should make regular checks to ensure that

(a)	the helmsman or the automatic pilot is steering the correct course;

(b)	the standard compass error is determined at least once a watch and, when possible,

after any major alteration of course; the standard and gyro compasses are frequently compared and repeaters are synchronized with their master compass;

(c)	the automatic pilot is tested manually at least once a watch;

(d)	the navigation and signal lights and other navigational equipment are functioning

properly.

The echo-sounder is a valuable navigational aid and should be used whenever appropriate.

AUTOMATIC PILOT

The officer of the watch should bear in mind the necessity to comply at all times with the requirements of Regulation 19 Chapter V of the International Convention for the Safety of Life at Sea, 1974.  He should take into account the need to station the helmsman and to put the steering into manual control in-good time to allow any potentially hazardous situation to be dealt with in a safe manner.  With a ship under automatic steering it is highly dangerous to allow a situation to develop to the point where the officer of the watch is without assistance and has to break the continuity of the look-out in order to take emergency action.  The changeover from automatic to manual steering and vice versa should be made by, or under the supervision of a responsible officer.

ELECTRONIC NAVIGATIONAL AIDS

The officer of the watch should be thoroughly familiar with the use of electronic navigational aids carried, including their capabilities and limitations.

RADAR

The officer of the watch should use the radar when appropriate and whenever restricted visibility is encountered or expected, and at all times in congested waters having due regard to its limitations.

Whenever radar is in use, the officer of the watch should select an appropriate range scale, observe the display carefully and plot effectively.

The officer of the watch should ensure that range scales employed are changed at sufficiently frequent intervals so that echoes are detected as early as possible.

It should be born in mind that small or poor echoes may escape detection.

The officer of the watch should ensure that plotting or systematic analysis is commenced in ample time.

In clear weather, whenever possible, the officer of the watch should carry out radar practice.

NAVIGATION IN COASTAL WATERS

The largest scale chart on board, suitable for the area and corrected with the latest available information, should be used.  Fixes should be taken at frequent intervals, whenever circumstances allow, fixing should be carried out by more that one method.

The officer of the watch should positively identify all relevant navigation marks.

CLEAR WEATHER

The officer of the watch should take frequent and accurate compass bearings of approaching ships as a means of early detection of risk of collision; such risk may sometimes exist even when an appreciable bearing change is evident, particularly when approaching a very large ship or a tow or when approaching a ship at close range.  He should also take early and positive action in compliance with the applicable regulations for preventing collisions at sea and subsequently check that such action is having the desired effect.

RESTRICTED VISIBILITY

When restricted visibility/,is encountered or expected, the first responsibility of the officer of the watch is to comply with the relevant rules of the applicable regulations for preventing

collisions at sea, with particular regard to the sounding of fog signals, proceeding at a safe speed and having the engines ready for immediate manoeuvres.  In addition, he should:

(a)	inform the master;

(b)	post a proper look-out and helmsman and, in congested waters, revert to hand

steering immediately;

(c)	exhibit navigation lights;

(d)	operate and use that radar.

It is important that the officer of the watch should know the handling characteristics of his ship, including its stopping distance, and should appreciate that other ships may have different handling characteristics.

CALLING THE MASTER

The officer of the watch should notify the master immediately in the following circumstances:

(a)	if restricted visibility is encountered or expected-,

(b)	if the traffic conditions or the movements of other ships are causing concern-,

(c)	if difficulty is experienced in maintaining course;

(d)	on failure to sight land, a navigation mark or to obtain sounding by the expected

time;

(e)	if, unexpectedly, land or navigational mark is sighted or change in sounding occurs;

(f)	on the breakdown of the engines, steering gear or any essential navigational

equipment;

(g)	in heavy weather if any doubt about the possibility of weather damage;

(h)	if the ship meets any hazard to navigation, such as ice or derelicts;

(i)	in any other emergency or situation in which he is in any doubt.

Despite the requirement to notify the master immediately in the foregoing circumstances, the officer of the watch should in addition not hesitate to take immediate action for the safety of the ship, where circumstances so require.

WATCHKEEPING PERSONNEL

The officer of the watch should give watchkeeping personnel all appropriate instructions and information which will ensure the keeping of a safe watch including an appropriate look-out.

SHIP AT ANCHOR

-In all circumstances, while at anchor, the officer of the watch should

(a) determine and plot ship's position on the appropriate chart as soon as practicable;

when circumstances permit, check at sufficiently frequent intervals whether the ship is

remaining securely at anchor by taking bearings of fixed navigation marks or readily identifiable shore objects;

(b)	ensure that an efficient look-out is maintained;

(c)	ensure that an inspection rounds of the ship are made periodically;

(d)	observe meteorological and tidal conditions and the state of the sea;

(e)	notify the master and undertake all necessary measures if the ship drags anchor;

(f)	ensure that the state of readiness of the main engines and other machinery is in

accordance with the master's instructions;

(g)	if visibility deteriorates, notify the master and comply with the applicable regulations for preventing collisions at sea;

(h)	ensure that the ship exhibits the appropriate lights and shapes and that appropriate sound signals are made at all times, as required;

(i)	take measures to protect the environment from pollution by the ship and comply with applicable pollution regulations.

ANNEX VIII: Sailing in heavy weather

Having received gale warning the following should be taken into consideration:

-	seaworthiness of the ship having regard to cargo character, location and fastening;

-	safe operation of the main engine;

-	fuel reserve;

-	ship's position and course with regard to stormy area;

-	navigational dangers in the area;

-	location of shelters - ports and safe anchorages on the ship's course.

1.	Preparation of the ship

·	1.      Inform the crew.

.2	Fasten ship's equipment.

.3	Check and if necessary strengthen cargo fastenings.

.4	Check safe and hermetic sealing of holds, watertight closings, sounding tube plugs, working condition of return valves, if possible put blinds on ventilation ducts.

.5	Fit storm pendants.

.6	Check ship's stability In case of necessity make ballasting/ reballasting to avoid free surfaces in tanks.

2.	Sailing in stormy conditions:

1	Take regular weather forecasts.

2.     Keep systematic look-out of the actual meteorological situation, length, height, wave frequency, and direction.  See to the ship's avoiding dangerous rolling and pitching.

.3	See to the water level in bil2es and drain them regularly.

.4	Daily check cargo fastenings, make refastening and change the damaged fastenings.

.5	See to the regime of liquid stores consumption, avoid free surfaces in more than one tank at a time.

.6	Regularly check metacentric height regarding rolling frequency. Take notice, that preciseness of this method is considerably reduced if metacentric height is less than 0,2m and there are large free surfaces of liquid cargoes.

.7	Prior to course and/or speed change check if the ship's position as a result of such manoeuvre may be changed for the worse.  Bear in mind that course alteration on the wave may result in considerable list.

8	Take into consideration that water on deck- reduces stability.

.9	During the work on the open spaces instruct personnel accordingly and strictly. comply with safe operation requirements.

3.	Case of emergency - constant list

I	In case of emergency immediately inform the shipowner.  Remember, let the alarm be unnecessary or premature than delayed.

,2	Unsymmetrical rolling is the evidence of constant list.

.3	Prior to any concrete steps with regard to equalization - state the reason of constant list !!!

.4	Prior to equalization upgrade stability using all possible means.

.5	Alter course and change speed so that the ship is in the most favourable situation regarding rolling and pitching.

.6	If possible, turn the ship to the shelters- ports or under the shelter of the coast

.7	In case of small stability reserve do not try to pump liquid cargoes from tanks on one side into tanks on the other side, as it will cause additional free surfaces and reduce stability.  Take ballast not in all tanks at a time but start with those free surfaces in which less influence stability.

8	Taking into consideration concrete situation first test by pressure or drain those tanks which already have free surfaces.

.9	Take ballast as quickly as possible.  Do not stop taking ballast until the tank is full even if at the beginning of this operation the list is increased.

.10	Stop equalization if angle of heel is less than 5 degrees, not to allow the ship to shift on the other side.

4.	Sailing in low temperatures

1.  Watch carefully air and see water temperature, ship's splashes and water freezing on ship's upper deck structures.

.2	In case of danger of being covered with ice Check ship's stability taking into account icing up.

.3	Inform the crew, prepare ice- frighting equipment, check deck lighting.

.4	Choose course and speed to minimize icing up.

.5	Take ice fighting measures without delay: freeing from ice, leaving icing up area or going for the shelter of the coast, etc.  Ice fighting should be made from the beginning and up to the end of icing up.

.6	In the process of freeing from ice first of all free storm ports and upper deck structures, masts and spars. Changing ship's position regarding wind and waves, carry out freeing from ice from the wind side.

.7	Safety rules should be complied with. Crew members working on the open spaces should be dressed in life jackets with safety lines.

.8	Duly inform the shipowner of the ship's condition and all threatening circumstances.

5.    Lying in the port / at the road

Having received gale warning:

. I   Keep main engine in readiness.

.2	Haul and in case of necessity fasten additional mooring lines.

.3	If the wind strengthens stop cargo operations, watch carefully mooring lines, get the ship ready to leave the berth.

.4	Lying at the road the ship shall be ready to heave up anchor in compliance with conditions of the ship's staying, protection and weather forecast. The ship shall heave up anchor and put to sea for storming if her safety can not be guaranteed at the road.

Annex IX : Emergency towage

Ways of emergency towage depend on the type of the tow and the towing vessel, equipment, damages and their scope, weather conditions and area of sailing.

There are two basic types of towage:

-    by a trading vessel

-    by a salvage tugboat.

Specific character of towage by/of a trading vessel is determined by the necessity to install towing equipment if there is no established gear, as well as by a limited availability of means for making a towing line and absence, in many cases, of precise data for calculations required.

Prior to commencement of operations the following should be detailed:

1 .   Methods of fastening the towing, equipment on the tug and the tow.

2.	Methods of towage depending on damages and the type of emergency towing equipment ( fore or aft ) .

3.	Usage of the tug's or the tow's equipment to arrange a towing line.

4.	Methods of passing and taking in of a towing line.

5.	Methods of on-science communications using VHF, lights, sound signals and

flags during the period of operations.

6.	Methods of emergency let go of the towing line.

7.	Towing speed depending on the length and strength of the available towing line and taking into account weather conditions and region of sailing.

8.	Safety measures while passing or fastening the towing line.

9.	Actions of  both ships at commencement of the towage, slackening away or heaving up the towline, at finishing the towage and at the completion of the towage and let go of the tug.

The same things should be defined for towage by a tug boat, but in this event the task is simplified as the tug is provided with an established towage equipment.

Prior to commencement of the operations the staff employed for this purpose on the ship / ships should be instructed in detail on observance of safe working practices.

Directions given by the tug in respect of towage should be immediately carried out by the tow.

During the towage operation the following should be kept in mind:

1	To avoid dangerous tension in the towing line the latter should have a slack equal to the wave height.

2.	Although the stopped propeller increases resistance to movement, the tow keeps the course better.

3.	If possible, the tow should use its own steering gear, otherwise the rudder blade should be put straight.

4.	If the M.E. is operative, it should be used only on the tug's order.

5.	During the towage operation a continuous watch over the towing line should be posted on the ship and means should be provided for emergency let go of the tug.