WALLEM SHIPMANAGEMENT LIMITED

# SAFETY AUDIT AND TRAINING REPORT

M.V.  “ Hai Ji “

MSS Consultant:                  PNJ Cowdell

Date:  From:			 8th November                   To:       11th November 1999

Prepared by:				Marine Safety Services Limited

12 – 20 Camomile Street

London EC3A 7AS.

Telephone:  0171-929-2029

Fax:	        0171-929-1655

Telex:         9312100127

Email:	        Rwc.Mss@btinternet.com.

Project No:

# CONTENTS

## Vessel Details

Executive Summary

Vessel Assessment

SECTION	1	Documentation & Administration

SECTION	2	Bridge Equipment/Procedures

SECTION	3	Radio Equipment

SECTION	4	Accommodation

SECTION	5	Lifesaving Appliances

SECTION	6	Fire Fighting and Emergency Equipment (Deck)

SECTION	7	Deck Equipment and Loadline Items

SECTION	8	N/A Tanker Cargo Handling, Equipment and Procedures.

SECTION	9	Engine Room

SECTION	10	Non Tanker Cargo Handling and Related Equipment and Procedures

SECTION	11	Deficiency List

SECTION	12	Recommendations List

SECTION	13	Instruction and Training Conducted

ADDENDUM          Cargo Loss Prevention

# VESSEL DETAILS

| Name: HAI JI Type: PANAMAX GEARLESS BULKER Built: 1994 GRT: 38639 S.DWT: 70083 BREADTH: 32.2M TOTAL CREW: 20 | Port of Registry: PANAMA Cargo Onboard: PET COKE Date Keel Laid: 4.6.93 Date Last D/D: January 1999 L.O.A.: 225.00M L.B.P.: 215.00M I.M.O. I.D.: 9042233 |
| --- | --- |

|  | Name | Nationality | Certificate | No. | Expiry Date |
| --- | --- | --- | --- | --- | --- |
| Master | Y. TIKHONOV | Russian | Master Endorsements: N/A | O 431324 | 24.4.00 |
| Chief Officer | M. SOLDATENKOV | Ukranian | Master Endorsements: N/A | O430801 | 27.1.00 |
| Ch Engineer | V. MNIKH | Ukranian | Chief Engineer Endorsements: N/A | 431327 | 24.4.00 |
| 1st Engineer | O. AFANESYEV | Ukranian | 2nd Engineer Endorsements: N/A | 430800 | 27.1.00 |

##### EXECUTIVE SUMMARY

The vessel is almost six years old, has been in Management since new.

The organisation of the Bridge, Cargo Operations and Machinery spaces was of a mainly satisfactory standard aided by Company Documentation and check lists.

A few members of Staff were well motivated with a good attitude to the job.

Documentation and administration was generally satisfactory.

Bridge equipment was not up to the usual standard due to problems with radars and the Nor Control system. Hopefully the Technicians will have sorted the faults before the vessel finally sails.

Communication equipment is in good order.

Accommodation is kept clean and tidy

LSA are generally well maintained, but it was noted that 48 monthly lifeboat brake maintenance procedures are incomplete and hazardous.No record was found of the five yearly lifeboat brake test as required by Solas Ch 111 20.11.1 .

FFE is in good order.

Hatch covers appeared to be tight and loadline items are satisfactory.

The engine room maintenance has fallen back due to Staff being on watches.

Cargo operations were well supervised.

A number of minor deficiencies were noted. These will be dealt with as soon as time permits.

A full list appears as Section 11.

A small number of recommendations for the attention of Managers appears as Section 12.

Observations on Cargo Loss Prevention appear as an Addendum.

There was no time avalable for formal training. One brief session was held with the Filipino personnel at which it was established that  the WSM Emergency Organisation was being followed.

Many informal discussions were held with different personnel on various safety aspects.

Date:   11.11.99

##### VESSEL SAFETY ASSESSMENT

| SECTION | NUMBER OF DEFICIENCIES | POINTS TOTAL | CURRENT RATING | PREVIOUS RATING |
| --- | --- | --- | --- | --- |
|  | M | R | D |  |  |  |
| 1. Documentation/Administration |  | 1 |  | 98 | 1.9 |  |
| 2. Bridge Equipment/Procedures |  |  | 2 | 98 | 1.9 |  |
| 3. Radio Equipment. |  |  | 1 | 99 | 2.0 |  |
| 4. Accommodation |  |  | 5 | 95 | 1.9 |  |
| 5. L.S.A. |  | 1 | 1 | 97 | 1.9 |  |
| 6. F.F. & Emergency Equipment (Deck) |  | 1 | 2 | 96 | 1.9 |  |
| 7. Deck Equipment/L.L. Items |  |  | 5 | 95 | 1.9 |  |
| 8. Cargo Handling Equipment, Procedures |  |  |  |  |  |  |
| 9. Engine Room |  | 8 |  | 92 | 1.8 |  |
| 10. Non Tanker Cargo Handling & Related Equipment & Procedures |  |  |  | 100 | 2.0 |  |
| TOTALS |  | 872 | 1.92 |  |

Notes:

1)	Marks are deducted i.a.w. the following table from the maximum figure in each section (100).  The vessel rating figure is the average of all ten sections.

(100 points – rating 2.00, 90 points = rating 1.80, 80 points = rating 1.60).

Deficiency								Marks Deducted

M	Major in nature likely to result in accident or incident.				4

R	Regulatory or Procedural defect or defective item.					2

D	Minor defect or recommendation.							1

2)	The vessel rating may be categorised as follows:-

Rating Achieved						Rated As

> 1.90							Very good/excellent

1.80 – 1.90						Good to very good

1.70 – 1.80						Average to good

1.59 – 1.70						Poor to average

< 1.50							Very poor

SECTION ONE

DOCUMENTATION

|  | REMARKS |
| --- | --- |
| Inspections Port Date Expires Remarks/ Deficiencies National Flag: Ghent 10.11.99 10.11.99 Nil Port State: Qinhuangdao 11.8.99 N/A Nil MARPOL: N/A U.S.C.G. (COFR): 16.2.97 16.2.00 |  |
| 1.01 Certificates Issued Expires Ann Remarks Due 01 International Loadline To be re-issued by NYK 12.11.99 after Class change 02 Safety Construction " " 03 Safety Equipment " " 04 Safety Radio " " 05 International Oil Pollution " " 06 NLS Certificate N/A 07 Int. Tonnage Certificate 13.1.94 08 Safe Manning 28.5.98 09 Shipboard Management (state SBM and/or ISM) 9.12.96 27.9.01 Last 17.5.99 10 U.S. Financial Respons. 16.2.97 16.2.00 | 15 persons ISM |
| 1.02 Service Dates Due Date Remarks 01 Extinguishers (2Y) 5.1.99 02 CO2 System (2Y) 5.1.99 03 Halon System (2Y) N/A 04 CABA Cylinders (5Y) 10.96 05 Foam Analysis (1Y) N/A 06 Medical Locker (1Y) 26.3.98 Replacement items 10.11.99 07 Liferafts (1Y) 4 x 18.12.98 1 x 26.4.99 |  |

SECTION ONE  (Continued)

| 1.03 Manuals/Publications/Log Books etc. Y/N Edition Remarks 01 SEP Manual Y 2 SBM 1,2&3 02 Fleet Standing Instructions 03 Fleet Safety Manual Y Revised '98 04 Navigation Manual Y 05 Technical Manual Y 06 Drugs/Alcohol Policy Manual Y 07 Oil Tanker Operating Manual N/A 08 Specialised Manuals (Heavy Lift, AH etc.) Y Bulk 09 Flag Regulations Y 10 USCG Regs.(CFR 33, 35 & 46) onboard N Met Pubs 515 11 IMDG Code (1994) Y 12 Register for Lifting Appliances up to date (ILO 152) N/A 13 Garbage Disposal Record (required from 1.7.98) Y 14 Official Log and FRE 13 up to date Y 15 Oil Record Books in order and up to date Y 16 Medical Guide (Ship Captains/ WHO) Y Ship Captains 17 Clean Seas Guide (4th edition 1994) N/A 18 Ship to Ship Transfer Guide (Tankers – 1997) N/A 19 ISGOTT (4th edition 1996) N/A 20 Consolidated SOLAS & amendments Y 1997 1998 21 Consolidated MARPOL & amendments Y 1997 22 OCIMF Mooring Equipment Guidelines N/A 23 IMO Routing (6th + 1996 supplements) Y 24 STCW 95 Y 25 Inert Gas Guidelines (1990) N/A 26 Crude Oil Washing (1983) N/A 27 Bridge Procedures Guide (1998) Y 28 International Code of Signals (IMO 1987 (inc. amends. to 1995) Y 1992 edition 29 Prevention of Collision Regs. Y 30 Approved Loading & Damage Stability Data Y 31 Approved COW Manual N/A 32 IG Operations Manual N/A 33 VRP & USCG Approval Letter available N/A 34 Annual review carried out 35 Approved MARPOL Plan available N/A 36 GMDSS handbook (if applicable) Y 37 Recs. for Oil Tanker Manifolds N/A | REMARKS 3 Sets Included in SBM Bridge Procedures M Included in SBM Included in SBM Corr.29.98 on board No amendment |
| --- | --- |

SECTION ONE  (Continued)

|  | REMARKS |
| --- | --- |
| 1.04 Crew Management 01 Manning Complies with Safe Manning Certificate 02 Crew Qualifications adequate for trade of vessel? (STCW A11/4. A111/4) 03 Appropriate for flag? (Lib. Pan. etc.) 04 Random check of medical certificates satisfactory? (ILO 11 47) 05 Junior officers suitably trained/experienced on vessel type? (TASCO/Gas/Chem/FF etc.) 06 Procedures in place for monitoring and controlling work hours? | Yes Yes Yes Yes Yes Yes |
| 1.05 Planned Maintenance System 01 Examine PM records (ISM 10.2.4) 02 Maintenance up to date, including survival craft launching appliances and on-load release gear (if fitted) up to date? (SOLAS III 20.11.1) (Note date last examination and winch test (5Y)) | O.K. No record sighted. Refer to recommendations |
| 1.06 Training & Emergency Drills Record 01 Drill schedule up to date? 02 Personnel Trained for VEC operations? (46 CFR 29.10-11) 03 Personal booklets up to date? (Random sample) | Yes N/A Not sighted |
| 1.07 Accident/Incident Reporting 01 Reports being completed properly? 02 Check medical log for accidents which may not have been reported. | Yes O.K. |
| 1.08 Drug and Alcohol 01 Alcohol record sheets completed and satisfactory? 02 Drug & Alcohol Test Equipment in good order? 03 Calibration kit available and complete? 04 Date last calibrated? 05 Last unannounced alcohol test? 06 Last unannounced drug test? | Bond controlled by Master No expiry date on tubes. 2 year shelf life. N/A N/A 1997 Nil |

SECTION ONE  (Continued)

|  | REMARKS |
| --- | --- |
| 1.09 Other 01 Class quarterly listing available onboard? 02 All items up to date and no conditions listed? 03 DPA identified and known onboard? (ISM 4) 04 Class record complete and detail correct? 05 Language in manuals and drawings appropriate? (SOLAS II-1 26.10 (Applies from 1.7.98) 06 Enclosed spaces identified onboard? | Yes Yes Yes With GL, changed to NKK during Audit Yes Yes |

SECTION TWO

BRIDGE EQUIPMENT/PROCEDURES

|  | REMARKS |
| --- | --- |
| 2.01 Radars 01 Two sets fitted? (SOLAS V 12(h)) (Tankers – vVs>10000, others > 15000 grt) 02 Fully operational? 03 One set 3 cm (9 Ghz)? (SOLAS V 12(g)) 04 ARPA fully operational? 05 Means of pro-active passage plan monitoring available? (Recommended – also to include turns) 06 Type approval label on ARPA? (CFR 33, 164, 38) 07 Gyro/log inputs operational? (CFR 33, 165, 38) 08 Information on Blind Sectors posted? | Yes Service Technician attending to faults Yes Yes Yes Yes Yes No |
| 2.02 Echo Sounder 01 Operational? (Incl. trace recorder) (33 CFR 164, 35) 02 Trace marked with date and time when used? (Starting and stopping) 03 Remote readout available and operational? | Yes No Not fitted |
| 2.03 Speed Log 01 Doppler or electro-magnetic type log 02 Operational? | Doppler Yes |
| 2.04 Instrumentation 01 Rudder angle, RPM and Rate of Turn visible from conning position? (CFR 33, 164, 35) (Rate of Turn only required on v/ls >100000 grt) 02 Displayed on bridge wings? Suez Canal) 03 /GPS/Loran fitted and operational? 04 Course recorder fitted, used and time set to GMT? 05 Quantity and Condition of binoculars? 06 Clearview screens/wipers operational? | Yes, but no ROT fitted Not ROT Yes Yes Satisfactory Yes |

SECTION TWO  (Continued)

|  | REMARKS |
| --- | --- |
| 2.05 Radio Direction Finder 01 Date of last calibration check? (Recommend annual verification by Master) 02 DF log book of check bearings being maintained? (ISM 10.2.4) (min 3 in each quadrant annually) | 25.6.99 Yes |
| 2.06 Standard and Gyro Compasses 01 Standard compass last adjusted? (SOLAS V 12) (Recommend annual verification by Master) 02 Gyro compass last serviced? 03 Errors checked and logged each watch? (STCW AVIII/2 34.2) 04 Illumination adequate? (SOLAS V 12(b)2) 05 Means to take visual bearings available? (Repeaters, azimuth rings, also over reasonable arc of horizon) (SOLAS V 12(b), (d)) 06 Condition of standard compass and fittings | 25.6.99 9.2.96 Compass error lo kept Yes Yes Yes |
| 2.07 Charts, Publications etc. 01 Full Kelvin Hughes package incl. tracings? 02 Notices regularly received? 03 Date and number of last notice received? 04 Number of and date last chart update received? 05 All charts corrected? (ISM 11.1) 06 Chart correction records available? (ISM 10.2.4) 07 Random check charts against Cumulative Notice satisfactory? 08 T&P file kept? 09 Nav. Warning file kept? 10 Sailing Directions Corrections file kept? 11 Publications, Light Lists etc. corrected? 12 Full set publications as per Chart Index? (ISM 11.1) 13 Charts/publications index corrected? | Yes Yes 35/99 277693 12.3.99 Yes Yes Yes Yes Yes Yes Yes Yes Yes |
| 2.08 Accident/Incident Reporting Passage Planning 01 Practised to Company standard? (ISM 7) 02 Forms used and kept on file? 03 Planning check list used? 04 Frequency of position fixing during arrival and pilotage adequate? (STCW AVIII/2/98) 05 Pilot information card available? | Yes Yes Yes Yes Yes |

SECTION TWO  (Continued)

|  | REMARKS |
| --- | --- |
| 2.09 Master’s Standing Orders 01 Daily order book in use and signed? (ICS BPG 1.1.3) 02 Copy of Company Standing Orders attached? 03 Master’s personal Standing Orders attached? 04 Orders signed by Master and all Deck Officers? 05 Bridge resource management policy and procedures in place? (33 CFR 157.415) (Required on single hulled vessels, recommended on others) | Restricted to Night Orders No, posted Yes Yes N/A |
| 2.10 Steering Gear 01 Is block diagram posted? (SOLAS V 19-2(c)) 02 Is steering gear changeover procedures posted? (CFR 33 164.35(k)) 03 Off course alarm tested and operational and officers familiar with operation? (ISM 10.2.1. SOLAS V 19-2(c)) 04 Steering gear manual override alarm fitted and operational? (33 CFR 157.440) (Required on single hulled vessels) | Yes Yes Reported operational No |
| 2.11 Manoeuvring Characteristics 01 Are these posted and understandable? 02 In USCG or IMO format? (CFR 33 164.35) 03 Manoeuvring Booklet available? (Recommended) (SOLAS II-1 28.3 IMO Res. A601(15)) 04 Class Flag letter of completion available? (33 CFR FR 157.445) (Single hulled tankers) | Yes USCG No N/A |
| 2.12 Sextants 01 Number? 02 Condition? | 2 Good |
| 2.13 Chronometers 01 Rate Book kept? (ISM 10.2.4) 02 Daily entries? | Yes Yes |

SECTION TWO (Continued)

|  | REMARKS |
| --- | --- |
| 2.14 Muster Lists 01 Comply with SOLAS III Reg 53? (SOLAS III 8) | Yes |
| 2.15 Pyrotechnics Enter expiry dates for bridge items (SOLAS III 6.3, 18) 01 Rocket Line (minimum 4 units) 02 Parachute Rockets (minimum 12) | 5.02 10.01 |
| 2.16 Man Overboard Lifebuoys 01 Correctly rigged and capable of quick release? (SOLAS III 7.1.3) 02 Lifebuoys of adequate mass? (at least 4kg) 03 Lanyard connecting buoy to signal 4km long? 04 Release gear free? Note expiry dates for light/smoke units 05 Port 06 Starboard | Yes Yes No Yes 9.01 11.00 |
| 2.17 Lifejackets 01 Sufficient number on bridge? (Min 3) 02 Location marked by IMO signs? (SOLAS III 7 2.2) | Yes Yes |
| 2.18 Fire Detection System 01 Operational? Areas protected? 02 Tested weekly? 03 Method of isolating loops fitted? 04 Instructions on the procedure for isolating loops posted and understood? (Recommended) 05 Records of testing available? (ISM 10.2.4) | Yes ER, Steering Gear, Accommodation alleyways Yes Yes No instructions Yes |

SECTION TWO  (Continued)

|  | REMARKS |
| --- | --- |
| 2.19 Deck Log 01 Boat/fire drills held? (weekly on Liberian vessels) 02 Bridge Movement Book (Bell Book) kept in ball- point? (ISM 10.2.4) 03 All sections of log completed and up to date? 04 Standard of entries (Inc. CFR entries) Log entries made: 05 Entries for radar operation? 06 Entries for use of check lists (SEP)? 07 Entry for manual steering test each watch? (STCW AVIII/2 34.3) (if not included in check list) Note Dates: 08 Last fire drill? 09 Last boat drill? 10 Lifeboats last in water (SOLAS III 19.3.3.3)? 11 Rescue boats last in water (SOLAS III 19.3.3.3.)? 12 Last spill pollution exercise? | Yes Yes Yes Generally good. Master taking con to be added. In radar log Yes In check list 6.11.99 23.10.99 Port 10.11.99 St.5.8.99 N/A 23.10.99 |
| 2.20 Garbage Disposal 01 Garbage Disposal Log maintained and satisfactory? (MARPOL Ann V 9.3 (Now IMO format), ISM 10.2.4) 02 Method of Plastics Disposal (Shore/Incinerator)? 03 If shore – receipts available? 04 If incinerator – Method of plastic ash disposal? 05 Garbage disposal prohibition notices posted? (MARPOL Annex V 9.1 & USCG) 06 Waste management plan in effect? (MARPOL Ann V 9.2) | Yes Shore when possible, or incinerator. Yes Retained on board Yes Yes |
| 2.21 Contingency Planning 01 SOPEP Manual on bridge? 02 Copies of ship’s plans available? 03 Information file on towing equipment available? MSC 35(63), SOLAS II-1 3-4 (inc. deployment instructions for ETA) (Recommended) 04 Documentation correct including contact list? 05 Senior officers received training in oil spill mitigation? (SOPEP 5.7) | Yes Yes N/A Yes Nos. |
| 2.22 Fire Control Plans 01 Available on bridge? (Recommended) 02 IMO type symbols used? (IMO Res A654(16)) | No Yes. Plans being upgraded to NKK standard during Audit. |

SECTION TWO  (Continued)

|  | REMARKS |
| --- | --- |
| 2.23 Other 01 Rescue Signal Table displayed? (SOLAS No. 1 poster) (SOLAS V 16) 02 2 means of communication with ER? (SOLAS II- 1) 03 IG pressure indicator operational? 04 Permit to work file maintained containing copies of permits issued? (Tankers – ISGOTT 2.8.1 & 11.6.1, LPG – TSG 3.5.4 LGHP 9.8.1, others – FSI) 05 Permits issued cover hot work, enclosed spaces, electrical, overside and work aloft? 06 Records of daily soundings available? (ISM 10.2.4) 07 Instrument labelling in appropriate language? 08 Safe access within wheelhouse? (No obstructions which may cause injury) 09 Condition of masts, stays and fittings? 10 Wheelhouse visibility (SOLAS V 22) (Applies to vessels built after 1.7.98 and as far as practicable on existing ships). | Yes No Yes N/A Yes Yes No Yes Yes Yes Good Good |

SECTION THREE

RADIO EQUIPMENT

|  | REMARKS |
| --- | --- |
| 3.01 GMDSS OR SOLAS 01 Vessel complies with GMDSS or SOLAS requirements? (Must be GMDSS by 1.2.99) If GMDSS is method of compliance on maintenance (SOLAS IV (15.6/7):- 02 a) Shore based maintenance contract 03 b) Duplication of equipment 04 c) Onboard maintenance (V/ls operation in areas A1 & A2 may use combination V/ls operation in areas A3 & A4 must use combination of at least two of the above methods) | GMDSS Yes Yes No |
| 3.02 Main Aerials 01 Grounded during cargo operations? (Tankers – ISGOTT 4.11.2, LPG – TSG 3.5.3) 02 Warning notice on above displayed? | N/A Yes |
| 3.03 Emergency TX/RX Auto Key 01 Are instructions for operation clearly posted? (OCIMF Check List Section 13) | N/A |
| 3.04 Lifeboat Radio (If Carried) 01 Is equipment tested weekly? (86 SOLAS IV 13(j), ISM (10.2.1) 02 Date of last test? (86 SOLAS IV 13 & 14) | N/A N/A |
| 3.05 Communications Systems Fitted 01 Satcom? (SOLAS IV 7.1.5) 02 MF/HF telex? 03 Fax? 04 Weatherfax? (Recommended) 05 2 VHF sets with USCG Ch 22A and one set from emergency supply and DSC fitted? 06 Navtex fitted? (SOLAS IV 1.4) 07 All equipment in good order? | Yes Yes Yes Yes Yes Yes Yes |

SECTION THREE  (Continued)

|  | REMARKS |
| --- | --- |
| 3.06 Walkie Talkies 01 Min 3 survival craft? (SOLAS III 6.2.1.1) 02 Sets used for emergencies only? 03 Expiry date of batteries? (if applicable) 04 Sets highly visible and watertight? (IMO Res 605(15)) 05 Channel 16 fitted plus one other? 06 Number of other sets onboard? 07 Sets intrinsically safe with approval label showing US cargo classifications or alternative approval? (Tankers – 46 CFR 110.15, 111.80) (for sets in every day use) | Yes Yes 1.02 Yes Yes 4 No |
| 3.07 Radio Log (ISM 10.2.4) 01 Routine entries regarding weekly testing of walkie talkies and lifeboat radio and inspection of EPIRBs, SART’s vertified? (SOLAS IV 17, ISM 10.2.1) 02 Monthly tests of EPIRB and SARTs carried out? (Recommended) 03 Date last check of radio batteries entered in log? 04 Recorded battery densities sighted? 05 Charged daily? (SOLAS IV 13) | Yes Yes 6.11.99 No Auto mode |
| 3.08 Radio Notices 01 Radio Signals publications up to date and corrected? (ISM 11.1) | Yes |
| 3.09 Lifejacket 01 Available to Radio Officer? 02 Location marked by IMO sign? (SOLAS III 7.2.2) | N/A N/A |
| 3.10 Emergency Radio Batteries 01 Fully charged & SG checked weekly? (SOLAS IV 13) 02 Suitable hydrometer for battery type available? 03 Goggles and gloves in locker? (COSWP 24.2.2) 04 Eyewash bottle in locker? (COSWP) 05 “No Smoking” notice posted in locker? (COSWP) 06 Condition of battery locker including fire flaps? (should only be one battery type in locker) (COSWP 24.1.17) | Yes Yes Yes No Yes Good, but two types of battery present. |

SECTION THREE  (Continued)

|  | REMARKS |
| --- | --- |
| 3.11 Aerials Condition 01 Are aerials and insulators in good condition? 02 Are aerials rigged out of reach and/or safety screens fitted around aerials? (COSWP 23.1.8) 03 Satcom dome radiation zone marked? (Usually 3 metre zone) | Yes Yes No |
| 3.12 EPIRBs 01 Float free satellite unit? (SOLAS IV 7.1.6) 02 Battery/hydrostatic release expiry dates? 03 Condition of EPIRB and HRU? | Yes Battery 9.00 HR.U 12.00 Tested operational |
| 3.13 SARTs 01 Minimum 1 each side of vessel? (If fitted in survival craft must be 1 for each survival craft except for’d liferaft) 02 Condition of SART? 03 Note expiry dates for SARTs batteries. | Yes Good 5.02 |

SECTION FOUR

ACCOMMODATION

|  | REMARKS |
| --- | --- |
| 4.01 Muster Lists 01 Comply with SOLAS III Reg 37? 02 Sufficient number displayed? (SOLAS III 8) 03 Emergency muster information displayed for shore officials? (Clear sign posted giving instructions and emergency signals etc.) | Yes Yes No |
| 4.02 Training Manual 01 Located in each messroom/recreation room or in each cabin? 02 Comply with SOLAS III 51? 03 Contents ship specific? (ISM 6.3-6.5) (Inc. GMDSS equipment) | Messrooms Yes Yes |
| 4.03 Fire Hoses 01 General condition, including gaskets and hose bindings? 02 Wheel key present? 03 Nozzles present and in good condition? 04 Nozzles jet/spray type? (SOLAS II-2-4.8) (All v/l’s after 1986 strong preference on older vessels) | Satisfactory Yes Yes Not all |
| 4.04 Fire Extinguishers 01 Locations and extinguishers numbered? 02 Date last checked onboard (by ship staff) 03 Date pressure tested ashore? (ISM 10.2.1) (4Y) 04 Instructions in appropriate language? (English or crew language) 05 Ship’s PM tag attached? 06 Are extinguishers colour coded? (on new ships must be red but 10% of surface must be coded for medium, some companies use coloured labels, on existing ships extinguishers to be changed to red as pressure tested) | Yes 10.99 2.93 when new Yes Yes Yes |

SECTION FOUR  (Continued)

|  | REMARKS |
| --- | --- |
| 4.05 Fire Control & LSA 01 On display? (SOLAS II-2, MSC/Circ 451) 02 Is drawing of fire main on display? 03 Plans legible and detail correct? 04 Are plans/changes class approved? 05 Fire plan symbols in IMO format? (IMO Res. A654(16) | Yes Yes Being modified Yes Yes |
| 4.06 Exits 01 Clearly marked with luminous IMO type signs? 02 Direction arrows or arrow type used to mark routes? | No Yes |
| 4.07 Fire Doors 01 Manual or Magnetic release? 02 All doors closed? (not wedged or tied back) 03 Are doors free from home made hooks? (SOLAS II-2 47.2) 04 Are door closers operating correctly? | Manual Yes Yes Yes |
| 4.08 Hospital/Medical Locker (ILO Art 14) 01 Condition/appearance? 02 Are scupper clear and toilet/sink water traps full? 03 Medical log kept and up to date? (ISM 10.2.4) 04 Stretchers suitable for enclosed space rescue available? 05 Oxygen resuscitator available? (LPG – IGC 14.3.2, Others – Medical scales) 06 Personnel trained in the use of resuscitator? 07 Cylinders full, spares? 08 Pressure test date of cylinders (5Y)? | Good & clean Yes Yes Yes Yes 2/0 yes 170/200 full x1 cylinder no spare 2.92. Aluminium cylinder, due test before refill |
| 4.09 Galley/Storerooms 01 Condition, Cleanliness including tiling/flooring? 02 Exhaust vents/grids clean and intact (Tankers – ISGOTT 2.3)? 03 Deep fat fryers fitted with safety covers and unplugged? (COSWP 25.1.12) 04 Stocked medical kit available? 05 Free of infestation? (if No – state type) | Surface clean. Several tiles detached. Yes Yes Broken plastic box, inadequately stocked. Yes |

SECTION FOUR  (Continued)

|  | REMARKS |
| --- | --- |
| 4.09 Continued 06 Galley food storage satisfactory? 07 Paper bags used for collecting garbage? 08 Garbage segregation satisfactory? 09 “No Smoking” sign displayed and policy enforced? 10 Fire blanket available in galley? (Tankers – ISGOTT 2.3) 11 Galley windows and external door closed? 12 Work surfaces, storerooms/handling areas clean and tidy? 13 Galley staff wearing appropriate protective c clothing? 14 Fixed FE system fitted to galley range vent trunking (SOLAS II-2 15.6, KL>7/86) (Where trunking passes through accommodation spaces – does not apply for pre 7/86 vessels) | Yes Yes Yes Yes Yes Yes Yes Yes No. Foam to range. |
| 4.10 Internal Accommodation Fire Dampers 01 Operation frequency? 02 Condition? 03 Clearly marked? | ? Satisfactory Yes |
| 4.11 Lifts (If fitted) 01 Signs displayed outside each lift entrance warning against using lift during emergency? 02 Certificate of test on display in lift? 03 Date last tested? (Recommend 2Y or D/D) 04 Machinery guarded? | N/A |
| 4.12 Accommodation Doors/Windows 01 All ports and doors closed? (ISGOTT 6.1.2) 02 Closure satisfactory and all dogs fitted and free? 03 Condition of door seals? 04 Sign displayed at doors “To be kept closed during cargo operations”? 05 Accommodation free of jury rigged radio aerials? 06 Air lock alarms operational? (if fitted) 07 ER hatch closed? | N/A Yes Good N/A Yes N/A N/A |
| 4.13 Alleyway Access and Lighting 01 Lighting adequate? 02 Fittings in good condition? 03 Safe access within accommodation spaces? (Condition of decks etc) (COSWP 9.2.1) | Yes Yes Yes |

SECTION FOUR  (Continued)

|  | REMARKS |
| --- | --- |
| 4.14 Smoking Restrictions 01 Are Company and Port smoking regulations being complied with? 02 Are these posted and understood? (Recommended) 03 Designated smoking areas identified (Tankers – ISGOTT 4.8.2, LPG – TSG 3.5) 04 Doors and ports in smoking areas closed? (Recommended doors fitted with self-closers if not already) 05 Only safety (self extinguishing) ashtrays in use? use? | N/A No N/A No No |
| 4.15 Muster Stations 01 Adequately marked/signposted? | Yes |
| 4.16 A/C System 01 Can intakes be sealed? 02 Do flaps close properly? | Yes Yes |
| 4.17 Emergency Stops 01 Locations of groups of switches? 02 Frequency of testing? 03 Clearly labelled? | Fire station Three monthly Yes |
| 4.18 Other 01 Are copies of Officers’ licences displayed? (Liberian flag MR 10.293) 02 Company Safety & Environmental Policy displayed? (ISM 2.1, 2.2) 03 Copies of Statutory Certificates displayed? (SOLAS 1 Reg 16) 04 Notice displayed warning against use of mobile phones, pagers, cameras etc outside the accommodation? (In accomm. & at gangway) (Tankers – ISGOTT 4.10.2, LPG – TSF 2.5.2) 05 Condition of sanitary facilities in accommodation? 06 Condition of service spaces? | N/A No No N/A Mainly satisfactory Good and clean |

SECTION FIVE

LIFESAVING APPLIANCES

|  | REMARKS |
| --- | --- |
| 5.01 Lifeboats 01 Launch instructions posted adjacent and easily seen in emergency lighting (SOLAS III 9.2.2) 02 Lighting of launch area satisfactory? 03 Exterior free of cracks or damage? 04 External fittings in good condition? (including bowsing tackle if applicable) 05 Tricing pennants rigged correctly? (if applicable) 06 Remote release wire free of flammable materials? Boats with On-Load/Free Fall Release Gear 07 Release gear set properly? 08 Clear instructions posted? 09 Maintenance requirements known and carried out correctly? (Incl records) (SOLAS III 20.11) 10 Engine tested weekly? (ISM 10.2.1) 11 Waterproof starting/operating instructions posted nearby? 12 Fuel tanks full? 13 Plugs clearly indicated inside boat? 14 Reflective marking tape fitted? 15 Seat markings? 16 Seat belt fittings in good condition? (All, not just ones n way of hatches) 17 Cleanliness? 18 Water replaced regularly? 19 All equipment/small gear correct? (ISM 10.2.1) 20 Number and call sign marked on canopy? 21 Embarkation ladders condition? 22 Lifeboat engines operational? (ISM 8) 23 Mountings for SARTs in lifeboats 1m above water level? (IMO Res A697(17)) Note Expiry Dates 24 Medical kits 25 Food packs 26 Water packs 27 Hand flares 28 Parachute rockets 29 Smoke floats | Yes Yes Yes Yes N/A No Yes Yes Yes Yes Yes Yes Yes Yes Yes Yes Good Yes Yes Yes Satisfactory Yes, after charging starb lifeboat battery Yes 6.02 4.02 N/A Water changed 9.99 P 10.01 S 4.02 P 2.03 S 10.01 P & S 10.01 |

SECTION FIVE  (Continued)

|  | REMARKS |
| --- | --- |
| 5.02 Lifeboat Air Bottles (If fitted) 01 Operating instructions posted? 02 Lifeboat air bottles full and in good condition? 03 Pressure test date? 04 Air pipework in good condition with no leaks present? 05 Filling hose (high pressure) available? | N/A |
| 5.03 Lifeboat Fire Protection (If fitted) 01 Operating instructions posted? 02 Water sprays last tested? 03 Spray nozzles in good condition? 04 Condition of spray system pipework? | N/A |
| 5.04 Liferafts Inflatable or rigid? 01 Location, condition and capacities? (SOLAS III 31.1.1.2) (Vessel must have sufficient capacity each side for all persons or rafts must be transferable – also rafts must not be obstructed by overhead structure) 02 Launch instructions posted adjacent? (easily visible under emergency lighting) 03 H.R.U. service dates? 04 Rigged correctly? 05 Apparent condition of weak link and H.R.U.? 06 Senhouse slip fitted to forward liferaft? (SOLAS III 31.1.4) 07 Boarding line or ladder available for all rafts including fwd liferaft? (SOLAS III 11.7) 08 Lifejackets available for capacity of fwd raft? (SOLAS III 7.2.1.2) (Recommended) | Inflatable 2 x 15 P & S 1 x 6 Forward Yes 18.12.98 Yes Satisfactory Yes Yes Yes |
| 5.05 Rescue Boat 01 Condition? 02 Equipment correct? 03 Sufficient immersion suits for designated complement? (Recommend 4 as minimum complement) | Port lifeboat |

SECTION FIVE  (Continued)

|  | REMARKS |
| --- | --- |
| 5.06 Davits 01 Davits for lifeboats, liferafts (if fitted) and rescue boat free and well maintained? (SOLAS III 20.11.1) 02 Note date falls due reversal? 03 Note date falls due renewal? (SOLAS III 20.4) (If not reversed falls must be inspected periodically and renewed at 4 years max (SOLAS III 20.4.1)) 04 Dates stencilled on/near davits? (Recommended) 05 Davit trips free and in good condition? 06 Condition of wires? 07 Lifeboat lowered to water level? 08 Crew proficient in launching procedures? (also question crew on emergency duties) Boats Fitted with On-Load Release Gear 09 Davits equipped with hanging-off points and suitable pennants available? (SOLAS III 16.2) (Required for some systems) 10 Weight of boat supported only by hooks? | Yes 11.00 5.03 Yes Yes Good Port side 11.11.99. Starbd 25.8.99 Satisfactory No Yes |
| 5.07 Lifebuoys Total number? 01 Sufficient? (8 or as per SOLAS III 7.1, 31.1) 02 Locations as per Class Record? 03 Required attachments correct? 04 Reflective tape? 05 Markings correct? 06 Condition of roping and lights? | 14 Yes Yes Yes Yes Yes. One light to be replaced IWO forecastle |
| 5.08 Lifejackets 01 Condition? 02 Fitted with required attachments? 03 Light batteries in date? (Lights of white colour required from 1.7.98 or when due replacement but before 1.7.01) 04 Children’s sizes? 05 Donning instructions displayed in accommodation alleyways? (SOLAS III 8.4) 06 Locations marked with IMO signs? (SOLAS III 7.2.2) 07 If any inflatable lifejackets onboard are they serviced annually (SOLAS III 19.8) | Good Yes Yes Yes Yes Yes N/A |

SECTION FIVE  (Continued)

|  | REMARKS |
| --- | --- |
| 5.09 Immersion Suits 01 Sufficient number? 02 SOLAS approved? 03 Locations? 04 Condition? 05 Suit zippers adequately lubricated? (Recommended) 06 Last serviced? 07 Service interval? (Maker’s instructions) (At least three per lifeboat, unless fully enclosed boat. One for each person assigned to crew rescue boat, even if fully enclosed but the three per life- boat can be countered for this if carried). (SOLAS III 33) | Three Yes Port lifeboat. Good Yes Not N/A |
| 5.10 Thermal Protective Aids 01 Sufficient number? 02 SOLAS approved? 03 Location? 04 Condition? Ships with open boats: One for each person onboard without an immersion suit, plus in each boat, sufficient for 10% or 2. In each liferaft sufficient for 10% or 2 minimum. Ships with totally enclosed boats: In each boat sufficient for 10% or 2. In each life- raft sufficient for 10% or 2 minimum). (SOLAS III 34). | Yes Yes Three each lifeboat New |
| 5.11 Other Comments Include here general aspects on L.S.A. where additional information can be of interest. | 48 monthly maintenance procedures for opening and overhauling lifeboat winch brakes are incomplete and hazardous. No record of 4 yearly lifeboat brake test in compliance with Solas. Refer to recommendations. |

SECTION SIX

FIREFIGHTING AND EMERGENCY EQUIPMENT (DECK)

|  | REMARKS |
| --- | --- |
| 6.01 Emergency Equipment Stations 01 Location of station(s)? Station 1 02 Station 2 03 Station 3 04 Station 4 05 Equipment listed and present as stated? 06 Condition of space and equipment? 07 Number of complete fireman’s outfits? (B/A set, gloves, helmet, lamp, boots, suit, lifeline, lifeline, axe) (Tankers – SOLAS II-2 17.3.1.2, 4 sets) (Chem – SOLAS II-2 17,4 sets) (Dry – SOLAS II-2 17, 2 sets) (LPG – SOLAS II-2 17, 17.3.2, IGC 11.6) (<5000m3 – 4 sets >50003 – 5 sets) 08 Condition BA sets and outfits? 09 BA sets of positive pressure type? (Tankers – ISGOTT 11.5.2, others – Recommended) 10 Locations widely separated? (SOLAS II-2 17.4) 11 Air bottles fully charged? 12 Anti-sparking covers available for BA set bottles? 13 Sufficient spare bottles onboard? (2 spare bottles per set) 14 Air bottles last pressure tested (5 yearly)? (ISM 10.2.1) 15 Spare face masks onboard? (Recommended 2 for 4+ sets, 1 for 2 sets) | EHQ Upper deck Forecastle Engine Control Room Midship locker Yes Good 4 Good Yes Yes No No Yes 6.96 Nil |
| 6.02 Fixed Gas Flooding Systems 01 Type? 02 Areas protected? 03 Date of last cylinder pressure test? 04 Auto fan trips last tested? 05 Operating instructions posted? | CO2 E.R. 1994 6.11.99 Yes |
| 6.03 Fixed Foam Systems 01 Areas protected? 02 Capacity and type? (Alco Res./Prot./Syn.) 03 Last test of system (i.e. activity test) 04 Last foam analysis? 05 Foam type and capacity stencilled on tank? 06 Date of last foam analysis stencilled on tank? 07 Clear instructions posted, valves marked? | N/A |

SECTION SIX  (Continued)

|  | REMARKS |
| --- | --- |
| 6.04 Other Fixed Fire Extinguishing Systems 01 Types (water mist, dry powder etc.)? 02 Spaces served? 03 Gas propellant cylinders pressure test date? (ISM 10.2.1) 04 Operating instructions posted? | Foam Galley range. 1994 Yes |
| 6.05 Breathing Apparatus Compressor 01 Fitted and operational? (LPG – 46 CFR 154.1415) 02 Connected to emergency power supply? 03 Running hours log maintained? (ISM 10.2.4) 04 Date filter last changed? 05 Spare filter cartridge onboard? 06 Outside air supply to compressor? 07 Relief valve set correctly? 08 Set at bottle working pressures? (Max 10% above working pressures) | Yes Yes No Unknown No Yes Yes 240 bars. |
| 6.06 Other Breathing Equipment 01 Bellows type sets? 02 Airline breathing sets? | N/A |
| 6.07 Fire Hoses/Boxes 01 Condition of hoses, seals, nozzles, bindings etc.? 02 Nozzles jet/spray type? (SOLAS II-2 4.8) 03 Pressure tested annually? 04 Records of testing maintained? (ISM 10.2.4) 05 Condition of box? 06 Unobstructed? 07 Tools available with each hose? (SOLAS II-2 4.7.1) | Satisfactory Yes Yes 3.12.98 Many catches are defunct and are lashed with rope Yes N/A, instantaneous |
| 6.08 Fire Line and Hydrants 01 Are hydrants capped and unobstructed? 02 Are caps easy to remove? 03 Pipework and hydrants free of leaks? 04 Are isolating valves clearly marked and free? 05 Are caps drilled and holes clear? | Yes Yes Yes Yes No |
| 6.09 Foam Hose Stations 01 Locations and type? (Min 4) (SOLAS II-2 61.8) 02 Condition? 03 Hoses pressure tested annually? (ISM 10.2.1) 04 Portable foam containers in good condition? 05 Date last activity test of portable foam? | 1 portable foam applicator EHQ 1 Boiler Good ? Yes ? |

SECTION SIX  (Continued)

|  | REMARKS |
| --- | --- |

| 6.10 Foam Monitors 01 Condition? 02 Valves free? 03 Wheelkey available at each monitor? (Recommended) | N/A |
| --- | --- |
| 6.11 Foam Line and Hydrants 01 Distinguishable and separate from fire line and hydrants? (SOLAS II-2 61.10) 02 Condition? 03 Are isolating valves clearly marked and free? | N/A |
| 6.12 International Shore Connection 01 Number and location? 02 Is location(s) clearly marked at gangway access? 03 Are required fittings present (SOLAS II-2 19)? | One EHQ. One forward No. Yes |
| 6.13 Fire Control Plans 01 External plan containers each side or one portable container? (SOLAS II-2 20.2) 02 Is container(s) easily opened? 03 Are contents in good condition? 04 Is copy of current crew list and cargo plan in container(s)? (Tankers – ISGOTT S/S Check List, SOLAS II-2 20.2, other vessels – recommended). | Yes Yes Yes Yes |
| 6.14 Fire Flaps and Dampers 01 Free? 02 Operated weekly? (ISM 10.2.1) 03 Are open/shut positions clearly marked? 04 Are flaps numbered and labelled for inclusion in “Close Down” plan? 05 Seals in good condition? | Yes Yes Yes Yes Yes |
| 6.15 Spare Charges for all Extinguishers 01 100% minimum 02 1 spare extinguisher for each CO2 onboard? (Up to 10 spares) | Yes No, 8 spares for twelve. Class approved |
| 6.16 Other |  |

SECTION SEVEN

DECK EQUIPMENT AND LOADLINE ITEMS

|  | REMARKS |
| --- | --- |
| 7.01 Anchoring Equipment 01 Anchor chains, pins and swivels in acceptable condition? 02 Windlass brakes in good order? 03 Windlass gear covers fitted and in good condition? 04 Bitter end release arrangements apparently free? 05 Sledge hammer for use in release available? | Yes Yes Yes Yes No |
| 7.02 Mooring Equipment 01 Winch brakes in good order? 02 Winch brakes last tested? (Tankers – ISGOTT 3.55 (1 yearly), others - recommend 2 years) 03 Winch test data available and marked on reels? (Recommend marked on reels) 04 Moorings wound on storage drums correctly? 05 Direction of reeling marked on drums? (Tankers – ISGOTT 3.5.5) 06 Adequate numbers moorings onboard? 07 Moorings in good condition? 08 Are moorings of adequate size for vessel? 09 rope tails and mandal shackles used, or available for use, with mooring wires? 10 Rope tails correct length and size? (11m/+25% MBL) 11 Are moorings on same lead of same material? (wire or ropes) 12 Are moorings turned up properly on bitts? 13 Appropriate stoppers used? (Not single tailed) 14 Are fire wires properly rigged fore and aft? (ISGOTT 3.7.2 & port requirements) 15 Are turns on bitts lashed? 16 Fire wires correct size? <100K dwt:28mm/45m, 100 – 300K dwt: 38mm/60m 17 Vessel equipped for SPM operations? (OCIMF SPM 6.4) 18 Fairleads and rollers free? 19 Towing strong points and fittings onboard? (IMO MSC Res 35(63), SOLAS II-1 3.4 v/s >20000 dwt) 20 Mooring decks painted with non-slip coatings? | Yes At building yard No Yes Yes Yes Yes Yes N/A N/A All rope No N/A N/A N/A N/A N/A Yes N/A Yes |

SECTION SEVEN  (Continued)

|  | REMARKS |
| --- | --- |
| 7.03 External Watertight Doors 01 Seals in good condition? 02 Dogs in place and free? 03 Closure satisfactory? 04 Condition? (ISGOTT 6.1.2) 05 Doors clearly marked for spaces served? (Recommended) | Yes Yes Yes Good Yes |
| 7.04 Main Deck Openings W/T Integrity 01 Condition of seals/closures on manholes? 02 Condition of seals/closures on access hatches? | Apparently good Appear good |
| 7.05 Pilot Ladders 01 Number? 02 Condition? 03 Properly constructed? (IMO res 667 (16)) 04 Manropes? (SOLAS IV 17) 05 Pilot ladders free of tripping ropes? 06 Overside lighting adequate for safe access? | 2 Good Yes Yes Yes, stowed on reel Yes |
| 7. 06 Gangways and Accommodation Ladders 01 Accommodation ladders facing direction? (IMO Res. A667(16) 3.1) 02 Lifebuoy available with light and line? 03 Is safe access provided? (2 means recommended) 04 Number and condition of gangways and accommodation ladders? 05 Net in good condition and properly rigged? 06 No Visitors/No Smoking notice displayed? (Tankers – ISGOTT 4.7.1, others – recommended) 07 Visitor muster info displayed? (Recommended – giving instructions and alarm signals) | Forward Yes Yes 2 Pilot combination ladders facing aft 2 accommodation ladders in good order Yes Yes No |
| 7.07 Condition of Deck 01 Visual condition of deck area? 02 Apparent condition of steam/hydraulic lines? 03 Decks free of oil/oily material (pollution risk)? 04 Deck housekeeping satisfactory (incl. accommodation decks)? 05 Is safe access provided? 06 Are walkways clear? 07 Are trunks and access hatches unobstructed? 08 Railings around decks/crane platforms in good condition? 09 Platforms and walkways in good condition? (Inc. at winches and windlass) | Good Good Yes Yes Yes Yes Yes Yes Some wasting of pipe cross-overs observed |

SECTION SEVEN  (Continued)

|  | REMARKS |
| --- | --- |
| 7.08 Flame Screens 01 Fitted to ballast tank vents? 02 Fitted to fuel tank vents 03 Condition? 04 Mesh size correct (30 x 30)? (CFR 46 30.10) | Yes Yes Satisfactory Yes |
| 7.09 Sounding Pipes and Vents 01 Condition? 02 Sounding pipes capped? 03 Are air vents in good condition? 04 Savealls in satisfactory condition and fitted with proper mechanical plugs? 05 Saveall capacity marked in BBLS or M3? (Recommended) | Good Yes Many upper wing tank float seals are adrift Yes No |
| 7.10 Paint Lockers & Flammable Liquid Lockers 01 Is fire extinguishing arrangement provided? 02 Type of medium used? (SOLAS II-2 18.7) 03 Instructions posted and valves labelled? 04 Light fittings secure? | Yes Water No Yes |
| 7.11 Safety Clothing 01 Adequate stocks onboard? 02 In use? 03 Condition? | Yes Yes Satisfactory |
| 7.12 Stores Cranes Etc. 01 Cranes well maintained and in good condition? 02 Condition of trips? 03 Note date last tested? (ISM 10.2.1) 04 SWL clearly marked? 05 Hook/block painted highly visible colour? 06 Operators qualified? (ISM 6.3 – 6.5) | Davits and hoists Yes Good 1994 when new. Yes Yes No |
| 7.13 Oxy/Acetylene Bottles 01 Oxygen/acetylene stowage separate and outside ER? (Tankers – OCIMF Check List Sect 4, others – recommended). 02 Is fixed piping installed from gas bottles to welding position? (Recommended) 03 Notice posted “Bottles v/vs to be closed after use”? | Yes Yes No |

SECTION SEVEN  (Continued)

|  | REMARKS |
| --- | --- |
| 7.14 Duct Keel Spaces 01 Bilge alarm fitted? 02 Are alarms operational? 03 Frequency of testing? (ISGOTT 6.4, ISM 10.2.1) 04 Condition of space? 05 Ventilation fans operational? 06 Restricted access signs posted at hold/void space/ duct keel hatches? | Yes Yes No |
| 7.15 Other Comments 01 Draft, loadline, bow thruster and bulbous bow marks clearly and properly marked (Loadline 4.5.6) 02 All openings and hatchways suitably guarded? (COSWP 9.5) 03 ER sludge/bilge standard discharge connection and fittings available? (MARPOL Ann 1 Reg. 19) 04 Approved safety torches (flashlights) only in use? 05 Deck area free of unauthorised electrical equipment? (ISGOTT 2.4.4, TSG 3.5.2) 06 Deck lighting adequate? (33 CFR 155.790) | Yes Yes Yes N/A Yes Yes |

SECTION NINE

ENGINE ROOM

|  | REMARKS |
| --- | --- |
| 9.01 Engine Control Room 01 Bridge control operational? 02 UMS operation with check lists? (ISM 7) 03 Deadman alarm fitted and operational? (If UMS – alarm or log book on bridge) 04 Chief Engineer’s Standing Orders available? 05 Log book entries satisfactory? (ISM 10.2.4) 06 Ammeter readings for steering motors logged after tests? 07 Records of generator load tests available? 08 (ISM 10.2.4) USCG pollution warning notice posted? (CFR 33 154.450) 09 Records of testing resistance of portable tank cleaning hoses available? (Max 6 ohm/metre) (ISGOTT 9.1.4) (ISM 10.2.4) Note Date: (FSI 2.10) (ISM 10.2.1) 10 Last test of emergency generator? 11 Last test of emergency fire pump? 12 Last test of survival craft engines? 13 Last test of remote shut-offs? 14 Last test of emergency lighting? 15 Last test of emergency steering gear? | No N/A Yes Yes Yes No No Yes N/A Yes 10.11.99 10.11.99 11.11.99 10.11.99 10.11.99 10.11.99 |
| 9.02 Oil Transfer Procedures (Bunkering) 01 Permanently posted (33 CFR 155.740)? 02 Contents adequate (33 CFR 155.750)? 03 Pipeline diagram posted? 04 MSDS for fuels handled? (33 CFR 154.310) | Yes Yes Yes No |
| 9.03 IG Plant (If fitted) 01 Is equipment operational? 02 Fixed 02 equipment operational 03 Calibration demonstrated? | N/A |

SECTION NINE  (Continued)

|  | REMARKS |
| --- | --- |
| 9.04 Steering Flat 01 Condition of steering gear and compartment? 02 Communications systems operational 03 Door(s) to ER closed? (SOLAS II-2 47.2) 04 Gyro repeater fitted/aligned? (SOLAS V 12(f) 05 Hand rails, gratings (or non slip surface)? (SOLAS II-1 29.13 & 19.1) (Gratings recommended) 06 Header tank full? (SOLAS II-1 29.12.3) after tests? 07 Gauge glass valves self closing and closed? 08 Emergency steering tested and satisfactory? (ISM 10.2.1) 09 Copy of block diagram posted? (SOLAS V 19-2(c)i) | Satisfactory Yes No, lashed open Yes Handrails and gratings. Port half full, starboard full Yes Yes Yes |
| 9.05 Emergency Fire Pump 01 Location? 02 Prime mover? 03 If diesel powered, is fuel tank full? 04 Instructions posted? (OCIMF check list) 05 Is pump operational? 06 Pump tested and satisfactory? (ISM 10.2.1) | Steering gear Electric motor N/A Yes Yes Yes |
| 9.06 Workshops and ER Stores 01 Machinery guarded? (COSWP 12.4.18) 02 Instructions posted and safety posters displayed? 03 Goggles available? (Tankers – OCIMF Check list Section 4) 04 Clean and tidy? 05 Fire detector head unobstructed? 06 Hot work instructions posted? 07 Chemical stowage location? 08 Chemical safety gear provided? | Yes Instructions posted Yes Yes Yes Yes Steering gear compartment Yes |
| 9.07 Incinerator 01 Fitted and operational? 02 Safety devices operational? 03 Instructions posted? | Yes Yes Yes |
| 9.08 Sewage Unit 01 Operational? 02 Notice stating USCG approval and type? (CFR 33 159) 03 Direct overboard valve (Bypass) sealed shut? 04 Valve clearly marked? 05 Tank marked “Sewage Holding Tank”? (where fitted) (Recommended) | Yes Yes Closed By felt tip pen only N/A |

SECTION NINE  (Continued)

|  | REMARKS |
| --- | --- |
| 9.09 Flame Screens 01 Spare mesh onboard? (30 x 30 mesh) | No |
| 9.10 Main Fire Pump 01 Operational status of pumps? 02 Remote start locations? | Good Yes |
| 9.11 Emergency Generator 01 Generator tested and satisfactory? (ISM 10.2.1) 02 Auto start functional? 03 Instructions posted? 04 Can fuel supply be shut off remotely? 05 Remote shut-off tested and satisfactory? (ISM 10.2.1) 06 Clearly marked? 07 Is fuel tank full? 08 Are gauge glass valves self closing and operational? (SOLAS II-2 15.6.2.2) 09 Is regular test routine in operation? (SOLAS II-1 reg 43 and Saf Man App 1.2, ISM 10.2.1) | Yes Yes Yes Yes Yes Yes Yes Yes Yes |
| 9.12 Emergency Lighting 01 Tested (if possible) and result? | Tested, satisfactory. |
| 9.13 Switchboards 01 Is suitable insulated matting provided in front of main and emergency switchboards? 02 Instructions posted for treatment of electrical shock? (COSWP 22.9.2) | Yes Yes, in accommodation. Spare to be posted in ECR |
| 9.14 Emergency Alarm Switches/Alarms 01 Alarms audible throughout engine room spaces? 02 Tested if possible? (ISM 10.2.1) 03 Staff familiar with evacuation procedures? (ISM 7) (Random check to identify awareness within ER staff of alarm sounds and escape routes etc.) | Yes Yes Yes |

SECTION NINE  (Continued)

|  | REMARKS |
| --- | --- |
| 9.15 Purifier Room 01 Are door(s) closed and not lashed in open position? 02 Are bilges clean? 03 Savealls free of oil or debris? | No, lashed open Yes Yes |
| 9.16 Emergency Bilge Suction 01 Valves clearly marked and free? | Clearly marked. |
| 9.17 Sounding Caps 01 In position with chain? 02 Deadweight closing device operational? (SOLAS II-2 Reg. 15) | Swivel fitting which cannot be secured Yes |
| 9.18 Oily Water Separator 01 Operational? 02 USCG pollution warning notice displayed? 03 Overboard valve sealed shut? 04 Valve clearly marked? 05 Alarm operational? | Yes Yes No Yes Yes |
| 9.19 Condition of Bilges 01 Oily (ISGOTT 2.14.4) 02 Rubbish present? 03 Lighting adequate? 04 Frequency of bilge alarm testing? (ISM 10.2.1) | Clean No Yes Weekly |
| 9.20 Emergency Exits/Fire Doors 01 All doors closed and not secured in open position? 02 Unobstructed? 03 Are doors free of home made hooks? 04 Are exits and routes clearly marked with luminuous IMO type signs? (EEC, IMO Res 605 (15)) 05 Warning notice posted restricting access during UMS periods? Are warning signs posted on:- 06 Noise levels? 07 Equipment starting unexpectedly? (Recommended on all vessels) 08 Is escape route lighting adequate? | Yes except to S.G. Yes Yes Yes Yes Yes No Yes |

SECTION NINE  (Continued)

|  | REMARKS |
| --- | --- |
| 9.21 Engine Room – General 01 Pipework apparently free of soft patches/cement? (If “No” state position and condition) 02 Pipe lagging in good condition and not oil impregnated? 03 Decks clean and oil free? 04 Machinery free of oil leaks? 05 ER free of temporary leak collectors? 06 Safe access to all areas? after tests? 07 Condition of fuel tank quick closing mechanisms? 08 Fuel tank surfaces in ER with sign “No Hot Wor Work”? 09 Apparent condition of seawater pipework and pumps? 10 Condition and effectiveness of ER lighting? 11 Equipment/machinery adequately guarded? 12 Lifting equipment in good condition and clearly marked with SWL? (Including lifting beams) (COSWP 17.2.41) 13 Are fuel oil delivery lines and adjacent hot surfaces jacketed? (SOLAS II-2 15.2.9-12) (Required on new vessels from 1.7.98 and existing vessels from 1.7.03) 14 Visual condition of ER spaces? | Yes Yes Yes Yes Yes Yes Apparently satisfactory, but L.O. wired open No Good Very good in parts, barely adequate in others Yes Yes Yes Satisfactory |
| 9.22 ER Fire Fighting Equipment 01 Is equipment in place and unobstructed? General condition of equipment: 02 Extinguishers? 03 Semi-portable extinguishers? 04 Fire hoses and hydrants? 05 CABA/Fireman’s Outfit (if applicable?) 06 Sand boxes? | Yes Satisfactory Satisfactory Evidence of leaking hydrant valves Satisfactory Complete with shovel |
| 9.23 Safety Clothing 01 Is clothing and equipment available? 02 Is clothing and equipment in use? 03 Are ear defenders being worn? (SOLAS II-1 36) 04 Are safety helmets being worn? (as appropriate) | Yes, boiler suits and safety shoes Yes Yes Yes |
| 9.24 Other Comments |  |

SECTION TEN

NON TANKER CARGO HANDLING AND RELATED EQUIPMENT & PROCEDURES

|  | REMARKS |
| --- | --- |
| 10.01 Dry Bulkers 01 Hatch covers – condition/W.T. integrity? 02 Hatch covers – fully secured at sea? 03 Hold access – ladders safe, hatches W.T.? 04 Hold ventilators – condition/use? 05 Trim, stability and stress properly calculated? 06 Ballasting/deballasting conducted safely? 07 Hold bilge pumping arrangements adequate? 08 Regular check on soundings – cargo/ballast paces? Spaces? 09 Cargo lashings (if applicable) checked? 10 Fumigation procedures (if applicable) followed? 11 Smoking regulations/signage? | Appear good Apparently Appear satisfactory Satisfactory condition, use not recorded Yes Ballasting yes Yes Logged daily N/A N/A No smoking notices posted. |
| 10.02 Pure Car Carriers/Ro Ro’s 01 Vehicle ramps – condition/W.T. integrity? 02 Vehicle decks/holds ventilation - condition? 03 Vehicle stowage/lashings – condition & adequacy? 04 Personnel access to loaded vehicle decks? 05 Trim, stability and stress properly calculated? 06 Ship’s side/bow/stern W.T. doors – procedures followed? 07 Vehicle deck and W.T. door alarms operational? 08 Smoking regulations/signage? | N/A |
| 10.03 Miscellaneous Vessels 01 Container lashings and stowage. 02 Reefer plants – general safety. 03 Deck cargo – general securing arrangements. 04 Deck cargo – general personnel access. 05 Deck cargo – bridge visibility. 06 Deck cargo – pipes, valves etc. protection/access | N/A |

SECTION ELEVEN

DEFICIENCY LIST

The following list of deficiencies was discussed with the Master.

|  | REPORT SECTION REF | REG/MANUAL REF |
| --- | --- | --- |
| 1 Lifebuoy lanyards must be 4 metres in length 2 Instructions for isolating loops to be posted 3 Two types of battery in locker on bridge 4 Emergency mustering instructions for shore personnel to be posted 5 Floor tiles to be secured in Galley 6 Galley medical chest to be re-stocked 7 Company SEP to be displayed 8 Statutory Certificates to be displayed 9 Lifeboat remote release must be all wire (Non flammable) 10 Fire hose box door catches to be made operational 11 Location of Int. shore connection to be marked at gangways 12 Sledehammer required for anchor cable bitter end 13 UW ballast tank vent float seals are adrift in 8 places 14 Paint locker sprinkler valve to be identified 15 Oxygen and acetylene rooms: notice required BOTTLE VALVES TO BE CLOSED AFTER USE 16 Oxy acetylene equipment in workshop. A flash back arrestor must be fitted to the oxygen manifold A blow back valve must be fitted to the oxygen hose connection to the torch. 17 Duct Keel. Restricted access signs to be posted at deck access. VENTILATE BEFORE ENTRY. NO ENTRY WITHOUT PERMIT FROM MASTER 18 Post MSDS for Fuel Oils 19 Port side header tank for steering gear to be topped up 20 Sewage system not being operated in port of Ghent 21 Post Electric shock treatment poster in engine control room 22 Purifier room door secured open 23 Bilge overboard valve not locked shut 24 Post notice on ER entrance doors WARNING: EQUIPMENT MAY START UNEXPECTEDLY 25 Lub.Oil tanks: quick closing valves are wired open 26 Place signs on all ER Oil Tanks NO HOT WORK | 2.16.3 2.18.04 3.10.06 4.01.03 4.09.01 4.09.04 4.18.02 4 18.03 5.01.06 6.07.05 6.12.02 7.01.05 7.09.03 7.10.03 7.13.03 7.14.06 9.02.04 9.04.06 9.08.01 9.13.02 9.15.01 9.18.03 9.20.07 9.21.07 9.21.08 | COSWPMS ISM 2.1, 2.2 SOLAS 1 Reg 16 COSWPMS 33CFR 154. 310 COSWP 22.9.2 |

Inspector Signature________________________________  Master Signature______________________________

Date___________________________

SECTION TWELVE

RECOMMENDATIONS

1 Provide Breathalyser tubes showing expiry date. Reference 1.08.02

2  The 48 month maintenance instructions for the opening and inspection of lifeboat davit winch brakes,

Component 0269, are incomplete and hazardous and should be modified.

They instruct personnel to lower the boat to the embarkation deck,  open the brake and replace any parts as

necessary.

No mention is made of hanging off pennants, (Ref. 5.06.09) nor is there provision for fitting..

Reference 5.11.

It appears that the five yearly load test of brakes required by SOLAS 111 20.11.1 was not carried out at the

recent dry docking.

3  Provide a spare Triplex Filter cartridge for the Bauer Medical Air compressor.

Reference 6.05.05

SECTION THIRTEEN

INSTRUCTION & TRAINING CONDUCTED

With a very busy schedule of cargo operations, bunkering, change of Class, an Internal Audit by a visiting

Superintendent and Surveys by Class, Flag State and P & I Club no time was available for formal training.

One short session was held with all Filipino staff at which we were able to establish that WSM Emergency

procedures were being followed.

To tie in with the lifeboat launching exercise we discussed cold water rescue of a manoverboard victim and

treatment of hyperthermia.

Many useful discussions were held with different personnel concerning maintenance of safety equipment and

WSM procedures

ADDENDUM

CARGO LOSS PREVENTION

Hatch seals and compression bars were all seen to be in good order.

Access trunk seals and channel ways were in good order, securing dogs were all operational.

Grain spout openings were sealed,  the shafts below showed rust streaks, but none were serious and could be

attributed to condensation.

Ventilators were closed tight.

No sign of moisture was noted on cargo surfaces and no recent tell tale streaks of rust were sighted on hatch

coamings or hopper sides.

Hatch lid drain channels and coaming drains appeared to be clear.

Coamings had been swept clean before final closing at the load port. No sign of debris was seen compressed.

Seating wedges showed signs of wear, however good compression was obtained on the cross hatch joint by

securing the cross hatch dogs before lowering the wheels.

Ventilation was reportedly closed throughout. No log entries were noted.

Temperature probe points in the deck appeared to seal well and were clearly identified.

Gas sampling points in the coamings were apparently tight and marked as to their purpose.