| Name of Vessel | Call Sign | IMO Number | Date |
| --- | --- | --- | --- |
| "DUTCH SPEAR" | PIBR | 9056038 | 09.07.2003 |
| Flag | Port of Registry | Classification | Classification Number |
| DUTCH | ROTTERDAM | GERMANISCHER LLOYD | 034401-3 |
| Owner | Manager / Operator |
| DUTCH HARBOUR SPEAR B.V. Rotterdam | REDERIJ WESSELS B.V. Rotterdam CHARTERERS;NAVESCO BOGOTA/COLUMBIA |
| Type of Vessel | Year, Number of Built | Yard of Built |
| MULTIPURPUSE VSL | 1993 | SLOVENSKE LODENICE AS (KOMARNO) |
| Length o.a. | Length b.p. | Beam | max. Draft |
| 87,90 m | 81.85 m | 12.80 m | 5.52 m |
| Freeboard | Masthead Height a. WL | Gross Tonnage | Net Tonnage |
| 1.595 m | 15 m | 2514 BRZ | 1351 NRZ |
| Deadweight | Light Ship | Displacement | Holds | Crew |
| 3610 mt | 1359 mt | ~ 4930mt | 1 | 7 |
| Container | Character of Class |
| Below Deck | On Deck | Reefer | Hull | Machinery |
| 108 TEU 48 FEU | 60 TEU 24 FEU | 6 TEU |  100 A 5 E | MC E AUT |
| Main Engines | Aux. Generator Diesels |
| Number, Output | Type | Number, Output | Type |
| 1 1470 kW | MAN ; B&W 6 L 28/32 A | 2 210 kW | MAN D 2866 LE |
| Propeller | Shaft Generator |
| Number, Type | Diameter | Number, Output | Type |
| 1 MAN VB 640 |  | 1 400 kVa | LEROY SOMER (france) |
| Bow Thruster | Speed |
| Number, Output | Type | Service | Maximum |
| 1 185 kW | JASTRAM BU -40 F | 10.5kn | 11.5kn |
| Nautical Equipment |

Miscellaneous e.g. Grain Capacity cbm, Reefer Capacity cbf, Dangerous Goods, Elevators, Shell Doors, Cargo Gear, Cranes, Selfunloader, Fork Lifts,