To  the  Master  of  the  m/v “ Forest  “

Mr.  Yury  Pupkin .

From  Chief  Officer  V. Vaskin

R   E   P   O   R   T.

This  is  to  remind  You  that  condition  of  hatch  covers  and   coamings  is  :

1.  Hatch  covers  and   comings  are  completely  rusted.  There  are  plenty  of

visible  and  invisible  holes  and  cracks  at  all  the  perimeters  of  the  holds

and  at  the  junctions  of  the  hatches .

2.  Rubber  is  old  and  worn  out  .

3.  All  cleat  locks  are  badly  corrode.  Tension  cannot  be  adjusted  due  to

corrosion  of  cleat  bolt  threads.  Elastic  and  steel  washers  are  mostly

worn  out  .

4.  From  existing  cheating  Assy  98  pcs.  at  the  hold  No. 1  missing  30 pcs.

At  the  hold No. 2  missing  46  pcs ,  at  the  hold  No. 3  missing  22  pcs,

at  the  hold  No. 4  from  240  pcs  missing 27  pcs,  at  the  hold  No. 5

from  98  pcs  missing  37  pcs ,  at  the  hold  No.  6  missing  28pcs.

It  was  impossible  to  replace  the  rubber  in  ship’s  condition  by  the  crew.

We  have  no  any  spare  cleat  on  board .  It  was  necessary  to  stop  all

other  repairing  operations  minimum  for  two  weeks  to  recover  cleat  holders.

We  couldn’t  to  do  that  because  of  wreckage  condition  deck  equipment.

In  view  of  forthcoming  loading  and  fumigating , I  consider  that  it’s

my  duty  as  a  safety  officer  to  inform  You  .  We  can  make  our  holds

watertight  by  using  the  silicon  and  waterproof  band  but  not  gasproof.

Furthermore  the  hold’s  bulkhead  between  cargo  hold  No. 6  and

engine  room  badly  corroded  also. Perhaps  there  are  some  microcracks

in  it.  If  it  is  so  gas  will  penetrate  directly  into  the  engine  room.

Proceeding  from  the  above  said  I  consider  that  it’s  impossible  to  avoid

penetration  of  fumigating  gas  into  engine  room  as  well  as  on  deck  and

further  into  living  accommodations .

In  case  forthcoming  fumigating  is  insalubrity’s  for  the  crew  I  ask  You

to  inform  the  Company  concerning  our  situation  for  avoiding  possible

accidents  .

Yours   faithfully  ,

Chief  Officer  of  the  m/v “ Forest  Sovereign”

V. Vaskin

30  January  1998